## Slide 1: WF on gNB positioning measurement requirements
Ericsson
3GPP TSG-RAN WG4 Meeting # 98-e
Electronic Meeting, Jan 25-Feb 05, 2021
Agenda: 7.7.2.3
R4-2103587

## Slide 2: General: Side conditions for gNB measurement accuracy
Accuracy requirements for gNB measurements shall be defined for the following Ês/Iot values:
  Ês/Iot1 [dB] (High Ês/Iot) = 3 dB for FR1 and FR2
  Ês/Iot2 [dB] (Low Ês/Iot) = -13 dB for FR1 and FR2.
The gNB, which declares the support of positioning measurements, needs to declare the support of measurements for at least either high Ês/Iot or low Ês/Iot side conditions.

## Slide 3: General: Beam sweeping during gNB measurement
gNB accuracy requirements do not mandate gNB RX beam sweeping
Options for capturing above agreements:
  Option 1:
    gNB accuracy requirements do not mandate gNB RX beam sweeping is captured only in the WF.
  Option 2:
    gNB accuracy requirements do not mandate gNB RX beam sweeping is included in the accuracy side conditions.
  Other options not precluded

## Slide 4: General: SRS parameters for gNB measurement accuracy
gNB accuracy requirements shall be defined for group of SRS BWs
  grouping of SRS BWs will be decided based on link simulation results
FFS: whether gNB measurement accuracy is agnostic to or depends on comb and symbols size
  Decision will be based on link simulation results
FFS: whether gNB accuracy requirements are also be based on grouping of SRS parameters other than SRS BW (e.g. SCS).
  grouping of other parameters (e.g. SCS) will be decided based on link simulation results
Link simulations are based on assumptions in R4-2012142 and agreements in this meeting (e.g. on propagation channel).

## Slide 5: General: Samples for gNB accuracy requirements
FFS: number of samples/snapshots used for deriving gNB accuracy requirements.
Option 1:
  Define the gNB accuracy requirements based on single shot measurement assumption
Option 2:
  Define the gNB accuracy requirements based on multiple shots (Ns)
    Ns is FFS
Other options not precluded

## Slide 6: SRS-RSRP: Factors impacting SRS-RSRP accuracy for different gNB types
Baseline SRS-RSRP measurement accuracy without margin is based on link simulation results
RF calibration error for SRS-RSRP measurement for gNB type 1-C (X) is smaller than that for gNB types 1-O/2-O (Y) i.e. Y>X.
Implementation and RF margins are specific to SRS-RSRP. Values are FFS.

## Slide 7: gNB Rx-Tx: Factors impacting gNB Rx-Tx accuracy for different gNB types
Baseline timing measurement accuracy without margin is based on link simulation results
RF calibration error for timing measurements depends on gNB type (1-C, 1-H, 1-O, 2-O).
Implementation and RF margins are are FFS:
  Candidate options:
      Option 1:
        2 times calibration error
      Option 2:
        group delay calibration margin = 8 Tc
      Option 3:
        Depends on frequency range, SRS configuration and implementation (e.g. antenna)
      Other options not precluded

## Slide 8: gNB Rx-Tx: Applicable propagation channel for gNB Rx-Tx accuracy
gNB Rx-Tx measurement accuracy requirements apply in AWGN.

## Slide 9: UL RTOA measurement accuracy requirements
FFS: whether gNB Rx-Tx time difference accuracy can be reused for UL-RTOA accuracy
FFS: how to define reference time in the ideal UL-RTOA
Agreements in GTW:
  Further identify how to derive reference time in the ideal UL-RTOA (e.g. whether it is determined by gNB’s own timing based on LMF configuration).
    If no consensus reached in the 2nd round, then further send LS to RAN1 and RAN3 to clarify the procedure.
Candidate options to define the reference time in the ideal UL-RTOA:
  Option 1: it is based on gNB’s interpretation of the SFN initialisation Time, and thus determined by gNB local timing.
  Option 2: it is based on an external interpretation of the SFN initialisation Time
  Other options are not precluded.