## Slide 1: WF on test case for DL interruption due to Tx switching between two uplink carriers
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, 25 Jan -05 Feb, 2021
      R4-2103599
Document for: Approval

## Slide 2: Agreements
Indicate the EUTRAN cell is FDD in test case A.4.5.8
Verify the case that no interruption is allowed if UE does not report uplinkTxSwitching-DL-Interruption-r16.
  -To test the case where no interruption is allowed, aperiodic CSI-RS for L1-RSRP reporting is triggered on symbol#12 FDD carrier (@SCS15KHz):
  -To test the case where no interruption is allowed, aperiodic CSI-RS for L1-RSRP reporting is triggered on symbol #10 for S=’11DL:1GP:2UL’ on TDD carrier