## Slide 1: WF on R16 NR RRM enhancements - BWP switching on multiple CCs, UL spatial info switch
Intel Corporation, Apple
3GPP TSG-RAN WG4 Meeting #98-e R4-2103619
Electronic Meeting, 25, Jan-05, Feb. , 2021

## Slide 2: BWP switching on multiple CCs in core part
Issue 1-1-1: Scenario for RRC based BWP switch on multiple CCs
  Wait for the feedback from RAN2.
    Issue 1-1-2: Clarification for N for DCI-based simultaneous BWP switch on multiple CCs
  A clarification is added to the description of N:
    The number of CCs, N, on which the UE can simultaneously switch BWPs, while still meeting the requirements, if any, related to allocations on downlink, uplink, or transmission of HARQ-ACK, depend on the UE reported capabilities related to BWP switching, the network configuration and the BWP switch method.

## Slide 3: BWP switching on multiple CCs in performance part(1)
Issue 3-1-1: Whether to define DCI/Timer based FR1+FR2 simultaneous BWP switch test case
Do not define DCI/Timer based FR1+FR2 simultaneous BWP switch test case
Issue 3-1-2: Whether to define DCI/Timer based non-simultaneous BWP switch test case
Not to define DCI/Timer based non-simultaneous BWP switch test case.

## Slide 4: BWP switching on multiple CCs in performance part(2)
Issue 3-1-3: whether to define RRC based BWP switch on multiple CCs test case
To be discussed after receiving RAN2 response
Issue 3-1-4: TC4: DCI-based and Timer-based simultaneous Active BWP Switch on multiple CCs on FR2 in SA
Cell configuration: NR FR2 PCell + NR FR2 SCell + NR FR2 SCell

## Slide 5: UL Spatial Relation Info Switch in core part(1)
Background
  PUCCH Spatial Relation Info IE also has Pathloss Reference RS
  Spatial relation info switch for PUCCH may also change Pathloss Reference RS
  Existing known condition is based on associated DL-RS
  Existing delay requirements for spatial relation info switch for PUCCH do not consider change to PL-RS

## Slide 6: UL Spatial Relation Info Switch in core part(2)
Known condition definition update to include PL-RS
  Do not update known condition

## Slide 7: UL Spatial Relation Info Switch in core part(3)
Delay requirements for MAC–CE based UL spatial relation switch for PUCCH
  Option 1: Refer to section 8.14 for additional delay due to PL-RS switch in UL spatial relation switch
    Option 1a: Refer to section 8.14 for additional delay due to PL-RS switch in UL spatial relation switch for known PL-RS
  Option 2: Longer delay is expected when PL-RS and DL-RS in the UL spatial relation are changed simultaneously