## Slide 1: WF on performance requirements of CSI-RS based L3 measurement
CATT/OPPO
3GPP TSG-RAN WG4 Meeting #98e R4-2103630 Electronic Meeting, 25 Jan. – 5 Feb., 2021

## Slide 2: CSI-RSRP and CSI-RSRQ measurement accuracy requirements
Background:
Agreements in RAN4#97e
  Specify the following L3 CSI-RSRP measurement accuracy requirements
    Case 1: the timing offset between the reference measurement timing and the target CSI-RS in one layer is smaller or equal to [CP]
      FFS: Reuse the accuracy requirements of SS-RSRP
      FFS on whether gNB needs to know that the timing offset is smaller or equal to CP and how to provide such information if needed
    FFS: Case 2: the timing offset between the reference measurement timing and the target CSI-RS in one layer is larger than [CP]
    Reference measurement timing for one layer is the
      Intra-frequency case: Serving cell timing
      Inter-frequency case: Up to UE implementation and shall be based on the timing of one of the target cells
        Note: UE may use a single or multiple reference measurement timings for different measurements on different symbols

## Slide 3: CSI-RSRP and CSI-RSRQ measurement accuracy requirements
Issue 2-1-1: The upper bound of timing offset for case 1
  For CSI-RSRP and CSI-RSRQ the upper bound of timing offset for case 1 is TBD
    Option 1: 1 CP
    Option 2: 0.9 CP
  Companies are encouraged to bring additional simulation results for different values of timing offset and evaluate both positive and negative timing offsets.
  Note: the timing offset value in the test cases can be specified in []

## Slide 4: CSI-RSRP and CSI-RSRQ measurement accuracy requirements
Issue 2-1-2: The CSI-RSRP and CSI-RSRQ measurement accuracy requirements for case 1
  Reuse the accuracy requirements of SS-RSRP and SS-RSRQ measurement.

## Slide 5: CSI-RS based measurement accuracy requirements
Issue 2-1-3: Whether to define CSI-RS measurement accuracy requirements for case 2
  Do not define CSI-RS measurement accuracy requirements for case 2

## Slide 6: CSI-RS based measurement accuracy requirements
Issue 2-1-6: Whether gNB need to know the timing offset
  gNB does not need to know the exact timing offset.
  No feedback signaling is needed.

## Slide 7: CSI-RS based measurement accuracy requirements
Issue 2-1-8: UE behaviour when the timing offset is beyond the threshold defined above
  UE is not required to meet the requirements if the timing difference exceeds [CP].

## Slide 8: CSI-SINR accuracy requirements
Issue 2-3-1: The upper limit of Es/Iot for CSI-SINR measurement with timing offset(T△)
    Option 1: Es/Iot ≤ [10] dB for the case that timing offset is within CP.
    Option 2: Es/Iot ≤ [18] dB for the case that timing offset is within CP/2.

## Slide 9: CSI-SINR accuracy requirements
Issue 2-3-2: The CSI-SINR measurement accuracy requirements under the condition in issue 2-3-1
  Reuse the accuracy requirements of SS-SINR measurement.

## Slide 10: Test cases for CSI-RS based L3 measurement
Sub-topic 1-1: Whether to introduce test case for FDD mode
  Option 1: No (Qualcomm, OPPO, vivo, MTK, Xiaomi, CATT)
  Option 2: Yes (Huawei, CATT, Nokia, Apple, CMCC)
    If option 2 was agreed, FFS time offset for FDD mode (e.g., CP, 3ms or others)

## Slide 11: Test cases for CSI-RS based L3 measurement
    Sub-topic 1-2: DRX configuration for Test Cases with DRX
DRX configuration for test cases:
  320ms (DRX.5 in A.3.3) for FR1
  40ms (DRX.1 in A.3.3) for FR2

## Slide 12: Test cases for CSI-RS based L3 measurement
Sub-topic 1-3: Time offset configuration
  the timing offset between cells in test cases is [TBD].