## Slide 1: WF on FR2 new FWA UE RRM performance requirements
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #98-e
Online, 25th Jan – 5th Feb, 2021
Agenda: 9.24.3
R4-2103664

## Slide 2
Issue 1-1: Band grouping of bands n257 and n258 for UE power class 5:
    Bands n257 and n258 for UE power class 5 can be defined as the group K
Agreements on RRM Perf requirements in NR

## Slide 3
Issue 1-2: Minimum SSB_RP values of bands n257 and n258 for UE power class 5:
    The minimum SSB_RP values for UE power class 5 can be defined based on Table 2
Agreements on RRM Perf requirements in NR
Table 2: Minimum SSB_RP values for UE power class 5
Case | Direction | Bands for PC5 | Refsens Diff with PC3 (dB) | YPC3 /ZPC3 (dB) | Minimum SSB_RP (dBm/120kHz)
Intra-freq | Rx Beam Peak | n257 | -6.9 | 7 | -123.4+YPC5
 |  | n258 | -7.1 | 7 | -123.6+YPC5
 | Spherical coverage | n257 | -11.5 | 7 | -115.4+ZPC5
 |  | n258 | -11.7 | 7 | -115.6+ZPC5
Inter-freq | Rx Beam Peak | n257 | -6.9 | 7 | -121.4+YPC5
 |  | n258 | -7.1 | 7 | -121.6+YPC5
 | Spherical coverage | n257 | -11.5 | 7 | -113.4+ZPC5
 |  | n258 | -11.7 | 7 | -113.6+ZPC5