## Slide 1: WF on further RRM enhancement for NR and MR-DC - PUCCH SCell activation/deactivation requirements
CATT
3GPP TSG-RAN WG4 Meeting #98e R4-2103675 Electronic Meeting, 25 Jan. – 5 Feb., 2021

## Slide 2: Sub-topic 1-1 General(1/5)
Issue 1-1-1: The working scope of R17 PUCCH Scell
  RAN4 defines PUCCH SCell activation/deactivation requirements based on the “legacy R15 SCell activation mechanism” rather than “R16 direct SCell activation from DC/CA enhancement WI”.

## Slide 3: Sub-topic 1-1 General(2/5)
Issue 1-1-0: Whether CSI report of PUCCH SCell is transmitted on PCell or PUCCH SCell to be activated
  Further study the procedures for the following 2 scenarios
    CSI report of PUCCH SCell is transmitted on PUCCH PCell
    CSI report of PUCCH SCell is transmitted on PUCCH SCell to be activated
    FFS whether to define requirements for both cases.

## Slide 4: Sub-topic 1-1 General(3/5)
Issue 1-1-4: Whether the beam information is needed for NW to initiate the RA for TA updating by a PDCCH order
  The beam information (SSB index) is needed for NW to initiate the PDCCH order to trigger RA

## Slide 5: Sub-topic 1-1 General(4/5)
Issue 1-1-5: Whether the beam information of the PUCCH SCell being activated is needed to be indicated to NW
  Option 1: (Huawei, MTK, Nokia, Xiaomi, OPPO)
    The beam information of the PUCCH SCell being activated is needed to be indicated to NW
  Option 2: (Ericsson, Qualcomm, Apple, CATT, NTT DOCOMO)
    Depends on what activation sequence we are assuming.
  Option 3: (Apple, Qualcomm, NEC)
    Need to differentiate unknown and known cases.
  Option 4: (NEC)
    Agree on whether L1-RSRP is transmitted on spCell or SCell first.
  Option 5: (Ericsson, Nokia, vivo, NEC)
    Need further discussion

## Slide 6: Sub-topic 1-1 General(5/5)
Issue 1-1-6: Whether the UL spatial relation should be considered for PUCCH SCell activation
  Option 1: (Huawei, Ericsson, Qualcomm, NTT DOCOMO, MTK, Apple, Xiaomi, OPPO, Apple, NEC, vivo)
    Yes
  Option 2: (Nokia)
    No
  Option 3: (CATT)
    Need further discussion

## Slide 7: Sub-topic 1-2 PUCCH SCell activation requirements(1/6)
Issue 1-2-1: The condition that TA of target PUCCH SCell is valid
  A TA is considered to be valid provided that the TimeAlignmentTimer associated with the TAG containing the PUCCH SCell is running.

## Slide 8: Sub-topic 1-2 PUCCH SCell activation requirements(2/6)
Issue 1-2-2: The PUCCH SCell activation delay when TA of target PUCCH SCell is valid
  Option 1: (Apple, CATT, Xiaomi, CMCC, NTT DOCOMO, vivo, Nokia, OPPO, Qualcomm, Ericsson, MTK)
    Same as the normal SCell activation delay in TS38.133 section 8.3.2 which is (( THARQ + Tactivation_time +TCSI_Reporting)/ NR slot length).
  Option 2: (Huawei, NEC, Ericsson, CATT)
    Related to issue 1-1-6, can be FFS

## Slide 9: Sub-topic 1-2 PUCCH SCell activation requirements(3/6)
Issue 1-2-3: Compared to valid case, whether the NR PUCCH SCell activation delay requirements should be relaxed for invalid TA case
  Compared to valid TA case, additional delay is needed for the NR PUCCH SCell activation delay requirements with invalid TA.

## Slide 10: Sub-topic 1-2 PUCCH SCell activation requirements(4/6)
Issue 1-2-4: The additional delay parts for NR PUCCH SCell activation with invalid TA
  Option 1: (Apple, Xiaomi, CMCC, NTT DOCOMO, NEC, Qualcomm, vivo, OPPO, MTK)
    The following three additional delay parts (T1/T2/T3) in LTE PUCCH SCell activation with invalid TA could be reused for NR PUCCH SCell activation with invalid TA.
      the delay uncertainty in acquiring the first available PRACH occasion in the PUCCH SCell
      the delay for obtaining a valid TA command for the sTAG
      the delay for applying the received TA for upling transmission
    The values for T1/T2/T3 might be revisited for NR PUCCH SCell activation.
  Option 2: (Nokia)
    The UE shall be capable to perform downlink actions related to the SCell activation command for the SCell being activated on the PUCCH SCell no later than in slot .
    The UE shall be capable to perform uplink actions related to the SCell activation command for the SCell being activated on the PUCCH SCell no later than in slot , where TRACH is the delay to perform RACH procedure and apply the TA.
  Option 3: (CATT)
    Further discussion is needed for the completion of downlink and uplink actions.
  Option 4: (Ericsson, Huawei)
    Existing RRM requirements for activation of single downlink NR SCell to be used as baseline for completion of downlink actions. Completion of uplink actions are to be further studied.

## Slide 11: Sub-topic 1-2 PUCCH SCell activation requirements(5/6)
Issue 1-2-5, 1-2-6 and 1-2-7
  FFS:
    The delay uncertainty in acquiring the first available PRACH occasion in the PUCCH SCell (i.e. T1)
    The delay for obtaining a valid TA command for the sTAG to which the SCell configured with PUCCH belongs (i.e. T2)
    The delay for applying the received TA for uplink transmission on target PUCCH SCell being activated (i.e. T3)

## Slide 12: Sub-topic 1-2 PUCCH SCell activation requirements(6/6)
Issue 1-2-8: Applicability of PUCCH SCell activation requirements
  Option 1: (Apple, Qualcomm, vivo, CATT, NTT DOCOMO, MTK)
    The PUCCH SCell activation delay requirement shall apply provided that,
    The UE has received a PDCCH order to initiate RA procedure on the PUCCH SCell within Tactivate_basic otherwise additional delay to activate the SCell is expected; and
    No interruption occurs in same FR as the target PUCCH SCell during the SCell activation procedure if UE supports per-FR MG, otherwise the PUCCH SCell activation delay can be extended, and
    No interruption occurs during the SCell activation procedure if UE does not support per-FR MG, otherwise the PUCCH SCell activation delay can be extended.
    The above interruption is caused by factor defined in TS38.133 section 8.2.1.1 for EN-DC, in TS38.133 section 8.2.2.1 for NR SA, in TS38.133 section 8.2.3.1 for NE-DC and in TS38.133 section 8.2.4.1 for NR-DC.
  Option 2: (Ericsson, Qualcomm, NEC, NTT DOCOMO)
    Need to settle the basics on which steps are taken and in which order during the activation first.

## Slide 13: Sub-topic 1-3 SCell activation delay requirement for deactivated PUCCH SCell with multiple Scells
Issue 1-3-1 and 1-3-2
  RAN4 to define requirements for PUCCH SCell activation with multiple SCell after requirements for PUCCH SCell activation with single SCell are completed.

## Slide 14: Sub-topic 1-4 PUCCH SCell deactivation requirements
Issue 1-4-1: The type of PUCCH SCell deactivation requirements
  Only MAC CE based SCell deactivation requirement is specified for PUCCH activated SCell, i.e., no timer based PUCCH SCell deactivation is assumed.

## Slide 15: Sub-topic 1-4 PUCCH SCell deactivation requirements
Issue 1-4-2: The PUCCH SCell deactivation requirements
  Reuse MAC CE based normal SCell deactivation requirement specified in section 8.3.3 of TS 38.133, which is ((THARQ + 3ms)/ NR slot length).

## Slide 16: Sub-topic 1-5 SCell deactivation delay requirement for activated PUCCH SCell with multiple SCells
Issue 1-5-1: SCell deactivation delay requirement for activated PUCCH SCell with multiple Scells
  Option 1: (CMCC, NEC, vivo, Apple, Ericsson, Qualcomm, Xiaomi, CATT, NTT DOCOMO, MTK, Nokia)
    Reuse the SCell deactivation delay requirement for activated SCell with multiple downlink SCells specified in section 8.3.8 of TS 38.133, which is (( THARQ + 3ms)/ NR slot length).
  Option 2: (Huawei, OPPO, Xiaomi)
    FFS. Focus on the single PUCCH SCell deactivation requirements first

## Slide 17: Sub-topic 1-6 Interruption caused by PUCCH SCell activation/deactivation
Issue 1-6-1: Interruption requirements for PUCCH SCell activation/deactivation
  Option 1: (Apple, OPPO, MTK, Nokia)
    Reuse the interruption requirement of normal SCell activation/deactivation.
  Option 2: (Ericsson)
    Interruption requirements for PUCCH SCell deactivation reuse the interruption requirement of normal SCell deactivation.
    Interruption requirements for PUCCH SCell activation are FFS.
  Option 3: (Qualcomm)
    Reuse the interruption requirement of normal SCell activation/deactivation for valid TA case. FFS for invalid TA case.