## Slide 1: 3GPP TSG-RAN WG4 #98-e Meeting Electronic Meeting, 25th Jan. - 5th Feb. 2021
Intel
WF on R17 NR MG enhancements – Pre-configured MG patterns and NCSG
R4-2103677

## Slide 2
Agreements in the 1st round/GTW
Agreements in the 2nd round
Still open for discussion
(For the FFS issues, the other options will not be precluded in current stage)

## Slide 3
Part 1. Pre-configured MG

## Slide 4: General procedures of pre-configured MG
Further study the following procedures for pre-configured MGs:
  1. (Re)Configuration of the pre-configured MG
    FFS if specific procedure for activation after the RRC configuration is needed
  2. Activation the pre-configured MG following a DCI or timer-based BWP switch
  3. Deactivation the pre-configured MG following a DCI or timer-based BWP switch
  Note 1: The conditions and details of each procedure are FFS
  Note 2: MG activation in this context means that both NW and UE assume that the pre-configured MG will be used for measurements.
  Note 3: MG deactivation in this context means that both NW and UE assume that the pre-configured MG will not be used for measurements and UE should be able to receive scheduled data.

## Slide 5: Configuration procedure
FFS on how pre-configured MGs can be configured:
  Option 1. Pre-configured MGs are configured per BWP
  Option 2. Pre-configured MGs are configured per UE or per FR which are same as these of legacy MGs
FFS on relation of pre-configured MG pattern and with the current RRC configured MG
  Option 1. Pre-configured MG in one active BWP can over-ride current RRC configured MG until active BWP switch to a new BWP without per-configured MG pattern
  Opiton 2. Pre-configured MG is the RRC configured MG in Rel-15, and it may be ON/OFF after BWP switch.

## Slide 6: Activation/Deactivation procedures
FFS on in which cases the pre-configured MGs shall be activated
  Option 1. Depending on both BWP switching and MOs configured
FFS on how pre-configured MGs can be activated/deactivated:
  Option 1 Autonomously/implicitly triggered by DCI/Timer based BWP switching.
  Option 1a A per-UE or per-FR MG is (de)activated following a BWP switch as follows:
    If MG is not required by any of the configured MOs, the MG is deactivated
    If MG is required by one or more of the configured MOs, the MG is activated
  Option 2 Either network centralized or UE centralized rules will work.
  Option 3 :RAN4 need to account robustness of the gap changes when evaluating and agreeing on activation/deactivation of MG pattern(s).
FFS on evaluation on MG activation/deactivation mechanism
FFS on Signaling to activate (enable) the pre-configured MGs

## Slide 7: Using scenarios
FFS on whether the pre-configured MG when BWP switching on the multiple CCs be discussed?
  Option 1. Yes. Study CA and with BWP switch on single/multiple CC cases
  Option 2. Study CA and with BWP switch on single CC cases only.
Whether pre-configured MGs are applicable in MR-DC scenario
  Deprioritize MR-DC scenario.
Whether the pre-configured gaps shall be considered as a part of multiple concurrent gap patterns framework
  Considered this in 2nd stage.

## Slide 8: RRM requirements with Pre-configured MGs
FFS on activation/deactivation delay
  Option 1: No separated activation delay for the pre-configured MG activation/deactivation
  Option 2: some transition time (T) shall be included in the pre-configured MG activation/deactivation time.
  Option 3: The delay of MG (de)activation is same as that of BWP switching.
  Option 4 :MGP change delay shall be evaluated based on realistic latencies.
No any new interruption requirements introduced by pre-configured MGs
FFS on measurement period for the measurements with the pre-configured MGs
FFS on transitions between gapless and gap-based measurement procedures during ongoing measurements
  Option 1:
    RAN4 is to investigate the maximum number of transitions (N1,max) allowed for switching from gapless measurement procedure to gap-based measurement procedure during the ongoing measurement.
    RAN4 is to investigate the maximum number of transitions (N2,max) allowed for switching from gap-based measurement procedure to gapless measurement procedure during the ongoing measurement
FFS on scheduling restriction during pre-configured MGs when not used
  Option 1: If the UE is measuring without pre-configured gaps and no other frequency layer which needs gaps is configured then the UE can be scheduled during the pre-configured gaps while meeting existing scheduling restriction requirements defined in TS 38.133

## Slide 9: Gap patterns for pre-configured MGs
FFS on Number of pre-configured MG patterns:
  Option 1: The existing gap patterns (0~23) in Rel16 can be reused for the pre-configured MG.
  Option 2: The existing gap patterns (0~25) in Rel16 can be reused for the pre-configured MG.
FFS on Per-UE/Per-FR pre-configured MG pattern applicability
  Option 1
    If the gap patterns which can be used as the pre-configured gap are reused from Rel16, the same applicability(per-UE/per-FR) shall follow the rules defined in Rel16 also.
  Option 2:
    If per UE MG is configured, the BWP of PCell is referenced to activate its MG pattern which applies to all the serving carriers including PSCell and SCells.
    If per FR MG is configured, BWPs of PCell and PSCell are referenced respectively to decide the pre-configured MGs for applying to the SCells of respective FR.
  Option 3
    The applicability of current per FR gap pattern should also apply for per BWP MG configuration

## Slide 10
Part 2. NCSG

## Slide 11: Scenarios and use cases
The use cases of NR NCSG can be similar as these of LTE
  The specific use cases can be FFS
  Whether the usage of per-CC gap can be FFS
NCSG supports both synchronous/asynchronous operation
  FFS on whether to define separate NCSG patterns for sync and async needs more discussion

## Slide 12: UE behavior within NCSG
Same as UE within LTE NCSG, that is
  During VIL1/VIL2 UE is not expected to transmit or receive any date on corresponding serving cell(s).
  During ML UE is expected to transmit and receive data on the corresponding serving cell(s).

## Slide 13: NCSG pattern
The general NCSG design principle :
  FFS on which legacy patterns in Rel16 can be reused for NCSG
    Option 1. All 26 NCSG patterns in Rel16
    Option 2 Reuse part of the legacy MG patterns in [2] as the new NCSG patterns in NR.
    Option 2a : reuse part of the legacy MG patterns with long MGL, e.g., gap pattern with ID 0,1,4,5 for FR1, or ID 12,13,14,15 for FR2.
    Option 2b : NR gap patterns #0~23 .
    Option 2c : RAN4 should consider defining a limited number of suitable NCSG patterns and assign a UE capability to some of them, while the remaining ones will form a basic set. In addition, RAN4 may consider a UE capability in view of different support levels related to VIL requirements
VIL: FFS on whether VIL shall be defined as the equivalent time of the interrupted slots or, equals to absolute RF retuning time defined in Rel-15
  FFS: depending on numerology
ML: If legacy gap pattern can be reused for NCSG, we can assume that MGL= VIL1+ML+VIL2
VIRP: If legacy gap pattern can be reused for NCSG, VIRP = MGRP of legacy MG
FFS on Per-UE/Per-FR NCSG applicability
  Option 1 : NCSG pattern should be configured based on MG configuration considering per FR1 or FR2 gap.
  Option 2: Support both per FR and per UE NCSG patterns

## Slide 14: NCSG configuration
FFS on Implicit or explicit configuration of NCSG
  Option 1. UE may assume the implicit and explicit configurations of NCSG are not concurrently activated.
    Implicit activation of NCSG means UE may introduce VILs at the start and stop of a configured MG while ML is the same as MGL and VIRP is the same as MGRP.
    Explicit activation of NCSG means UE follows the configuration of the network in terms of VIL1/VIL2/ML and VIRP.
  Option 2. NW explicitly configures the NCSG for VIL1/VIL2/ML/VIRP and offset.
FFS on Number of NSCG patterns configured
  Option 1. RAN4 should consider defining a limited number of suitable NCSG patterns and assign a UE capability to some of them, while the remaining ones will form a basic set. In addition, RAN4 may consider a UE capability in view of different support levels related to VIL requirements

## Slide 15: Impacts on RRM requirements due to NCSG
FFS on Interruption requirements
  Option 1: The interruption requirements in TS38.133 and TS36.133 shall be revisited
  Option 1a. for UE supporting per-FR gap, VIL is allowed only on the serving cell in the same FR wherein there is NCSG operation. Otherwise, VIL is allowed on all serving cells.
  Option 2: Existing interruption requirements for SCell activation/deactivation can serve as starting point for the study of VIL requirements
Requirements related to MGTA and impact to UL transmission follow Rel-15.
FFS on Per-UE or Per-FR capability support
  Option 1:per UE and per FR NCSG for RRM measurement needs the specific UE capability.

## Slide 16: Measurement applicability
FFS: whether NCSG can be configured simultaneously with legacy gap pattern
FFS on RF combination limitation
FFS on Rx beam limitation
FFS on searcher limitation
RAN4 needs to further investigate the scheduling and measurement restriction between serving cell L1 measurement, intra-frequency measurements and inter-frequency measurements for NCSG

## Slide 17: Specification impacts
FFS on Which clause can be used to include NCSG pattern in 38.133
  Option 1: Similar section for defining NCSG patterns can be introduced in the 38.133 section 9.1.2 Measurement capability.
  Option 2: NCSG patterns can be introduced in the 38.133 in a separate (dedicated) section

## Slide 18: Signaling
FFS on How to consider the relation between NCSG and ‘NeedForGap’?
  Option 1: Rel-17 NCSG to directly reuse Rel-16 ‘NeedForGap’ signalling with ‘no gap’ equaling NCSG.
  Option 2: The “NeedForGap” signaling structure can be reused for NR NCSG as a start point
  Other options not precluded.
FFS on NW configuration signaling e.g gp-ncsg0/1…/n like LTE.
Note: regardless of the selected option, decision will involve RAN2 feedback