## Slide 1
3GPP TSG-RAN WG4 Meeting #98-e R4-2103678
Electronic Meeting, 25 Jan. - 5 Feb., 2021
Agenda Item: 11.6.2
WF on FR1 HST RRM
CMCC

## Slide 2: Agreement
  Activated Scell, intra-frequency measurement without measurement gap
    PSS/SSS detection, time index detection, and measurement period for activated Scell for the scenario of intra-frequency measurement without measurement gap need to be enhanced
    For intra-frequency measurement without measurement gap, PSS/SSS detection requirements specified in R16 HST can be reused for the enhancement of PSS/SSS detection for activated SCell in R17 FR1 HST. Further enhancement can be further studied
    For intra-frequency measurement without measurement gap, time index detection requirements specified in R16 HST can be reused for the enhancement of time index detection for activated SCell in R17 FR1 HST. Further enhancement can be further studied
    For intra-frequency measurement without measurement gap, measurement period requirements specified in R16 HST can be reused for the enhancement of measurement period for activated SCell in R17 FR1 HST. Further enhancement can be further studied

## Slide 3: Agreement
  Activated Scell, intra-frequency measurement with measurement gap
    PSS/SSS detection, time index detection, and measurement period for activated Scell for the scenario of intra-frequency measurement with measurement gap need to be enhanced
    For intra-frequency measurement with measurement gap, PSS/SSS detection requirements specified in R16 HST can be reused for the enhancement of PSS/SSS detection for activated SCell in R17 FR1 HST. Further enhancement can be further studied
    For intra-frequency measurement with measurement gap, time index detection requirements specified in R16 HST can be reused for the enhancement of time index detection for activated SCell in R17 FR1 HST. Further enhancement can be further studied
    For intra-frequency measurement with measurement gap, measurement period requirements specified in R16 HST can be reused for the enhancement of measurement period for activated SCell in R17 FR1 HST. Further enhancement can be further studied

## Slide 4: Agreement
  Deactivated Scell, intra-frequency measurement without measurement gap
    PSS/SSS detection, time index detection, and measurement period for deactivated Scell for the scenario of intra-frequency measurement without measurement gap need to be enhanced
    Enhancement on PSS/SSS detection for deactivated Scell, intra-frequency measurement without measurement gap
      Similar enhancement to PCell measurement in R16 HST can be used as baseline for PSS/SSS detection enhancement on deactivated Scell.
        FFS whether Rel-16 Kp requirements modifications (if any) shall also apply for R17 HST

## Slide 5: Agreement
  Deactivated Scell, intra-frequency measurement without measurement gap
    Enhancement on time index detection for deactivated Scell, intra-frequency measurement without measurement gap
      similar enhancement to PCell measurement in R16 HST can be used as baseline for time index detection enhancement on deactivated Scell.
        FFS whether Rel-16 Kp requirements modifications (if any) shall also apply for R17 HST

## Slide 6: Agreement
  Deactivated Scell, intra-frequency measurement without measurement gap
    Enhancement on measurement period for deactivated Scell, intra-frequency measurement without measurement gap
      Option 1: similar enhancement to PCell measurement in R16 HST can be used as baseline for measurement period enhancement on deactivated Scell.
      Option 2:
      Other options are not precluded
      Note: FFS whether Rel-16 Kp requirements modifications (if any) shall also apply for R17 HST
DRX cycle | T SSB_measurement_period_intra
No DRX | 5 x measCycleSCell x CSSFintra
DRX cycle≤ 320ms | ceil(5 x M2 ) x max(measCycleSCell, DRX cycle)) x CSSFintra
DRX cycle> 320ms | Y x max(measCycleSCell, DRX cycle) x CSSFintra
M2 = 1.5 if SMTC periodicity > 40 ms, otherwise M2=1 Y=3 when SMTC <= 40ms, Y=5 when SMTC > 40ms | 

## Slide 7: Agreement
  Deactivated Scell, intra-frequency measurement with measurement gap
    Not to introduce the intra-frequency de-activated Scell measurement requirement with MG
  Legacy SCell deactivation delay can be reused in high speed train scenario
  FFS whether legacy SCell activation delay can be reused in high speed scenario

## Slide 8: Agreement
  FFS whether to discuss inter-frequency measurement enhancement under high speed scenario
  Except the requirements related with Scell activation/deactivation, other requirements to be discussed in work item of HST with CA
    Option 1: The requirements of timing, interruption, UL carrier RRC reconfiguration delay, link recovery (BFD/CBD), CSSF, Intra-frequency measurement, L1-RSRP measurement and measurement accuracy for L1-SINR measurement shall be further discussed in the work item of HST with CA.