## Slide 1: WF on NR NTN RRM requirements
Moderator: Fraunhofer HHI

## Slide 2: Outline
Proposed way forward based on the outcomes of “Email discussion summary for [98e][237] NR_NTN_solutions_RRM”
See R4-2103718

## Slide 3: Content
Topic #1: General RAN4 RRM NTN related aspects
Topic #2: GNSS requirements
Topic #3: PVT Satellite precision
Topic #5: NTN UL frequency synchronization requirement
Topic #7: RRM requirements for beam switching
Topics #4 and #6 are handled in separate documents, see R4-2103681 and R4-2103682.

## Slide 4: Summary
Main RRM issues and preliminary proposals have been discussed
  In green: proposals which are agreeable
  In orange: proposals for which a potential agreement may be found with suggested changes (needs further discussion)
  In purple: proposals for which there is no agreement yet

## Slide 5: Topic #1: General RAN4 RRM NTN related aspects
Sub-topic 1-1: RP to be considered for time and frequency synchronization
  Issue 1-1: Send information LS to RAN1
    Defer the LS. Further discuss the impacts of different reference points on RRM requirements and inform RAN1 in case any common observations are identified.
  Issue 1-2: Possibility of using satellite and gNB as time and frequency reference
    Further investigate the impact of different timing and frequency reference points based on RAN1 design on the RRM requirements. Inform RAN1 if any issues are identified.

## Slide 6: Topic #1: General RAN4 RRM NTN related aspects (cont’d)
Sub-topic 1-2: NTN use cases and scenarios
  Issue 1-3: Scenarios to be considered for NTN RRM
    Wait for RAN1, RAN2 and RAN4-RF to specify scenarios. The focus shall be on FR1 and single CC first.
Sub-topic 1-3: NTN RRM requirements
  Issue 1-4: Definition of NTN RRM requirements
  Issue 1-4: Definition of NTN RRM requirements
    As a starting point, RAN4 is to consider defining the NTN RRM requirements for
      Basic mobility procedure (cell reselection and HO)
      RRM measurement (delay and accuracy)
      Servicing cell related (RA, timing and RLM)
    Other requirements (e.g. beam related) are not precluded in the future

## Slide 7: Topic #2: GNSS requirements
Sub-topic 2-1: GNSS usage
  Issue 2-1: Definition of GNSS requirements
    Requirements shall be defined with on-board GNSS as the baseline. FFS on how to handle satellites/HAPS without on-board GNSS
Sub-topic 2-2: GNSS accuracy
  Issue 2-2: Impact of GNSS accuracy on RRM requirements
    RRM requirements can be assumed to be impacted by GNSS accuracy. Degree of impact and specific RRM requirements that are impacted are FFS.
  Issue 2-3: GNSS accuracy requirements
    GNSS accuracy is taken as an assumption to define other requirements. Explicit accuracy requirements are outside the scope of RAN4.
  Issue 2-4: Reference GNSS scenario
    Companies should define typical and worst-case scenarios. FFS which one will be used for defining RRM requirements.

## Slide 8: Topic #3: PVT Satellite precision
Sub-Topic 1: Requirements for PVT computation and distribution
  Issue 3-1: NTN PVT Accuracy Aspects
    Postpone discussion until RAN1 has reached a decision

## Slide 9: Topic #5: NTN UL frequency synchronization requirement
Sub-topic 5-1: Frequency accuracy requirements
  Issue 5-1: Will be handled in the RF session
  Issue 5-2: Time/Frequency pre-compensation accuracy requirements
    Tentative agreement: RAN4 to investigate factors that can affect time/frequency pre-compensation accuracy requirements. Specific requirements are FFS

## Slide 10: Topic #7: RRM requirements for beam switching
Sub-topic 7-1: Beam switching
  Issue 7-1: RRM requirements for beam switching
    RAN4 is to study the RRM requirements for beam switching once RAN1 has determined the final PCI mapping mechanism for NTN scenario.
    Further clarification and input from RAN1 and RAN2 is necessary, especially on beam/BWP/PCI mapping mechanisms and details.