## Slide 1: WF on NTN RRM timing related requirements
Xiaomi
3GPP TSG-RAN4 Meeting #98-e
Electronic Meeting, 25th Jan. – 5th Feb., 2021
Agenda item: 11.8.4
R4-2103681

## Slide 2: Background
The WF (R4-2017350) on NTN RRM requirement was approved in RAN4#97-e meeting
  NTN UL Time synchronization requirements, the following requirements shall be defined but require RAN1 further progress:
    Timing Advance adjustment accuracy
    Timing error limits & UE Time alignment behavior
    Timing Issues and Requirements for UE with 2 feeder-links
RAN1 Agreement in RAN1#103-e:
  An NTN UE in RRC_IDLE and RRC_INACTIVE states is required to at least support UE specific TA calculation based at least on its GNSS-acquired position and the serving satellite ephemeris.

## Slide 3: NTN UE UL timing requirements
For NTN networks, RAN4 is to study how to define the timing requirements:
  Option 1: Define the requirements on UE transmit timing error limit and timing advance adjustment accuracy, provided that:
    UE self-estimating error of NTA is counted into the UE transmit timing error.
    Timing advance adjustment accuracy is derived from the sampling interval with minimum UL bandwidth.
  Option 2: Define the requirements on UE transmit timing error limit and timing advance adjustment accuracy, provided that:
    UE self-estimating error of NTA will be counted into the timing advance adjustment accracy.
    UE transmit timing error is derived from the UE capability of estimating downlink timing
  Option 3: Define the requirements on UE transmit timing error limit, UE self-estimating accuracy of NTA and timing advance adjustment accuracy, provided that:
    UE transmit timing error is derived from the UE capability of estimating downlink timing
    Timing advance adjustment accuracy is derived from the sampling interval with minimum UL bandwidth.
    UE self-estimating accuracy is derived from the accuracy of UE GNSS-acquired position and the serving satellite position
  Other option is not precluded

## Slide 4: NTN UE transmit timing requirements
Te: Timing Error Limit
  The impact due to DL timing estimation, use existing Te requirements defined in TS 38.133, Table 7.1.2-1, as baseline for R17 NR NTN
  RAN4 is to further investigate whether other aspects have impact on the Te requirements for R17 NR NTN
  FFS: NTN timing compensation accuracy has impact on Te timing error requirements for CONNECTED mode. FFS for IDLE mode.
    FFS on whether the existing value defined in Table 7.1.2-2 in TS38.133 can be reused or not
    Gradual timing adjustment
      RAN4 is to study the gradual timing adjustment rules for NR NTN including:
        Tq (Maximum Autonomous Time Adjustment Step)
        Tp (Minimum Aggregate Adjustment rate)

## Slide 5: NTN UE timer accuracy
Reuse the UE timer accuracy requirements as defined in section 7.2 in TS 38.133 for Rel-17 NR NTN

## Slide 6: Timing advance
TA adjustment accuracy requirement
  Timing Advance adjustment accuracy requirement depends on the mechanism of TA adjustment step size determined by RAN1 and the total uncertainty budget.
  FFS: Timing Advance adjustment accuracy scales inversely proportional to SCS
  FFS: whether UE specific TA estimation accuracy has impact on timing advance adjustment accuracy requirements.
  UE specific TA estimation accuracy requirement
  RAN4 is to define the requirements for UE specific TA estimation accuracy
  FFS on how to capture the UE specific TA estimation accuracy
    Option 1: the UE specific TA estimation accuracy is counted into the UE transmit timing error requirement
    Option 2: the UE specific TA estimation accuracy is counted into the timing advance adjustment accuracy requirement
    Option 3: the UE specific TA estimation accuracy is defined as a separate accuracy requirement
    Other option is not precluded