## Slide 1: Way Forward on NR-U UE demodulation requirements
Qualcomm
3GPP TSG-RAN4 Meeting #98-e
Jan 25th – Feb 3rd, 2021
Agenda Item: 7.1.7.1/2/3
Tdoc Num: R4-2103805

## Slide 2: Test Scope
Semi-static Channel Access Devices v/s Dynamic Channel Access Devices
Prioritize test cases agnostic to semi-static and dynamic channel access devices if it is feasible.
Do not define additional test cases dedicated to FBE/LBE devices.
Tests with SMTC duration larger than COT duration should be deprioritized.

## Slide 3: Test Scope
Requirement definition according to UE capability of supporting CSI-validation features
FFS: Option 1: One generic LBT modelling for all test cases
    Option 1a: no applicable test cases for UE which does not support CSI-validation features
    Option 1c: for UE which does not support CSI-validation feature set LBT failure probability as 0. Separate requirements will be introduced.
FFS: Option 2: Different test set-up/[performance requirements] for UE with different UE capability
    Test set1: LBT modelling which applied for UE support CSI validation feature
    Test set2: Test set-up for UE which does not support support CSI-validation feature
      FFS how to enable TRS always on considering LBT failure

## Slide 4: Test Scope
For CSI Validation, define requirements for based on the optional capability ‘csi-RS-ValidationWith-DCI’
Do not introduce requirements based on optional capability typeB-PDSCH-length-r16.

## Slide 5: Test Scope
Test Scenarios
Define requirements for the unlicensed CC, and apply to both Scenario A and C.
If the test setup is the same, define a single set of PDSCH Requirements for the unlicensed CC
FFS: Details of the test set-up for scenario A and C;
For reference:
  Scenario A (Carrier aggregation between licensed band NR (PCell) and NR-U (SCell))
  Scenario C (Stand-alone NR-U (PCell))

## Slide 6: Test Scope
Define requirements definition for Scenario A for BW {20,40,60,80} MHz, to reuse the applicability rule in Rel-15 CA to test the largest supported BW.
Define requirements for Scenario C for 20 MHz only.

## Slide 7: Test Scope
Do not define tests for NR-U Demod PDCCH demodulation requirements;
Define CQI Requirements at least for UEs supporting optional capabilities related to CSI-RS Validation.
The decisions on the CQI Requirements definition for UEs not supporting optional capabilities will follow the agreements reached on the same issue related to PDSCH Requirements.

## Slide 8: Test Setup Details
Define tests with fixed DRS window duration set to 1ms.
Do not consider UL LBT Failure in DL Tests.
Reuse Rel-16 NR CA Requirements for the licensed cell where applicable;
Define Scenario C PDSCH requirements using Rel-15 NR PDSCH Requirements as a starting point;

## Slide 9: Test Setup Details, CQI Performance tests
UE reporting following a scheduled CSI-RS transmission cancelled due to LBT failure CQI Tests is expected to be disregarded and to be ignored for test pass/fail statistics.
FFS Type of CSI reporting:
  Option 1: Aperiodic CSI;
  Option 2: Periodic CSI with CSI-RS Validation;

## Slide 10: Test Setup Details, CQI Performance tests
FFS CQI Performance Test Design:
  Option 1: Two sets of burst transmissions, each with distinct transmission power level and keeping the interference level constant during the test.
  Option 2: Two different runs with different SNR values
CQI Test Metrics: FFS to study the impact of LBT on PDSCH measurement

## Slide 11: Downlink Transmission Model
Use Burst Transmission Model for LAA (36.101-4, B.8) as a starting point.
Use a fixed DL Transmission Periodicity (or FFP in Dynamic Channel Access).
The DL periodicity is 5 ms.
The Maximum COT duration within the DL periodicity is 4 ms, to comply with local regulations.
Use a Random DL duration within the COT, with equal probability between:
-Option 1: {2,3,5,6} Slots;
-Option 2: {2,4,6,8} Slots;
  To be verified that Option 2 does not cause issues with Japan regulation

## Slide 12: Downlink Transmission Model
Details on allocation within the COT
Allocate PDCCH in Symbols 0 and 1, in every slot in the DL COT.
Allocate PDSCH from Symbol 2 to Symbol 13 in every slot within the DL COT, except for the last slot in the DL COT.
Allocate PDSCH in Symbols FFS [{5-14}, {6,9,12,14}] in the last slot in the DL COT.
Always schedule UL Slot in the last fully available slot of the DL Transmission Periodicity/FFP to avoid Cross-COT HARQ, assuming a minimum timing K1 sufficient according to spec (assuming 1 slot is sufficient).
TDD Pattern can be defined once agreements are reached on FFP duration, COT and UL scheduling.

## Slide 13: LBT Parameters
Model LBT Failure as part of the Downlink Transmission model;
Apply the Downlink Transmission model to all DL signals in unlicensed carrier (including SSB and TRS transmission);
Define a single LBT model, to be used for both ‘dynamic’ and ‘semi-static’ Channel Access;
Do not define tests with sub-band LBT failure (either all sub-bands are transmitted, or no sub-band is transmitted).

## Slide 14: LBT Parameters
Define the same probability of LBT Failure for Scenario C and Scenario A.
FFS The probability value is [0.50, 0.25].

## Slide 15: Simulation Assumptions for PDSCH Tests
Use 20 MHz LBT BW (for channel sensing and clear channel assessment).
Do not multiplex SSB and Data.
Define tests for TDD 30kHz only.
Define tests with low delay spread and low doppler speed propagation channel.
Q factor for SSB: = 8;

## Slide 16: Simulation Assumptions for PDSCH Tests
Use Type A PDSCH Mapping Type.
Do not use PDCCH DCI 2-0 in the PDSCH Tests

## Slide 17: Detailed Simulation assumptions [1/3]
Test num. | Reference channel | Bandwidth (MHz) / Subcarrier spacing (kHz) | Modulation format and code rate | Slot Pattern | Propagation condition | Correlation matrix and antenna configuration | Reference value | 
 |  |  |  |  |  |  | Fraction of maximum throughput (%) | SNR (dB)
1-1 | NR-U DL Transmission Model | [20, 40, 60, 80]/30 | 16 QAM, 0.48 | According to NR-U DL Transmission Model | TDLA30-10 | 2x2, ULA Low | 70 | [TBD]
Test num. | Reference channel | Bandwidth (MHz) / Subcarrier spacing (kHz) | Modulation format and code rate | Slot Pattern | Propagation condition | Correlation matrix and antenna configuration | Reference value | 
 |  |  |  |  |  |  | Fraction of maximum throughput (%) | SNR (dB)
2-1 | NR-U DL Transmission Model | [20, 40, 60, 80]/30 | 16 QAM, 0.48 | According to NR-U DL Transmission Model | TDLA30-10 | 2x4, ULA Low | 70 | [TBD]

## Slide 18: Detailed Simulation assumptions [2/3]
Parameter |  | Unit | Value
Active DL BWP index |  |  | 1
Slot Pattern |  |  | [TBD, according to decision in the WF]
LBT failure probability |  |  | [0.50, 0.25]
Common serving cell parameters | Physical Cell ID |  | 0
 | SSB position in burst |  | The first SSB
 | SSB Q factor |  | 8
PDSCH configuration | Mapping type |  | Type A
 | k0 |  | 0
 | Starting symbol (S) |  | 2
 | Length (L) |  | According to DL Transmission Model
 | PDSCH aggregation factor |  | 1
 | PRB bundling type |  | Static
 | PRB bundling size |  | 2
 | Resource allocation type |  | Type 0
 | RBG size |  | Config2
 | VRB-to-PRB mapping type |  | Non-interleaved
 | VRB-to-PRB mapping interleaver bundle size |  | N/A
PDSCH DMRS configuration | DMRS Type |  | Type 1
 | Number of additional DMRS |  | 1
 | Maximum number of OFDM symbols for DL front loaded DMRS |  | 1
RB Allocation |  |  | Full BW
MIMO Layers |  |  | 2
Number of HARQ Processes |  |  | 8
TX EVM |  |  | 6%

## Slide 19: Detailed Simulation assumptions [3/3]

## Slide 20: CR Work Split
Item List | Description | Company
1 - CR Work | PDSCH Performance Requirements for Scenario A (Can be split in 2/4 RX if needed) | Ericsson
2 - CR Work | PDSCH Performance Requirements for Scenario C (Can be split in 2/4 RX if needed) | MediaTek
3 - CR Work | [CQI Requirements for Scenario A if agreed] | Apple
4 - CR Work | [CQI Requirements for Scenario C if agreed] | Huawei
5 - CR Work | Introduction of new Fixed Reference Channel and TDD Pattern | Huawei
6 - CR Work | Introduction of new Downlink Transmission Model | Qualcomm
7 – Simulation Work | Collect and Organize Simulation results. | Apple