## Slide 1
WF on single link tests for NR V2X demodulation performance
3GPP TSG-RAN WG4 Meeting #98-e Electronic Meeting, 25 Jan. – 5 Feb., 2021
Agenda Item: 7.3.6.1
R4-2103810
LG Electronics

## Slide 2: PSSCH demodulation
Following additional PSSCH demodulation tests are introduced
  16QAM for 260km/h relative velocity
  64QAM for 30km/h relative velocity
Test for 256QAM modulation order
  256QAM is not introduced in Rel-16. Considering RAN4 work load and time limitation in Rel-16, RAN4 can further discuss and define corresponding requirements if needed in Rel-17 timeframe i.e. Rel-17 side-link enhancement WI.
Test for gNB based sync
  gNB sync source based test is not introduced in Rel-16. Considering RAN4 work load and time limitation in Rel-16, RAN4 can further discuss and define corresponding requirements if needed in Rel-17 timeframe i.e. Rel-17 side-link enhancement WI.

## Slide 3: PSSCH demodulation
Test 1: Remaining issues for QPSK for 500km/h relative velocity (already agreed the test)
  20 PRB for PSSCH resource allocation
    10 PRB sub-channel size and number of allocated sub-channels is 2
  PSFCH periodicity
    4 periodicity
  DMRS pattern
    {3,4} DMRS symbols
  Propagation condition
    Option 1: TDLA30
    Option 2: TDLB100
  Beta value for 2nd stage SCI
    Beta value = 3.5

## Slide 4: PSSCH demodulation
Test 2: Remaining issues for 16QAM for 260km/h relative velocity
  20 PRB for PSSCH resource allocation
    10 PRB sub-channel size and number of allocated sub-channels is 2
  DMRS pattern
    {2,3} DMRS symbols
  Beta value for 2nd stage SCI
    Beta value = 5

## Slide 5: PSSCH demodulation
Test 3: Remaining issues for 64QAM for 30km/h relative velocity
  PRB for PSSCH resource allocation
    Option 1: 10 PRBs PSSCH allocation
    Option 2: 10 PRB sub-channel size and number of allocated sub-channels is 2
    Option 3: 20 PRBs PSSCH allocation with single sub-channel size
  PSFCH periodicity
    4 periodicity
  DMRS pattern
    2 DMRS symbols
  Beta value for 2nd stage SCI
    Beta value = 5

## Slide 6: PSCCH demodulation
Remaining issue for PSCCH demodulation test
  Payload size
    26bit

## Slide 7: RMC naming
RMC naming
  Follow RMC naming of TS38.101-4 NR demodulation
    E.g., R.PSSCH.2-x.y, R.PSCCH.2-x.y

## Slide 8: Specification structure
Additional agreement for specification structure for NR V2X
  Add sub-clause with number of Rx antenna
11. V2X Requirements 11.1 Demodulation performance requirements (conducted requirements) 11.1.1 General 11.1.2 PSSCH demodulation requirements 11.1.2.1 2Rx requirements 11.1.2.1.1 Minimum requirements 11.1.3 PSCCH demodulation requirements 11.1.3.1 2Rx requirements 11.1.3.1.1 Minimum requirements ...... [other tests have the same approach] A.6 SL reference measurement channels A.6.1 General A.6.2 Reference measurement channels for PSSCH performance requirements A.6.2.1 Reference measurement channels for SCS 15kHz FR1 A.6.2.2 Reference measurement channels for SCS 30kHz FR1 A.6.3 Reference measurement channels for PSCCH performance requirements A.6.3.1 Reference measurement channels for SCS 15kHz FR1 A.6.3.2 Reference measurement channels for SCS 30kHz FR1 A.6.4 Reference measurement channels for PSBCH performance requirements A.6.4.1 Reference measurement channels for SCS 15kHz FR1 A.6.4.2 Reference measurement channels for SCS 30kHz FR1 ..... [other physical channels have the same approach if needed] A.7 SL reference resource pool configurations