## Slide 1: Way forward on multiple link tests for NR V2X demodulation performance
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #98-e
E-meeting, 25 January – 5 February 2021
Agenda Item: 7.3.6.3
R4-2103819

## Slide 2: Power imbalance requirements
      Agreements from RAN WG4 Meeting #97-e
  Methodology for NR V2X power imbalance test
    Reuse the methodology from LTE V2X power imbalance test
  PSSCH MCS 4
  Test metric: PSSCH BLER 10% of Sidelink UE 2
      Agreements for RAN WG4 Meeting #98-e
  ICS level: -27dBc
  Distance between the two links: 20 PRBs, UE1 PRBs 0-9, UE2 PRBs 30-39
  SCI format 2-A configuration: Payload = 35 Bits, = 1, = 3.5.
  SNR UE1 = 30.35 dB

## Slide 3: HARQ buffer soft combining test
      Agreements from RAN WG4 Meeting #97-e
  Test purpose
    The main test purpose is to verify HARQ buffer combining. Configuring of high MCS and long interval between transmission and retransmission is not precluded.
  Test design
    CBW: 20 MHz
    For verification of n16 and n24, 16 or 24 UEs transmit signal one by one circularly for every slot and in the first subchannel.
    For verification of n32, the first 31 UEs transmit signal one by one circularly for every slot and in the first subchannel. The 32nd UE transmit signal in the same slot as the first UE but in the second subchannel.
    For verification of n64, first 31 UEs transmit signal one by one circularly for every slot and in the first subchannel, the next 31 UEs transmit signal one by one circularly for every slot and in the second subchannel, the last 2 UEs transmit signal in the same slot as the first two UEs but in the third subchannel.
  Propagation conditions: AWGN channel model
  PSCCH resource allocation: 2 symbols and 10 RBs
  2 DMRS symbols for PSSCH
  PSFCH configuration: PSFCH with periodicity 1
  Test metric: 5% of PSSCH BLER

## Slide 4: HARQ buffer soft combining test
      Agreements for RAN WG4 Meeting #98-e
  Test design for UE supporting n48 HARQ processes
    Add the following test to verify UE support receive 48 HARQ processes per slot: “For verification of n48, the first 31 UEs transmit signal one by one circularly for every slot and in the first subchannel. The next 17 UEs transmit signal one by one circularly for every slot and in the second subchannel
  Sub-channel size: 10 PRBs
  SCI stage 2 configuration: Payload = 35 Bits, = 2.5
  MCS
    MCS 28
  Rx assumptions for simulation alignment
    Option 1: 600 Hz frequency offset and 12 Ts time offset
    Option 2: 0 Hz frequency offset and 0 Ts time offset
    Companies are encouraged to prepare link level simulation results for Option 1 and Option 2 in the next RAN4 meeting for scenarios with and without soft combining
  How to define the requirements for different supported max number of HARQ process
    One set of performance requirements based on the results of n64

## Slide 5: PSFCH decoding capability test
      Agreements from RAN WG4 Meeting #97-e
  Test design
    N UEs transmit PSFCH one by one following procedure from Section 16.3 of TS 38.1213
    N is {5, 15, 25, 32, 35, 45, 50, 64} depending on UE capability
  PSFCH periodicity 1
  Feedback mode: ACK/NACK
  Propagation conditions
    Static propagation condition without external noise
  Test metric
    Pr(DTX to ACK)<1% and Pr(ACK miss)<1%
      Agreements for RAN WG4 Meeting #98-e
  CBW/SCS
    40 MHz, 30 kHz
  Number of sub-channels
    Multiple subchannels of size 10 PRBs (i.e. 10 for 40 MHz case)

## Slide 6: PSCCH/PSSCH decoding capability test
      Agreements from RAN WG4 Meeting #97-e
  DMRS configuration: 2 DMRS symbols
  MCS 4
  Propagation conditions: Static propagation condition without external noise
  Test metric: Probability of missed PSCCH 1%
      Agreements for RAN WG4 Meeting #98-e
  CBW and feedback configuration
    Option1: No PSFCH, AT command and 40 MHz
    Option2: Using PSFCH with PSFCH with periodicity 1 and flexibly CBW depending on psfch-TxNumber capability:
      40MHz channel bandwidth is for the UE supporting psfch-TxNumber =n16, 20MHz/30MHz channel bandwidth is for the UE supporting psfch-TxNumber =n8, and 10MHz channel bandwidth is for the UE supporting psfch-TxNumber =n4.
    Option 3: 40 MHz CBW, PSFCH based feedback and following test methodology
      TE sets PSSCH priority (in PSCCH) when PSFCH Tx capability < 10, x PSSCH with higher priority, 10-x PSSCH with lower priority. Note that PSFCH is selected according to PSSCH priority, hence if PSFCH Tx capability = x, the x feedback corresponding to x high priority PSSCH is transmitted to TE.
      TE can verify UE PSCCH decoding success or failure by checking whether all the higher priority PSSCH feedback is received. In order to always feedback all the high priority SCHs, UE has to decode all CCH to know the priority.
      To avoid UE cheating, TE can randomize the location of higher priority PSSCHs
    Companies are encouraged to analyze the pros and cons of each option for the next RAN4 meeting.
  Verification of 2*floor(NRB /10 RBs) capability
    Not to verify 2*floor(NRB /10 RBs) capability in Rel-16 V2X

## Slide 7: SDR with active sidelink test
      Agreements for RAN WG4 Meeting #98-e
  Not define the SDR test cases with active sidelink in Rel-16 V2X WI.
  RAN4 also realize with such agreements, the co-current operation has not been verified by Rel-16 RAN4 demodulation requirements. RAN4 can further discuss and define corresponding test cases if needed in Rel-17 timeframe i.e. Rel-17 sidelink enhancement WI.