## Slide 1: Way forward on UE/BS demodulation on NR 47GHz band
Ericsson
3GPP TSG-RAN WG4 Meeting #98-e
Electronic meeting, 25 January – 5 February 2021
Agenda item: 9.25.4.2, 9.25.4.3
Document for: Approval
R4-2103875

## Slide 2: Agreements for UE demodulation requirements on NR 47GHz band
Whether the existing UE performance requirements applicable for 47GHz band or not
  Interested companies are encouraged to provide the evaluation results whether the existing UE demodulation requirements are applicable for 47GHz band or not
    For evaluation, use MCS 18 Rank 1 (Test 1-3 in TS38.101-4 Table 7.2.2.2.1-3) and MCS 17 Rank 2 (Test 2-6 in Table 7.2.2.2.1-4) for n262, as an example.
      Other scenarios are not precluded
    Phase noise (PN) model is up to UE implementation
Set Noc level for n262 in TS38.101-4 Table 4.5.3.2-1 based on REFSENS defined in RF session

## Slide 3: Agreements for BS demodulation requirements on NR 47GHz band
Requirements applicability
  The baseline assumption is the existing BS requirements are applicable up to 52.6GHz
  Companies can bring more analysis to further check whether above assumption is valid or not
Test feasibility
  Companies are encouraged to bring more analysis for link-budget issue and absolute power level in receiver side to ensure 47GHz performance requirements testability
Update of BS demodulation requirements in TS38.141-2
  No updates on ΔOTAREFSENS, EISREFSENS_50M and ΔFR2_REFSENS, are expected for n262
  MU and TT may need to be updated according to the conclusion in RF session