## Slide 1
3GPP TSG-RAN WG4 Meeting #98-e R4-2103876
Electronic Meeting, Jan. 25 - Feb. 5, 2020
Agenda Item: 11.6.3
WF on UE demodulation for FR1 HST
CMCC

## Slide 2: PDSCH requirements for CA scenarios
  Maximum doppler shift
    Reuse Maximum Doppler shift and corresponding configuration from Rel-16 HST-SFN requirements( 870 Hz for 15 kHz SCS; 1667 Hz for 30 kHz SCS)

## Slide 3: PDSCH requirements for CA scenarios
  Transmission schemes
    Define HST CA requirements for HST-SFN joint transmission
    FFS whether to define HST CA requirements for DPS transmission scheme (with one active TCI state and/or two active TCI states)
      It’s RAN4 common understanding DPS scheme can achieve better performance compared to joint transmission schemes and no advanced received required for HST deployment.
      Candidate option for further discussion:
        It’s RAN4 recommendation to include DPS scheme into FR1 HST WI, and further discuss whether test cases need to specified or not, and if specified, test applicable rules will be specified to ensure only one scheme will be verified for CA cases for UE.

## Slide 4: PDSCH requirements for CA scenarios
  Antenna configuration
    2x2 and 2x4
  Define PDSCH CA demodulation requirements with the combination of following component carriers:
    for 15KHz SCS, specify PDSCH requirements on single carrier of BW of {5, 10, 15, 20, 25, 30, 40, 50} MHz
    for 30KHz SCS, specify PDSCH requirements on single carrier of BW of {5, 10, 15, 20, 25, 30, 40, 50, 60, 80, 90, 100} MHz
    for FDD 10MHz/15kHz SCS and TDD 40MHz/30kHz SCS, reuse SNR from the Rel-16 NR HST WI, and run simulation for other cases

## Slide 5: PDSCH requirements for CA scenarios
  HARQ process
    Reuse HARQ process number and k1 values for HST CA requirements as in normal CA requirements
  Add 1 dB margin to all CA requirements for HST-SFN JT similar to single carrier requirements

## Slide 6: PDSCH requirements for CA scenarios
  SCS configuration
    At least cover following cases:
      FDD 15 kHz + FDD 15 kHz
      TDD 30 kHz + TDD 30 kHz
      FDD 15 kHz + TDD 30 kHz
    FFS whether following need to be included or not:
      FDD 15 kHz + TDD 15 kHz CA
      TDD 15 kHz + TDD 30 kHz CA

## Slide 7: PDSCH requirements for CA scenarios
  MCS, Rank, and other test setup
Parameter | Value
DMRS type | type 1
Number of DMRS symbols | DMRS 1+1+1
TDD pattern | DDDSU, S: 10D+2G+2U for 15 kHz SCS 7DS2U, S: 6D+4G+4U for 30 kHz SCS
MCS | For HST-SFN JT: MCS 13 based on 64QAM table For DPS: MCS 17 based on 64QAM table Note: can be updated depending on the discussion of whether to define HST CA requirements for DPS transmission scheme
TRS periodicity | 10 ms, 2 slot pattern
PDSCH mapping | Type A, Start symbol 2, Duration 12
Ds and Dmin | Ds = 700m, Dmin = 150m
Rank | Rank = 2
Testing metric | SNR @ 70% of maximum throughput

## Slide 8: PDSCH requirements for CA scenarios
  Applicability rule for SCS configuration
    FFS whether reuse CA CQI applicability rule on CA duplex modes for testing: If UE supports both FDD 15 kHz + TDD 30 kHz and FDD 15 kHz + FDD 15 kHz CA duplex modes, apply requirements only to the first one
  Applicability rule for PCell configuration
    Use same applicability rule for Pcell configuration for HST CA requirements as in normal CA requirements

## Slide 9: PDSCH requirements for CA scenarios
  Release independent
    FFS whether HST PDSCH CA requirements can be release independent from Rel-15
  UE capability and network-assisted signalling
    FFS whether existing HST network assisted signaling and UE capability can cover CA scenario

## Slide 10: Enhanced transmission schemes
  Whether to specify PDSCH requirements for transmission scheme 2
    Firstly, focus on the study and evaluate the performance benefits of transmission scheme 2 in HST-SFN deployment comparing to other transmission schemes.
  Channel model
    Set Ds=700m and Dmin=150m as baseline
    Take maximum Doppler frequency “870Hz for 15KHz SCS, 1667Hz for 30KHz SCS” as baseline
      Further check whether Doppler/timing offset may exceed maximum UE capability with the assumption of Non-ideal synchronization

## Slide 11: Enhanced transmission schemes
  Time/frequency errors and assumptions on UE synchronization
    Single FFT operation can be assumed as baseline UE implementation for HST scenario
    Non-ideal synchronization between RRHs should be considered as a baseline assumption

## Slide 12: Enhanced transmission schemes
  Reference performance for comparison
    Option 1: mDCI-based transmission vs. HST-SFN joint transmission
    Option 2: mDCI-based transmission vs. HST-DPS
    Other options are not precluded
  Evaluation criteria
    Option 1: Max achievable throughput across all scheduled TB
      Different train locations and SNR points should be analyzed
    Option 2: SNR at 70% @max achievable throughput
    Option 3: Max supported Doppler frequency
    Other options are not precluded

## Slide 13: Enhanced transmission schemes
  PDSCHs allocations between different RRHs
    Baseline assumption for evaluation: reuse the same PRB allocation as Rel-16 eMIMO multi-DCI based transmission, i.e., overlapped in time domain but not overlapped in frequency domain
    FFS whether to consider both overlapped and non-overlapped PDSCHs allocations between different RRHs for performance analysis
  MCS
    MCS 13 and MCS 17 as baseline assumption for further evaluations
      For mDCI-based transmission vs. HST-SFN joint transmission, use MCS13
      For mDCI-based transmission vs. HST-DPS, use MCS 17
      Note: which MCS is adopted depends on the outcome of the discussion on Reference performance for comparison

## Slide 14: Enhanced transmission schemes
  Other parameters for evaluation:
    Antenna configuration: 2x2 and 2x4
    Rank: Rank 2
      DMRS ports 1000/1001 from TRP #(2i)
      DMRS ports 1002/1003 from TRP #(2i+1)
    DMRS type: Type 1
    Number of DMRS symbols: DMRS 1+1+1
    For TDD
      Use TDD pattern of 7D1S2U with S=6DL:4GP:4UL
      No PDSCH data transmission in the special slots
    TRS periodicity: 10ms

## Slide 15: Enhanced transmission schemes
  Link adaptation
    Use fixed FRC to define PDSCH demodulation requirements
    Fixed MCS approach is the baseline for performance analysis.
    Link adaptation approach can be considered if benefits with fixed MCS will not be observed for multi-DCI Tx scheme comparing to other schemes.

## Slide 16: Simulation
  Interested companies are encouraged to provide the simulation results of HST-SFN joint transmission and DPS for FDD SCS=15kHz and TDD SCS=30kHz with BW listed in page 4 according to the simulation assumption in page 7.
  Interested companies are encouraged to provide the performance evaluation of transmission scheme 2 (i.e., multi-DCI based transmission scheme) in high speed condition according to pages 10 – 15.