## Slide 1: WF on NR repeaters EMC
ZTE, [...]
3GPP TSG-RAN WG4 Meeting # 98-e
Electronic Meeting, 25 Jan – 5 Feb, 2021
R4-2103879
Agenda item: 11.11.4
Document for: Approval

## Slide 2: Background
A new WID RP-202927[1] was approved in last RAN Plenary, where a new TS for NR repeaters EMC was approved.
In RAN4 #98e meeting, some technical issues for NR repeaters (especially for TDD) comparing with LTE FDD repeaters were discussed in 1st round email discusison, where:
  One company think test condition and Performance assessment and Performance criteria in TS36.113 cannot be directly used for NR repeater, especially for TDD.
  Three companies think it might be good to further study before deciding reusing anything from LTE considering NR repeater is not the same with LTE repeater, also pending on the repeater RF discussion.
  Meanwhile one company would like to know what is the motivation to have separate EMC specification.
In addition, company think some EMC requirements and tests that are device-agnostic (ESD, Voltage dips, etc.), that could be reused from other specifications for NR repeaters.
LTE repeaters EMC requirements are captured in TS36.113. No NR spec covering NR repeaters EMC requirements so far.

## Slide 3: NR repeater EMC vs LTE repeater EMC
  Comparing with LTE FDD repeater, whether or not test condition and Performance assessment and Performance criteria in TS36.113 can be directly used for NR repeaters, especially for TDD?
The following options were identified during the meeting:
  Option 1: No, it cannot be directly used for NR repeaters, especially for TDD
  Option 2: It is premature to decide, pending on the repeater RF discussion, more discussions are needed.
  WF: provide further analysis of sections a/b/c (below) in TS 36.113 and TS 38.113 for LTE FDD repeater EMC and NR FDD/TDD repeater EMC:
  test condition and
  Performance assessment and
  Performance criteria

## Slide 4: EMC requirements
The following requirements are referred to CISPR or IEC specifications and can be applied to NR repeaters in transparent way:
  Radiated emission(ancillary equipment), conducted emission (including DC power input/output port, AC mains power input/output port, Telecommunication port) , Harmonic current emissions(AC mains input port), Voltage fluctuations and flicker (AC mains input port)
  RF electromagnetic field (80 MHz to 6000 MHz), conducted immunity (0.15 MHz - 80 MHz), ESD, EFT, Voltage dips, surges
WF: provide further analysis to check if LTE repeater EMC requirements listed above can be reused for NR FDD/TDD repeater EMC

## Slide 5: EMC specification for NR repeater
How to capture the NR repeaters EMC requirements?
The following options were identified during the meeting:
  Option 1: Keep as approved in RAN #90 meeting[1], i.e. generate a new TS to capture NR repeaters EMC requirements
  Option 2: Extend the TS 38.113 (NR BS EMC) scope to capture NR repeaters EMC requirements
  Option 3: To be discussed once EMC requirements are agreed

## Slide 6: References
RP-202927, New WID on NR Repeaters, Qualcomm
R4-2103742, ”Email discussion summary for [98e] [303] NR_EMC”, ZTE Coporation
R4-2102181, Discussion on NR repeaters EMC, ZTE Coporation
R4-2102180, Proposal on the skeleton of NR repeaters EMC, ZTE Coporation
R4-2100361, Discussion on the definition of EMC requirements for NR Repeater. Ericsson
R4-2102579, EMC core requirements for NR repeater, Huawei