## Slide 1: WF on FR2 MIMO OTA simulation assumption
Huawei, HiSilicon
R4-2103915
3GPP TSG-RAN WG4 #98-e
Electronic meeting Jan. 25-Feb. 5, 2021
Agenda item: 11.1.2
Document for: Approval

## Slide 2: Background
WF[1] is approved in RAN4 #97-e, following agreements are captured:
  both simulation results and measurement results are permitted to define requirements.
  Simulation parameters should be aligned with testing condition as much as possible, such as RMC, channel models, chamber environment, different UE form factors, etc.
  The potential gap between simulation and measurement should be discussed.
  simulation work plan in R4-2014829 is agreed as baseline.
In RAN4 #98-e meeting, FR2 simulation parameters are further discussed based on TR 38.827 and the approved WFs[1][2].

## Slide 3
FR2 MIMO OTA simulation assumptions
Assumption Items | Current status in TR 38.827 | Simulation assumptions for FR2 MIMO OTA | Note
The direction of the BS strongest beams | Not stated | CDL-A InO: (-4.0°, 93.6°) CDL-C UMi: (-12.0°,100.7°) | 
Clusters | CDL-A InO: 24 clusters CDL-C UMi: 23 clusters | Take 40 dB as threshold to apply on clusters, i.e. CDL-A InO: #2, #3, #4 CDL-C UMi: #1, #2, #3, #4, #5, #6, #7, #8, #10, #11, #13, #14, #15, #16 | Not valid if Opt 2 in PSP for simulation is adopted.
PSP for simulation | PSP validation measurements procedure is provided Target PSP for validation is FFS | Op1: Target PSP for simulation is slightly higher than the real PSP validation. How to emulate PSP in the simulation is FFS. Op2: RAN4 to provide the reference of channel model parameters after BS filtering under 6 probes layout. The feedback/information about 6 probes weights from CE/TE vendors might be needed. | 
UE antenna array | N/A | All options can be taken for simulation, in which OP1 and OP2 are with high priority Op1: two panels 2x2 patches Op2: two panels 1x4 patches Op3: three panels 2x2 patches Op4: three panels 1x4 patches | 0.5λ element spacing in horizontal and vertical dimension
BS/UE antenna parameters and Beam forming | BS antenna parameters are listed in Table 7.2-7 | BS antenna parameters and Beam forming follows TR 38.827 UE antenna parameters and Beam forming: Op1:Follow TR 38.803 Op2:Depends on UE implementation Op3:other is not precluded | 
Polarization alignment Between gNB/TE and UE side | N/A | Op1: polarization aligned between UE and TE, i.e. Op2: Polarization is 45o crossed between UE and TE, i.e. Op3: Polarization mismatch from different test directions is considered | 
Minimum number of slots | UMi CDL-C: 20k InO CDL-A: 75k | follows TR 38.827 | 
RMC parameters | Table 8.2-6 and Table 8.2-7 | 16QAM, 100MHz BW, 120kHz SCS Other RMC parameter follows TR 38.827 sub clause 8.2 | 

## Slide 4
[1] R4-2017585 “WF on NR MIMO OTA”, vivo, CAICT, Spirent, Huawei, Hisilicon, Samsung
[2] R4-2017585 “WF on FR2 MIMO OTA simulation assumption”, Huawei, HiSilicon
[3] R4-2102719 “Simulation assumption summary for NR FR2 MIMO OTA”, Huawei, HiSilicon
[4] R4-2102497 “Discussion on FR2 MIMO OTA performance requirements”, Qualcomm Incorporated
Reference