## Slide 1: WF on ETC and test time reduction
vivo
3GPP TSG-RAN WG4 Meeting #98-e R4-2103920
Electronic Meeting, Jan. 25-Feb. 5, 2021
Agenda item: 12.1.1
Document for: Approval

## Slide 2: ETC impact on test system
  EIRP/EIS beam peak searching procedure under ETC:
    Option 1: perform 3D scan
    Option 2: beam peak search within a certain cone of directions around peak position under NTC (by declaration or NTC peak searching results)
    -> By default, option 1 applied; if declaration present from UE vendor, then option 2 applied.
    Note: option1 is needed for UE with best antenna panel switch based on temperature and/or UE without declaration present (Further work on the texts into TR if needed)
  RAN4 agrees to define a temperature tolerance for FR2 ETC system. Several aspects need to consider:
    an accuracy of temperature control by an air conditioner
    accuracy of a thermocouple to measure a temperature in the ETC enclosure
  The value of temperature tolerance is FFS.
    [+/- 4] degrees Celsius tolerance is the starting point
    Test only can be executed under target temperature within the tolerance

## Slide 3: Test Time Reduction (1-MG)
  New Measurement Grid (MG) based on 4x2 array antenna assumption for PC3
    New Measurement grid with 4x2 array is one of the basic approaches to reduce the test time of spherical coverage and TRP based test cases as well as beam peak searches.
    New measurement grid by 4x2 array assumption should be recommended to RAN5 as additional option for PC3 conformance testing
      Different measurement grid can be selected based on manufacturer declarations
    Inform RAN5 via LS to allow the spherical coverage, TRP and beam peak search measurement grid requirements to be relaxed based on an optional vendor declaration while keeping the system-related assumptions unchanged in RAN5, i.e., based on the previously agreed worst case 8x2 assumptions.
Antenna Assumption Grid Type | 8x2 | 4x2 | Factor of Improvement
Constant-Step Size | 1106 | 366 | 3.0
Constant-Density | 800 | 275 | 2.9
Min Number of Grid Points for TX/RX Beam Peak Search

## Slide 4: Test Time Reduction (2-RSRP)
  RSRP(B) based RX beam peak search
    The general idea of RSRP(B) based RX beam peak search is agreed in RAN4
    Further discuss whether to use RSRP or RSRPB for the procedure
    Detailed test procedure on only RSRP(B)-based measurement or RSRP(B)&EIS-based measurement needs further study
  FFS RAN4 need to define a reasonable RSRP(B) accuracy at high power levels which is different as current TS 38.133
    The RSRP(B) accuracy should be defined based on simulation campaign in RRM session
  Further study RSRP(B) based RX beam peak search approach, including the test procedure, MU and UE performance impacts

## Slide 5: Test Time Reduction (3-Single Pollink)
  EIRP test of UL MIMO
    Single link polarization measurement is feasible for EIRP test in principle and details can be further optimized
    Further study antenna impact etc.
  EIRP test of Tx diversity
    Single link polarization measurement is feasible for EIRP test in principle and details can be further optimized
    Further study antenna impact etc.

## Slide 6: Test Time Reduction (4-others)
  Beam sweeping techniques
    RAN4 identified that this is related to UE behavior, whether this approach can be applied for conformance testing is FFS
  Define less sampling points for Rx test cases compared with Tx
    This approach is considered as an additional option based on the potential new measurement grid of 4x2, to further reduce the test time
    Needs further study the benefit after concluding the basic new measurement grid
  OEMs may declare search ranges where a beam peak is possibly located (e.g. hemisphere) along with applicable DUT alignment options
  Alternative search algorithms (e.g., coarse and fine searching)
    This approach is considered as an additional option based on the potential new measurement grid of 4x2, to further reduce the test time
    For Rx test cases, further discuss the necessarily of this approach ,if RSRP&EIS-based approach is adopted for Rx beam peak searching
  Fast spherical coverage test procedure
    The approach can be applied in addition to the new measurement grids
    The approach is considered a test time improvement, further details on the text proposal can be discussed next meeting.

## Slide 7: Test time reduction: prioritization of candidate solutions
Prioritization of candidate solutions
  Options 1-MG, 2-RSRP, and 3-Single Pollink are prioritized in the study, and their completion can conclude the test time reduction objective
  Work on 4-Others, including potential new options, is not precluded

## Slide 8: Reference
TDoc | Title | Source
R4-2100098 | DUT repositioning during ETC measurement in FR2 | Anritsu corporation
R4-2100161 | Test time reduction in FR2 using beam sweeping | Fraunhofer HHI, Fraunhofer IIS
R4-2100245 | Test time reduction in OTA measurement | Anritsu Corporation
R4-2100528 | Impact of ET on measurement uncertainty and test tolerance of spherical coverage EIRP and EIS | Apple Inc.
R4-2100665 | Discussion on enhance test method to reduce FR2 OTA test time | LG Electronics Inc.
R4-2100895 | Discussion on FR2 test time reduction | Samsung
R4-2101828 | Discussions on FR2 Extreme temperature conditions | vivo
R4-2101829 | Discussions on Test Time Reduction for NR FR2 RF | vivo
R4-2102088 | Discussion on test time reduction methods | Rohde & Schwarz
R4-2102401 | Analysis on reducing test time | Huawei, HiSilicon
R4-2102617 | On extreme temperature condition testing | Keysight Technologies UK Ltd
R4-2102618 | On Test Time Enhancements based on different Antenna Array Assumptions | Keysight Technologies UK Ltd
R4-2102675 | FR2 testability in ETC | Qualcomm Incorporated
R4-2103952 | Email discussion summary for [98e][330] FR2_enhTestMethods | Moderator (Apple)