## Slide 1: 3GPP TSG-RAN WG4 Meeting #98-e Electronic Meeting, 25 Jan - 5 Feb, 2021
Huawei, HiSilicon
WF on UE PRS measurement requirements
R4-2104076

## Slide 2: Measurement period for RSTD (1)
FFS whether and how to account for muting in measurement period requirements
  Option 1a
    If muting option 1 is applied, the periodicity of a PRS resource is scaled by
    where is X * dl-prs-MutingBitRepetitionFactor, and X is the size of NR-MutingPattern-r16 for mutingOption1-r16
  Option 1b
    If muting option 1 is applied, the periodicity of a PRS resource is scaled by
    where is X * dl-prs-MutingBitRepetitionFactor, and X is the [maximum] number of consecutive zeros in NR-MutingPattern-r16 for mutingOption1-r16
  Option 2:
    Muting is accounted with same approach as in LTE (the current requirements apply when up to ½ of PRS resources can be muted)
  Option 3:
    Do not define requirements for the case of PRS resource muting in Rel-16

## Slide 3: Measurement period for RSTD (2)
Consideration on different resource periodicities
  Use the least common multiple of PRS periodicities among all PRS resources in the PFL
    FFS: only the PRS resources or resource sets configured which are fully or partly within the MGs should be considered
FFS: the need to decide on the order of steps to derive
  Order for steps to derive
    Option 1
      The applying order to scale the PRS periodicity should be
        A): The PRS periodicity indicated by “NR-DL-PRS-Periodicity-and-ResourceSetSlotOffset-r16”
        B): Scale the PRS periodicity based on inter-period muting pattern
        C): Derive the frequency layer specific periodicity () if multiple periodicities are configured in this layer
        D): Derive the available periodicity within MGs ()
        E): Derive the effective periodicity based on PRS processing time ()
    Other options are not precluded

## Slide 4: Measurement period for RSTD (3)
FFS Consideration on different resource offsets in measurement period
  Option 1
    RSTD measurement period of a single PRS frequency layer is extended by T ms if different PRS resources on the PRS frequency layer have different offsets after muting.
  Option 2
    redefine as = + (currently = + )
  Option 3
    No change is needed due to different offsets.
  Option 4
    Avoid PRS configuration with different resource offsets on the same PFL
    FFS if the following parameters are concerned
      dl-PRS-Periodicity-and-ResourceSetSlotOffset-r16
      dl-PRS-ResourceSlotOffset-r16

## Slide 5: Measurement period for RSTD (4)
Definition of parameter Lprs
  Refer to clause 5.1.6.5 of 38.214 for calculation of Lprs.
  The calculation of Lprs should be based on the type (type 1 or type 2) as UE used to report {N,T}
  Further clarify the description and notations of Lprs in 38.133 (e.g. account PRS resources within MGs; clarify period of time over which Lprs is counted)

## Slide 6: Measurement period for RSTD (5)
Measurement period of multiple PLFs – overlapping case
  Measurement period of multiple PRS layers is defined as summation of the measurement period in each frequency layer
  CSSF is only for the MG sharing between PRS and RRM layers. Count only a single PRS layer for a gap occasion in CSSF calculation for both PRS and RRM layers.
  FFS how to capture the equations in the specifications
    Option 1A:
      Note: is already defined in the specification
    Option 1B
      TRSTD, Total =
      Note: needs to be removed from the specification

## Slide 7: Measurement period for RSTD (6)
FFS Measurement period of multiple PLFs – non-overlapping case
  Option 1
    Requirement of non-overlapping case should be the same as for overlapping case, i.e. sum approach
  Option 2
    Measurement period for the non-overlapping case shall be
    TRSTD, Total = maxi (TRSTD,i), where
    the measurement period starts with the first MG and it is the same for all frequencies (agreement from RAN4#96-e). Hence, the time to the last sample across all frequencies will correctly determine TRSTD, Total, regardless of the order the frequencies are measured

## Slide 8: Measurement period for RSTD (7)
FFS Measurement period of when configured with PRS-RSRP
  Scenario #1: PRS-RSRP is configured for DL-TDOA but not other positioning methods
    Option 1
      RSTD measurement period is not impacted by PRS-RSRP measurement.
    Option 2
      UE behavior when RSTD is configured together with PRS-RSRP and the required PRS-RSRP measurement period is longer than that for RSTD (configured without RSTD): the RSTD measurement continues over the entire PRS-RSRP measurement period
  Scenario #2: PRS-RSRP is configured for another positioning method but not for DL-TDOA
    Option 1
      RSTD measurement period is not impacted by the PRS-RSRP measurement configured for the other positioning method
    Option 2
      RSTD measurement period is impacted by the PRS-RSRP measurement configured for the other positioning method
  Scenario #3: PRS-RSRP measurements are configured for another positioning method and for DL-TDOA (different PRS resources are used for DL-TDOA and the other method)
    Option 1
      RSTD measurement period is not impacted by the PRS-RSRP measurement configured for the other positioning method
    Option 2
      RSTD measurement period is impacted by the PRS-RSRP measurement configured for the other positioning methods
  Scenario #4: PRS-RSRP measurements are configured for another positioning method and for DL-TDOA (identical PRS resources are used for DL-TDOA and the other method)
    Option 1
      RSTD measurement period is not impacted by the PRS-RSRP measurement configured for the other positioning method
    Option 2
      RSTD measurement period is impacted by the PRS-RSRP measurement configured for the other positioning methods
  FFS: need to also consider same or different frequency layers

## Slide 9: Measurement period for RSTD (8)
FFS clarification of UE behaviour at HO
  Option 1
    Clarify in section 9.9.2.5 of TS 38.133 (clarification is in bold):
      If intra-frequency or inter-frequency handover occurs while RSTD measurements are being performed, then the UE shall continue and complete the on-going RSTD measurements.
  Option 2
    the RSTD measurement requirements when HO occurs during the measurement are already clearly specified in 38.133 clause 9.9.2.5

## Slide 10: Measurement period for PRS-RSRP (1)
Measurement period when configured with RSTD or UE Rx-Tx
  FFS Scenario #1: UE being configured to measure PRS-RSRP for DL-TDOA (or Multi-RTT)
    UE behavior:
      Option 1
        UE continues PRS-RSRP over the entire RSTD/UE Rx-Tx measurement period, when
          PRS-RSRP is configured together with RSTD/UE Rx-Tx, and
          the required PRS-RSRP measurement period is shorter than that for RSTD/UE Rx-Tx (without PRS-RSRP)
      Option 2
        UE does not continue PRS-RSRP measurement
    Applicable PRS-RSRP measurement period requirements
      Option 1:
        The minimum measurement period is extended to that for RSTD/UE Rx-Tx
      Option 2:
        The minimum measurement period is linked with the accuracy and thus does not need to be extended, but the UE shall continue measuring so the PRS-RSRP matches RSTD/UE Rx-Tx
      Option 3
        Current requirements in clause 9.9.3 also apply for the case when PRS-RSRP is measured for DL-TDOA or Multi-RTT, the UE stops PRS-RSRP measurement
  Scenario #2: UE being configured to measure PRS-RSRP for different positioning methods
    If PRS-RSRP measurement is separately configured for each positioning method, the requirements shall be met independently for each positioning method.

## Slide 11: Measurement period for UE Rx-Tx (1)
FFS Whether SRS periodicity should be accounted in measurement period
  Option 1
    No
  Option 2
    can be extended if the SRS periodicity is longer than max().
FFS Whether SRS dropping should be accounted in measurement period
  Option 1
    No
  Option 2
    UE is allowed to extend the UE Rx-Tx measurement period (clarified in the requirements), but the exact value is not specified (aligned with RAN4 agreement on PRS dropping)

## Slide 12: Measurement period for UE Rx-Tx (2)
FFS PRS/SRS proximity
  Option 1
    The measurement requirements for UE Rx-Tx timing difference is applicable only if the configured parameters SRS-Slot-offset and SRS-Periodicity for SRS resource for positioning are such that any SRS transmission is within [-X, +X] ms of at least one DL PRS resource of each of the TRPs in the assistance data
      X = 50
      X = 160
      X = 80
  Option 2
    The requirements for UE Rx-Tx apply provided MIN(Tsrs, Tprs) ≤ 2*X; X = FFS (e.g. X = 160 ms)
  Option 3
    The requirements for UE Rx-Tx apply provided MIN(Tsrs, Tprs) ≤ Y; Y = FFS (e.g. Y = 320 ms)

## Slide 13: Measurement period for UE Rx-Tx (3)
FFS Measurement period requirements with TA change
  TA change due to TA command
    UE behaviour:
      Option 1
        UE shall continue UE Rx-Tx time difference measurement and meet accuracy requirements
      Option 2
        The UE shall discard the UE Rx-Tx time difference measurement if the uplink transmission timing (based on network-configured TA) changes during the UE Rx-Tx measurement period
    Applicable measurement period requirements
      Option 1
        the UE Rx-Tx time difference measurement requirement are not applicable
  TA change due to UE autonomous adjustment
    UE behaviour:
      Option 1
        UE shall continue UE Rx-Tx time difference measurement and UE Rx-Tx time difference measurement requirements shall apply
      Option 2
        The UE shall discard the UE Rx-Tx time difference measurement if the uplink transmission timing (autonomous) changes during the UE Rx-Tx measurement period
  TA change due to NTA_offset change
    Option 1
      No need to clarify UE Rx-Tx measurement requirements in case of NTA_offset change and the current accuracy requirements apply
    Option 2
      No need to clarify UE Rx-Tx measurement requirements in case of NTA_offset change, provided the current accuracy requirements do not apply
    Option 3
      It is clarified in UE Rx-Tx measurement requirements (section 9.9.4 in TS 38.133) are not applicable if the NTA_offset changes during the measurement period

## Slide 14: Measurement period for UE Rx-Tx (4)
FFS Measurement period requirements with cell change
  cell change impacting SRS configuration
    Option 1
      No need to specify requirements for SRS reconfiguration.
    Option 2
      If the serving cell (PCell, PSCell, or SCell) configured with the SRS for positioning changes during the measurement period, UE Rx-Tx measurement requirements do not apply
        What is the UE behaviour in this case?
    Option 3
      If the serving cell (PCell, PSCell, or SCell) configured with the SRS for the measurement, changes during the measurement period, UE Rx-Tx time difference measurement is restarted, after the SRS reconfiguration on the target cell is complete.
        In this case, the UE shall restart the UE Rx-Tx time difference measurement after the SRS reconfiguration on the target cell is complete.
  cell change not impacting SRS configuration
    Option 1
      if the serving cell (PSCell or SCell) changes while not configured with the SRS for positioning, the UE shall continue the on-going UE Rx-Tx time difference measurement
        the current measurement period applies
        accuracy requirements in clause 10.1.25 apply
    Option 2
      if the serving cell (PSCell or SCell) changes while not configured with the SRS for positioning, the UE shall continue the on-going UE Rx-Tx time difference measurement
        the current measurement period is extended
        accuracy requirements in clause 10.1.25 apply

## Slide 15: CSSF (1)
FFS Whether a PLF is considered as candidate for a MG occasion when part but not all resources on that PFL are within the MGL of the MG occasion
  Option 1
    PFL is counted as candidate for a MG occasion if at least one PRS resource on that PFL is fully covered by the MGL excluding RF switching time.
  Option 2
    Yes, a PFL is counted as candidate for a MG occasion if a sufficient number of PRS symbols are contained within MGL excluding RF switching time
FFS for the sum-based approach, Selection of one PFL in CSSF calculation for PRS measurement period
  Option 1
    Only one PRS frequency layer with a short periodicity would compete for MG with other gap-based RRM measurements at a time
    Selection of the one PRS frequency layer for measurement is up to UE implementation
  Option 2
    For PFLs that do not satisfy the long periodicity condition, CSSF would be calculated by counting only one PFL at a time.
    For RRM frequency layers, N intermediate CSSF values would be calculated, when N is the number of PFLs and each intermediate CSSF value accounts for only one of the PFLs. FFS: The CSSF value for a RRM frequency layer could be the highest among the N intermediate CSSF values or chosen depending on with PFL is being processed at the time.
  Option 3
    CSSF should be defined on per MG occasion basis, i.e. a PRS frequency layer is counted as candidate for a MG occasion if at least one PRS resource occasion is fully covered by the MGL excluding RF switching time.
    Count only a single PLF for each MG occasion.
FFS For the sum-based approach, CSSF for RRM measurements on a carrier frequency with PRS measurements
  Option 1: Rel-15 approach

## Slide 16: CSSF (2)
FFS: Definition of long periodicity measurement
  Option 1
    Tavailable,i≥320ms .
  Option 2
    max(Tprs * X * dl-prs-MutingBitRepetitionFactor) >=320ms, where X is the length of NR-MutingPattern-r16 for mutingOption1-r16r
  Option 3
    where is the PRS resource set index within a PFL, , is the PRS resource periodicity and is the number of consecutive zeros in NR-MutingPattern-r16 for mutingOption1-r16
  Option 4
PRS periodicity (ms) | DL-PRS-MutingPattern configuration
>160 | With or without muting
160 | With muting

## Slide 17: Requirements applicability considering UE capability (1)
FFS: time span of PRS resource instance > N
  Option 1
    The measurement requirements do not apply for a PRS resource, if time span of the PRS resource instance is greater than UE reported capability N
  Option 2
    at least UE should be able to measure one PRS resource without repetition
  Option 3
    No clarification is needed
FFS: time span of PRS resource instance > MGL
  Option 1
    The measurement requirements do not apply for a PRS resource, if the time span of a DL PRS resource instance is greater than the configured measurement gap length
  Option 2
    When time span of PRS resource instance > MGL, the PRS within the useful part of MG can be assumed
  Option 3
    The requirements apply , provided a sufficient number of PRS symbols are available within MGL excluding the RF switching time. The PRS symbols beyond MGL are not considered for PRS measurements

## Slide 18: Requirements applicability considering UE capability (2)
FFS: time span of PRS resource instance being across two sampling duration of N within duration Lprs
  Option 1
    The measurement requirements do not apply for a PRS resource, if the PRS resource is across two sampling duration of N within duration Lprs
  Option 2
    UE may need to combine the PRS resource in the two sampling periods, or overlapped sampling window can be used if the issue exists
  Option 3
    No clarification is needed
General applicability due to UE processing and measurement limitations
  Option 1
    The measurement requirements do not apply to any instance of a PRS resource that cannot be measured and processed in its entirety due to limitations imposed by either the UE PRS processing capability {N, T} or the configured measurement gap pattern.
  Option 2
    No further clarification is needed

## Slide 19: Use of MG pattern #24 and #25 for LTE RRM measurement (1)
FFS whether MG pattern #25 is an applicable pattern for LTE measurements
  Option 1
    Remove MG pattern #25 as an applicable pattern for LTE measurement
  Option 2
    No change is needed to the current specification
FFS Measurement window when MG pattern #24 is used for LTE measurement
  Option 1
    When MG pattern #24 is used for LTE measurement, the measurement window is defined as the first 5ms after the RF re-tuning time
  Option 2
    no need to limit this to 5 ms

## Slide 20: Alignment of terminoly in specification
FFS which term should be used in the specification
  Option 1
    Positioning frequency layer
  Option 2
    PRS frequency layer
  Option 3
    Frequency layer (with NR PRS measurement)
  Other options not precluded
    Companies are also encouraged to check specifications of other WGs