## Slide 1: WF on temporary RS for efficient SCell activation in NR CA
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, 25 Jan -05 Feb, 2021
      R4-2104083
Document for: Approval

## Slide 2: Agreement
SCell being activated is known and belongs to FR1
  If SCell measurement cycle is equal to or smaller than 160ms
    temporary RS can be used for time/frequency tracking
      1 burst (2-slot with four CSI-RS resources) is required based on RAN1 working assumptions on temporary RS design provided in the LS R1-2009798.
  If SCell measurement cycle is larger than 160ms
    temporary RS can be used for AGC
      1 burst (2-slot with four CSI-RS resources) is required
    temporary RS can be used for time/frequency tracking
      1 separate burst (2-slot with four CSI-RS resources) is required in addition to the one burst required for AGC
    The agreements above apply based on RAN1 working assumptions on temporary RS design provided in the LS R1-2009798.
    FFS: whether minimum gap between the RS symbol(s) for AGC and the RS symbols for time/frequency acquisition is considered to account for UE AGC application time delay
      The minimum gap length is FFS

## Slide 3: Way Forward
SCell being activated is unknown and belongs to FR1
  FFS: whether temporary RS can be used for time/frequency tracking? Or under which condition it can be used ?
    When temporary TRS is configured?
    If it is feasible, how many temporary RS bursts are required?

## Slide 4: Way Forward
SCell being activated is unknown and belongs to FR1
  Whether temporary RS can be used for AGC? Or under which condition it can be used?
  Option 1:
    -if the power imbalance between the SCell and activated serving cells in the same band is less than a threshold, no AGC is required.
    - if the power imbalance between the SCell and activated serving cells in the same band is larger than a threshold,
      For intra-band continuous CA, UE can perform AGC adjustment based on temporary RS.
      For intra-band non-continuous CA, UE shall perform AGC adjustment based on SSB as the coarse timing is not obtained.
      For inter-band non-continuous CA, UE shall perform AGC adjustment based on SSB as the coarse timing is not obtained.
  Option 1b : At least for some cases temporary RS is allowed for AGC.
  Option 1c: UE might need to know the power level different between SSS and TRS/CRS.
  Option 2 : No. Don’t expect using temporary RS for unknown case.
  Option 3 ：
    - coarse AGC based on temporary RS FDM’ed with unknown data is not feasible
    - exhaustive cell search based on temporary RS is not feasible
    - fine AGC based on temporary RS can be feasible, however, the QCL association for the temporary RS should first be established.
  Option 4: After coarse timing acquisition based on SSB, it is feasible to use temporary RS for AGC
  Option 5 : UE is not supposed to be required to consider large imbalance between intra-band CA carriers
  If the answer to above is “Yes” or “Yes for partial cases”, how many temporary RS bursts are required?

## Slide 5: Way Forward
SCell being activated belongs to FR2
  If there is at least one active serving cell on that FR2 band and temporary RS is provided, temporary RS can be used for time/ frequency tracking
      Option 1: 1 burst (2-slot with four CSI-RSs resources) is required
      Option 2: 2 bursts are required
  If target SCell is known to UE and no active serving cell on that FR2 band, temporary RS can be used for fine timing tracking
      Option 1: 1 burst (2-slot with four CSI-RSs resources) is required
      Option 2: 2 bursts are required

## Slide 6: Way Forward
SCell being activated belongs to FR2
  If the SCell being activated is unknown and there is no active serving cell on that FR2 band,
    FFS: whether temporary RS can be used for AGC? Or under which condition it can be used?
      If it is feasible, how many temporary RS bursts are required?
    FFS: whether temporary RS can be used for time/ frequency tracking? Or under which condition it can be used?
      If it is feasible, how many temporary RS bursts are required?

## Slide 7: Way Forward
Answers to Q2 in LS [R1-2009798]
  Most companies think Q2 is for the case that the SCell being activated is known and belongs to FR1 and the SCell measurement cycle is larger than 160ms.
  Option 1: UE does not require to receive another RS transmitted also on the other activated serving cell in the same band.
  Option2: UE expects another RS and/or SSB (burst) is also transmitted on the other activated serving cell, having all the RSs time-aligned within MTRD requirement for intra-band CA.

## Slide 8: Way Forward
Answers to Q3 in LS [R1-2009798]
  RAN1 working assumption for temporary RS (i.e., reuse existing Rel-15/16 TRS structure) can provide reduction in maximum allowed activation delay at least for the cases as listed in page2 and page 5.
  Are there any suggested changes from RAN4 perspective?
    Need further discussion