## Slide 1: WF on test cases for IAB-MTs
ZTE Corporation
3GPP TSG-RAN WG4 #98-e
Electronic Meeting, Jan. 25-Feb. 5, 2021
R4-2104091

## Slide 2: Way Forward - Core Maintenance
Remove gap patterns for IAB-MTs completely from TS 38.174 RRM requirements.

## Slide 3: Way Forward - Test configurations
Test configurations for IAB-MTs shall take TS 38.133 Annex as baseline. IAB-MTs are to be tested under specific and simplified test configurations which are specified in TS 38.133 Annex.

## Slide 4: Way Forward - Test configurations
Tests can be done for any TDD configuration. TDD pattern and related configurations shall be configurable and left for implementation including
  DL/UL scheduling related configuration
  PRACH and SRS configuration
  SSB/CSI-RS configuration

## Slide 5: Way Forward - Test configurations
In IAB-MT RRM tests only one serving cell shall be considered. However, there can be more than one cell in some tests to account for a target cell e.g. RRC re-establishment and RRC release with redirection.

## Slide 6: Way Forward - Test configurations
In IAB-MT RRM test requirements are derived using the corresponding configuration parameters as example. The actual IAB-MT RRM test can be conducted by any set of configuration parameters and corresponding test requirements shall be based on the actual configuration parameters used in the test.

## Slide 7: Way Forward - Test configurations
AoA related configurations are based on declaration. Only indicate the number of AoAs in the test cases.
No test cases and configurations are defined with DRX, CA or DC.

## Slide 8: Way Forward - Test cases
As agreed in previous meeting that no conformance testing will be defined for IAB-MT, the corresponding reference to conformance tests shall be removed to avoid ambiguities when specifying requirements and test cases in TS 38.174.

## Slide 9: Way Forward - Test cases
Define performance test cases for LA IAB-MTs.
FFS whether to define performance test cases for WA IAB-MTs.

## Slide 10: Way Forward - Test cases
Following test cases are defined to verify RRC re-establishment requirements in clause 12.1.1.1, TS 38.174:
  TC1: Inter-frequency RRC Re-establishment in FR1 for LA IAB-MT and IAB type 1-H
  TC2: Intra-frequency RRC Re-establishment in FR1 without serving cell timing for LA IAB-MT and IAB type 1-H
  TC3: Inter-frequency RRC Re-establishment in FR2 for LA IAB-MT and IAB type 1-O
  TC4: Intra-frequency RRC Re-establishment in FR2 without serving cell timing for LA IAB-MT and IAB type 1-O

## Slide 11: Way Forward - Test cases
FFS whether to have separate test cases for timing advance for WA IAB-MT and/or LA IAB-MT.

## Slide 12: Work split
RRM Test cases | Related RRM Requirements | Applicability | Company
RRC Re-establishment in FR1 | 12.1.1.1 SA: RRC Re-establishment | 1-H LA | Ericsson
RRC Re-establishment in FR2 |  | 2-O LA | 
RRC Connection Release with Redirection to NR in FR1 | 12.1.1.3 SA: RRC Connection Release with Redirection to NR | 1-H LA | Huawei
RRC Connection Release with Redirection to NR in FR2 |  | 2-O LA | 
IAB-MT transmit timing in FR1 | 12.2.1 IAB-MT transmit timing | 1-H LA | ZTE
IAB-MT transmit timing in FR2 |  | 2-O LA | 
RLM OOS with SSB in FR1 | 12.3.1.2 Requirements for SSB based radio link monitoring | 1-H LA | Nokia
RLM OOS with SSB in FR2 |  | 2-O LA | 
RLM IS with SSB in FR1 |  | 1-H LA | 
RLM IS with SSB in FR2 |  | 2-O LA | 
RLM OOS with CSI-RS in FR1 | 12.3.1.3 Requirements for CSI-RS based radio link monitoring | 1-H LA | Ericsson
RLM OOS with CSI-RS in FR2 |  | 2-O LA | 
RLM IS with CSI-RS in FR1 |  | 1-H LA | 
RLM IS with CSI-RS in FR2 |  | 2-O LA | 
Beam Failure Detection and Link Recovery with SSB in FR1 | 12.3.2.2 Requirements for SSB based beam failure detection12.3.2.5 Requirements for SSB based candidate beam detection | 1-H LA | ZTE
Beam Failure Detection and Link Recovery with CSI-RS in FR1 | 12.3.2.3 Requirements for CSI-RS based beam failure detection12.3.2.6 Requirements for CSI-RS based candidate beam detection | 1-H LA | ZTE
Beam Failure Detection and Link Recovery with SSB in FR2 | 12.3.2.2 Requirements for SSB based beam failure detection12.3.2.5 Requirements for SSB based candidate beam detection | 2-O LA | Huawei
Beam Failure Detection and Link Recovery with CSI-RS in FR2 | 12.3.2.3 Requirements for CSI-RS based beam failure detection12.3.2.6 Requirements for CSI-RS based candidate beam detection | 2-O LA | Nokia