## Slide 1: WF on UL MIMO EVM
RAN4#99-e R4-210xxxx
e-Meeting, May 2021
Qualcomm Incorporated

## Slide 2: Background -1
Motivation:
  The FR1 UL-MIMO EVM requirement must accommodate any mapping between SRS ports (logical) and antenna connectors (physical)
  Current requirement presumes 1:1 mapping, rather than the general case
  To accommodate the general case, TE must be able to resolve measured UL signals into their constituent layers (‘diagonalization’), prior to EVM calculation
Two schemes to diagonalize the channel have been proposed. Both diagonalize by equalizing with inverse of channel estimate:
  Method 1: channel estimate based on DMRS symbols alone
  Method 2: channel estimate based on LSE channel estimate
This WF focuses on defining evaluation criteria to help down-select between the EVM calculation methods

## Slide 3: Background – 2 : Method 1
Equalizer is derived from DMRS symbols alone
See R4-2109914

## Slide 4: Background – 3 : Method 2
Equalizer is derived by inversion of LSE estimate of channel
Extension of legacy SISO method to rank 2
See R4-2108818

## Slide 5: WF – Simulation assumptions
Method other than method 1 and 2 is not precluded
Test waveforms constructed with:
  Flat signal PSD
  Injected AWGN
Signal configuration:
  [50] contiguous RBs
  CP-OFDM (QPSK – 64 QAM) PUSCH, rank 2
  UL RMC as defined in appendix of 38.101-1
AWGN noise sweep for SNR range of 10 dB to 30 dB over allocated RBs
UE implementations:
  Evaluate for following matrices that relate SRS logical ports to physical antenna connectors ->
  Others unitary matrices not precluded

## Slide 6: WF – Criteria for comparison of methods
Calculated EVM accuracy for different SNR cases due to AWGN
Calculated EVM repeatability for above cases over 10 sub-frames average per standard for PUSCH
Sensitivity of calculated EVM to DMRS configuration
Sensitivity of calculated EVM to frequency domain smoothing
Sensitivity of calculated EVM to scheduled number of PUSCH symbols
Handling of non-invertible matrix cases
The allowable EVM measurement error
Implementation challenges
Other criteria not precluded