## Slide 1: WF on FR2 RF requirement applicability under ETC
vivo
3GPP TSG-RAN WG4 Meeting #99-e R4-2107750
Electronic Meeting, May 19-27, 2021
Agenda item: 4.1.2
Document for: Approval

## Slide 2: Applicability of FR2 RF requirements
According to the Rel-15 TS38.101-2, the following two aspects can be concluded:
  At least, the following FR2 RF requirements in Rel-15 TS38.101-2 have been confirmed not applicable for ETC
    Power control
    EVM and EVM equalizer spectrum flatness
  In Rel-15 TS38.101-2, the following FR2 RF requirements shall not be verified under ETC
    EIRP spherical coverage
    Beam correspondence
    EIS spherical coverage