## Slide 1: WF on 60 GHz UE Tx requirements
Intel Corporation
3GPP TSG-RAN WG4#99-e Meeting R4-2107973
Electronic Meeting, May 19 – 27, 2021

## Slide 2: UE power class framework
Agreement: Power classes will be a package of four parameters
  Minimum peak EIRP
  EIRP spherical coverage
  Maximum TRP
  Maximum EIRP (regulatory defined, captured for reference)
FFS whether EIRP PSD limit needs to be included

## Slide 3: Tx Power classes for spec
Proposal 1: to adopt the maximum EIRP/TRP and PSD in ETSI EN 303 753 for UE power class definition in unlicensed operation;
Proposal 2: to start with maximum TRP/EIRP in the existing TS 38.101-2 PC3 for UE power class definition in licensed operation;
Proposal 3: For an unlicensed NR band adopt the power limits given in Table 2 as a baseline (R4-2110686)
Proposal 4: Further discuss which, if any, of the existing power classes in 38.101-2 can be reused for an unlicensed NR band or a new power class is needed. As basis for power class definition, it is beneficial to discuss what are representative antenna array sizes in this frequency range.
Proposal 5: Postpone discussing RF output limits for a licensed band until spectrum and regulations becomes available.
Agreement: Proposal 4

## Slide 4: UE types
Agreement
  Consider handheld, FWA and vehicular type of UE
  Other UE types are not precluded
  The discussion can happen in parallel

## Slide 5: Regulatory limits
Further discussion and review is needed
  Alignment on which values to include is encouraged
    Review content available in TR38.805 (FCC 47 CFR 15.255), and latest ETSI EN 302 567, ETSI EN 303 722, and ETSI EN 303 753
    Other relevant sources are not precluded
  Max EIRP
    Discuss whether to include peak EIRP, or avg/mean EIRP
  Max TRP
    Consider whether 23 dBm can continue to used
  Maximum spectral power density (EIRP)
    Review latest applicable limits (23 dBm/MHz, 13 dBm/MHz)
    Discuss whether this limit needs to be included
Companies are encouraged to share their views of current proposals, current regulatory limits and provide further inputs during the next RAN4 meeting

## Slide 6: Initial access power
Whether UE open loop power control can always be set to Pmax during the initial access
Proposals
  Option 1: Agree UE initial access power is set at Pmax (Apple, MediaTek)
  Option 2: This is RAN1 issue (Ericsson, Intel, Qualcomm, Nokia, MediaTek, LGE)
Discussions will continue in next RAN4 meeting
Notes: Apple: Option 1 and 2 can go in parallel. We can send LS to RAN1 to seek feedback.

## Slide 7: Agreement: Maximum UL modulation order
Higher order modulation would result in challenging RF requirement, i.e., ACLR, due to RF impairments in 60 GHz, and RAN4 needs to consider a reduced max UL modulation order compared to FR2
To decide the max UL modulation order, companies are encouraged to study the following:
  MPR analysis for different modulation schemes
  Link level performance comparison of achievable throughput for different modulation schemes for high SNR region
Optionality of 64 QAM is FFS, depending on the outcome of the above study

## Slide 8: References
R4-2107956, “Email discussion summary for [99-e][146] NR_ext_to_71GHz_Part_2,” Qualcomm (moderator), RAN4 #99-e, May 2021