## Slide 1: WF on simultaneous Rx/Tx for synchronous/asynchronous NR-DC
Apple
3GPP TSG-RAN WG4 Meeting #99-e
Electronic Meeting, May 19th – 28th, 2021
Agenda Item: 8.44.2
R4-2108007

## Slide 2: Background (1)
The first round discussion related to simultaneous Tx/Rx and synchronous/asynchronous NR CA and NR-DC configurations is captured at right
Issue 2-1-3: Whether need to clarify how the UE capability signaling on simultaneous Tx/Rx is related to synchronous and asynchronous NR CA and NR-DC configurations OPPO: Option 1 for the time being. Need to better understand the impact of asynchronous NW. Qualcomm: Option 2. This capability is related to the RF implementation of the UE, it has nothing to do with synchronicity of the network. Xiaomi: Option 2. In our view, the simultaneous Rx/Tx capability just indicates the UE capability which mainly depends on implementation, it is not related with network configuration i.e. synchronous operation or not ZTE: Option 2. Apple: Option 1. For example, with asynchronous inter-band NR-DC, the network cannot guarantee slot alignment, and MRTD is 500 us; but with synchronous inter-band NR-DC, the network can guarantee slot alignment with MRTD of 33 us. Thus, if a UE does not support simultaneous Tx/Rx in a certain inter-band NR-DC combination, then it cannot be configured for it in an asynchronous network. One way to accommodate this is to introduce certain limitations on possible network configurations as a function of UE capability and sync/async scenario. Huawei: Option 2.

## Slide 3: WF (1)
The UE capability signaling for simultaneous Rx/Tx is separate from synchronous and asynchronous NR CA/DC network deployment
  This UE capability only shows whether UE is capable of simultaneous Rx/Tx and depends on UE implementation
Handling of UEs that are not capable of simultaneous Rx/Tx is up to the network scheduler
  Whether RAN4 will introduce limitations on possible network configurations as a function of UE capability and sync/async scenario is FFS