## Slide 1: WF on [312] NTN_Solutions_Part1 (NTN general part)
Moderator, THALES

## Slide 2: Outline
Proposed way forward based on the outcomes of “Email discussion summary for [99-e][312] NTN_Solutions_Part1”
See R4-2108699 (revision of R4-2108437)

## Slide 3: Content
Topic #1: NTN Architecture Aspects
Topic #2: NTN Generic Parameters
Topic #3: FR1 Generalities
Topic #4: FR2 Generalities

## Slide 4: Summary
List of proposals for each topics discussed
In “agreements” part
  Proposals with “green” comments are agreeable.
In “open issues” part
  Proposals with “purple” comments not agreeable.
  Proposals with “orange” comments not agreeable:
    If there is a GTW session and we could agree on some of them, this WF will be revised anyway;
    Please also note that the “orange” proposals were the results of “agreed with changes” comments.
  Proposals without any comment were not discussed.

## Slide 5
Agreeable Proposals
(after the 1st and 2nd round of discussions in RAN4#99-e, please also note that NTN GTW slot on 25/05/2021 could not be used)

## Slide 6: Topic #1
Proposal 1-1-2-1: RAN4 shall consider for NTN framework similar testing procedures as in TS 38.141-like. Based on different combinations and following similar testing procedures as in e.g. TS 38.141-like, the throughput measurement point at the Non-NTN infrastructure gNB can be used to determine the 5% throughput loss.
  Note1: For the Non-NTN infrastructure gNB, please refer to RAN3 NTN architecture.
Proposal 1-3-2-1: Satellite companies and some other companies expressed strong concerns if (Satellite+Feederlink+GW) is considered as a Repeater, because it would reduce NTN capacity and in general would not align with real satellite payload design.

## Slide 7: Topic #1
Proposal 1-1-3-1: RAN4 confirms the baseline assumption that from RF Tx, Rx requirements (for conductive RF requirements) perspective, NTN-Payload RF, Feederlink, GW, Non-NTN infrastructure gNB shall be considered as single entity.
  Note: The detailed test set-up can be further discussed. Further confirmation still required for OTA based RF requirements if introduced.
Proposal 1-1-1-1: RAN4 should first consider conducted mode testing (e.g. 1-H) for NTN gNB. 1-O can be considered in a later stage. FFS for 1-C.
  Note1: (from satellite company) in AIT phase (i.e. during Assembly, Integration and Test), the NTN-Payload is usually tested in conducted mode, meaning that the (radiant) antenna elements are disconnected before connecting the test equipment. RAN4 could therefore start with 1-H, but there should (probably) not be any restriction for 1-O.
  Note2: For NTN gNB please refer to RAN3 NTN architecture.

## Slide 8: Topic #1 – NTN REFSENS Test
Proposal 1-1-4-1: Additional evidence should be provided before concluding that OTA based REFSENS test is feasible for (Satellite + feeder link + NTN-Gateway + Non-NTN infrastructure gNB) as a single entity.
  Note1: RAN4 confirms conducted mode REFSENS test for (Satellite + feeder link + NTN-Gateway + Non-NTN infrastructure gNB) as a single entity.
  Note2: For the Non-NTN infrastructure gNB, please refer to RAN3 NTN architecture.
  Note3: RAN4 to identify any additional evidence to be provided.

## Slide 9: Topic #1 – NTN Blocking Test
Proposal 1-1-5-1: Additional evidence should be provided before concluding that OTA based Blocking test is feasible for (Satellite + feeder link + NTN-Gateway + Non-NTN infrastructure gNB) as a single entity.
  Note1: RAN4 confirms conducted mode Blocking test for (Satellite + feeder link + NTN-Gateway + Non-NTN infrastructure gNB) as a single entity.
  Note2: For the Non-NTN infrastructure gNB, please refer to RAN3 NTN architecture.
  Note3: RAN4 to identify any additional evidence to be provided.

## Slide 10: Topic #1 – NTN Intermodulation Test
Proposal 1-1-6-1: Additional evidence should be provided before concluding that OTA based Intermodulation test is feasible for (Satellite + feeder link + NTN-Gateway + Non-NTN infrastructure gNB) as a single entity.
  Note1: RAN4 confirms conducted mode Intermodulation test for (Satellite + feeder link + NTN-Gateway + Non-NTN infrastructure gNB) as a single entity.
  Note2: For the Non-NTN infrastructure gNB, please refer to RAN3 NTN architecture.
  Note3: RAN4 to identify any additional evidence to be provided.

## Slide 11: Topic #1
Proposal 1-1-1-2: RAN4 should reconsider/adapt the reference measurement channels for NTN use case.
  Note: Details are FFS.
Proposal 1-3-1-1: It can be assumed that the linkage between NTN-Gateway and Non-NTN Infrastructure gNB functions is expected to be typically implemented with a non-RF connection.

## Slide 12: Topic #2
Proposal 2-1-2-1: The common definition for channel bandwidth, transmission bandwidth configuration, minimum guard band, and RB alignment in 38.104 and 38.101-1 can be reused for NTN system.
Proposal 2-1-3-1: The supported channel bandwidth per operating band should be defined based on NTN operator input.
Proposal 2-1-4-1: The channel spacing in 38.104 can be reused for NTN. Exact definition pending channel raster decision.
Proposal 2-2-1-1: UE NTN FR1 may use similar specification as TS 38.101-1 (with different clauses for NTN).

## Slide 13: Topic #2
Proposal 2-1-1-1: The first NTN band will have the following frequency range definition: 1980-2010 MHz in UL and 2170-2200 MHz in DL. Its band number is FFS.
  Note: Companies are encouraged to provide a NTN band numbering scheme for next RAN4 meeting.
Proposal 2-3-1-1: RAN4 to study and agree on the reference assumption to be used for the on-board satellite amplification process.
  Note: Clarifications required on what “reference assumption” means, and typical implementations for on-board satellite amplification processes.
Proposal 2-3-1-2: RAN4 to consider Constant Equivalent Isotropic Radiated Power (EIRP) and/or Constant Power at Receiver options for on-board satellite amplification process.

## Slide 14: Topic #3
Proposal 3-1-2-1: RAN4 shall consider the following bandwidth size configuration for MSS S-Band with SCS 15 kHz: 5, 10, 15, 20 MHz.
Proposal 3-1-3-1: RAN4 shall consider the following bandwidth size configuration for MSS S-Band with SCS 30 kHz and SCS 60 kHz: 10, 15, 20 MHz.
Proposal 3-1-3-2: The supported channel bandwidth per operating band should be defined based on NTN operator input.

## Slide 15: Topic #3
Proposal 3-1-5-1: RAN4 shall consider a 100 kHz MSS S-Band Channel Raster.
Proposal 3-1-6-1: With respect to MSS S-Band Synchronization Raster, one solution is to reuse current NR work frame for NTN system, but for applicable SS raster entries per operating band RAN4 may need to further study it.
Proposal 3-2-2-1: RAN4 shall consider a 100 kHz MSS L-Band Channel Raster.
Proposal 3-3-3-1: 3GPP should take the relevant FCC and ETSI regulation into account when defining Tx and Rx NTN requirements for the pairing of 1610 - 1618.725 MHz UL and 2483.5 – 2500 MHz DL.

## Slide 16: Topic #3
Proposal 3-1-1-1: RAN4 shall use S-Band Reference Operational Deployment Scenario using 1980-2010 MHz for UL and 2170-2200 MHz for DL.

## Slide 17: Topic #3
Proposal 3-1-8-1: RAN4 may consider S-band extension in a new WI on operator’s request, as it’s common practice for any TN band in RAN4.
Proposal 3-3-1-1: RAN4 may consider mixed pairing of (L-band) and (S-band) in a separate dedicated WI, as it’s common practice for any TN band in RAN4. The core functionality should be forward compatible with mixed pairing.
Proposal 3-3-2-1: RAN4 may consider pairing of 1610 - 1618.725 MHz UL (L-band) and 2483.5 – 2500 MHz DL (S-band) in a separate dedicated WI, as it’s common practice for any TN band in RAN4. The core functionality should be forward compatible with mixed pairing.

## Slide 18
Candidate Proposals
(as discussed during NTN GTW slot on 27/05/2021)

## Slide 19: Topic #4
Candidate Proposal 4-1-1-1: Should there be any NTN FR2 study (coexistence) phase before the introduction to specification/normative phase?
Candidate Proposal 4-2-1-1: If yes, NTN FR2 coexistence studies in Rel-17 should consider:
  RAN4 will use UL (27-30 GHz) frequency range of Ka band to do co-existence study in Rel-17 NR-NTN WI;
  Ka band (UL)/FR2 co-existence analysis can be started once the S band/FR1 co-existence analysis principles are stable enough; The actual started time need to be checked at August meeting.
  Other bands such as Ku & Q/V band will leverage the FR2 co-existence study approach in the future.
  Note: Huawei, Ericsson still have concern on above proposals.

## Slide 20: Topic #4
Candidate Proposal 4-2-2-1: Consider the uplink part of satellite “Ka band”, corresponding with the 27.0 – 30.0 GHz range, which includes both “FSS” and “MSS” denomination, since the provision of VSAT and ESIM services from GSO and NGSO is allowed in FSS as well as MSS denominated spectrum within said range, with different denomination depending on regional regulations, as regulated by ITU-R regulations and recently harmonized on a global basis by WRC Resolutions 156 [8], 169 [9] and 173 [10].
Candidate Proposal 4-3-1-1: It has been clarified throughout the SI and WI definition that NTN covers both VSAT and ESIMs/ESOMPs (which are a type of mobile VSATs operating in FSS spectrum). VSAT and ESIM operates in the entire Ka-band, hence, the frequency bands considered for 3GPP NTN RAN4 work should include spectrum relevant to VSAT and ESIM/ESOMP operation. RAN4 to consider defining the entire “Ka Band” as an NTN-NR band in FR2 range for GEO and NGSO based satellite access as proposed in RP-200638 [2].

## Slide 21: RAN-P decisions from RP-210791
Agreed Proposal NTN-1.1: “For frequencies above 10 GHz, any work can be limited to VSAT, ESIM service and terminals.”
Agreed Proposal NTN-1.2: “The Satellite Ka band refers to [17.3 – 20.2 GHz] on the downlink and [27.0 – 30.0 GHz] on the uplink as allocated by ITU-R to satellite services. Some of this range is designated as FSS and some as MSS.”