## Slide 1: WF on Repeater System Parameters
Qualcomm Incorporated
3GPP TSG-RAN WG4 Meeting # 99-e
Electronic Meeting, May 19-27, 2021
R4-2108226

## Slide 2: Multi-band Support in FR2
Do not specify multi-band requirements for FR2

## Slide 3: Requirements Related to Multiband Support
For multi-band operation of the NR repeaters, requirements for Inter RF Bandwidth gaps need to be considered from the perspective of ACLR/CACLR, OBUE, etc. Other requirements can be further identified in the RF requirements discussions.
For spurious emissions, multi-band exceptions/exclusions need to be specified for each supported operating band.

## Slide 4: Pass Band Definition
Pass band is defined as follows:
  Pass band: The frequency range in which the repeater operates in with operational configuration. This frequency range can correspond to one or several consecutive nominal channels. If they are not consecutive each subset of channels shall be considered as an individual pass band. A repeater can have one or several pass bands.

## Slide 5: Repeater Channel Bandwidth
Channel Bandwidth is not needed in the repeater specifications
  If a suitable way to use channel BW is found during the discussion of RF requirements, this agreement can be revisited.
Pass band will be used as a reference in the specifications for defining bandwidth dependent requirements
  If a suitable way to use the pass band as reference is not found, this agreement can be revisited
  FFS how exactly the pass band will be used as a reference

## Slide 6: Channel and Sync Raster
Channel and Sync raster is not needed in the repeater specifications
  UE/BS specifications can be referenced for repeaters that would employ the SSB for synchronization
  FFS how the UE/BS specifications would be referenced (e.g. if some Note in the repeater specifications is enough)

## Slide 7: Repeater Transmit Bandwidth
Transmit Bandwidth is not needed in the repeater specifications
Pass band will be as a reference in the specifications for defining requirements dependent on the transmit bandwidth
  If a suitable way to use the pass band as reference is not found, this agreement can be revisited
  FFS how exactly the pass band will be used as a reference

## Slide 8: Addition of New Bands
New Bands will be added in the repeater specifications at the same time with the BS/UE specifications
  Bands requiring new general requirements(e.g. new passband) will be handled separately
  FFS what the framework for such bands should be

## Slide 9: Channel Spacing
Channel Spacing is not needed in the repeater specifications