## Slide 1: Way Forward on core requirement maintenance of Direct SCell activation
Ericsson, ...
3GPP TSG-RAN WG4 Meeting #99-e
Electronic Meeting, May 19 – 27, 2021
R4-2108290
Document for: Approval

## Slide 2: Background
Companies provided contributions on core requirement maintenance to RAN4#99-e.
Agreements and open issues pertaining to those contributions are captured in this WF.
Further background can be found in R4-2108385 or revision thereof.

## Slide 3: Agreements in RAN4#99-e (1/4) Core requirement maintenance – Direct SCell activation
Agreement:
  Timeline for directly activated SCell configured with multiple TCI states:[Issue 1-1-1]
    Ndirect = TRRC_Process + T1 + Tactivation_time + TCSI_Reporting - 3ms, when TCI state is not indicated within Tactivation_time, and
    Ndirect = TRRC_Process + T1 + THARQ + Tactivation_time + TCSI_Reporting, otherwise
Agreement captured in CR R4-2108292 or revision thereof.

## Slide 4: Agreements in RAN4#99-e (2/4) Core requirement maintenance – Direct SCell activation
Agreement:
  Removal of bracket for SCell known condition in NR FR1:[Issue 1-2-1]
  Remove bracket around [5] seconds in SCell known condition requirement for Direct SCell Activation in NR FR1.
  Agreement captured in CR R4-2108293 or revision thereof.

## Slide 5: Agreements in RAN4#99-e (3/4) Core requirement maintenance – Direct SCell activation
Yet to be settled:
Measurement period threshold value for requirement branching in NR FR1:[Issue 1-3-1]
  Option 1: Increase the measurement period threshold for Direct SCell activation in FR1 from 1280ms to [5]s.
  Option 2a: Use threshold [2560ms]xCSSFinter for Direct SCell activation in FR1.
  Option 2b: Use the threshold [1280ms]×CSSFinter for Direct SCell activation in FR1.
  Option 3: Do not use a threshold in the Direct SCell activation delay requirement. Always assume the longer activation procedure (TFirstSSB_MAX + Trs + 5ms) is needed.
  Option 4: Keep agreement in RAN4#98-bis-e unchanged, i.e. use [1280ms] for Direct SCell activation in FR1
  continued on next slide

## Slide 6: Agreements in RAN4#99-e (4/4) Core requirement maintenance – Direct SCell activation
continued from previous slide
  Option 5 (added during 2nd round GTW session):
    Case 1: Activation delay for an SCell which was a deactivated SCell prior to e.g. HO and now target for the direct SCell activation.
      Reuse requirements in 8.3.2
    Case 2: Other cells (i.e. cells which were not deactivated SCell prior to being target SCell in the direct activation)
      If the SCell is known and belongs to FR1, TCSI_Reporting is specified in clause 8.3.2 and Tactivation_time is defined as:
        TFirstSSB+ 5ms, if the measurement period is equal to or smaller than [1280]ms.
        TFirstSSB_MAX + Trs + 5ms, if measurement period is larger than [1280]ms.

## Slide 7: For RAN4#100-e
  Interested companies are asked to provide contributions on remaining open issues