## Slide 1
3GPP TSG-RAN WG4 Meeting #99-e R4-2108341
Electronic Meeting, May. 19-27, 2021
Agenda Item: 9.7.2
WF on RRM for FR1 HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-2103678 WF on RRM for NR HST, RAN4#98-e
  R4-2105793 WF on RRM for NR HST, RAN4#98-e-bis

## Slide 3: Agreement
  Inter-frequency measurement without MG, connected state
    For PSS/SSS detection for inter-frequency measurement without measurement gaps in connected state, the enhancement on PSS/SSS detection delay requirements specified for intra-frequency measurement in R16 HST can be reused, i.e. M2 is reused:
DRX cycle | TPSS/SSS_sync_inter
No DRX | max( 600ms, ceil( 5 x Kp) x SMTC period )Note 1 x CSSFinter
DRX cycle≤ 320ms | max( 600ms, ceil(M2x 5 x Kp) x max(SMTC period, DRX cycle)) x CSSFinter
DRX cycle>320ms | ceil(5 x Kp) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified NOTE 2: When [high speed] is not configured, M2 = 1.5. When [high speed] is configured, M2 = 1.5 if SMTC periodicity > 40 ms, otherwise M2=1. | 

## Slide 4: Agreement
  Inter-frequency measurement without MG, connected state
    For index detection for inter-frequency measurement without measurement gaps in connected state, the enhancement on index detection delay requirements specified for intra-frequency measurement in R16 HST can be reused, i.e. M2 is reused:
DRX cycle | TSSB_time_index_inter
No DRX | max(120ms, ceil( 3 x Kp ) x SMTC period)Note 1 x CSSFinter
DRX cycle≤ 320ms | max(120ms, ceil (M2 x 3 x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
DRX cycle>320ms | Ceil(3 x Kp) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified NOTE 2: When [high speed] is not configured, M2 = 1.5. When [high speed] is configured, M2 = 1.5 if SMTC periodicity > 40 ms, otherwise M2=1. | 

## Slide 5: Agreement
  Inter-frequency measurement without MG, connected state
    For measurement delay for inter-frequency measurement without measurement gaps in connected state, the enhancement on measurement delay requirements specified for intra-frequency measurement in R16 HST can be reused, i.e. M2 and Y are reused:
DRX cycle | T SSB_measurement_period_inter
No DRX | max(200ms, ceil( 5 x Kp) x SMTC period)Note 1 x CSSFinter
DRX cycle≤ 160ms | max(200ms, ceil(M2 Note 2 x 5 x Kp) x max(SMTC period,DRX cycle)) x CSSFinter
160ms < DRX cycle≤ 320ms | ceil(4 x M2 Note 2 x Kp) x max(SMTC period,DRX cycle)
DRX cycle>320ms | ceil(Y Note 3 x Kp ) x DRX cycle x CSSFinter
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified NOTE 2: When [high speed] is configured, M2 = 1.5 if SMTC periodicity > 40 ms, otherwise M2=1 NOTE 3: When [high speed] is configured, Y= 3 when SMTC <= 40ms, Y= 5 when SMTC > 40ms | 

## Slide 6: Agreement
  Inter-frequency measurement with MG, connected state
    PSS/SSS detection time requirement for inter-frequency measurement with MG in connected state for HST
      Option 1 (QC, Apple, CMCC):
Condition NOTE1,2 | TPSS/SSS_sync_inter
No DRX | Max(600ms, 6  Max(MGRP, SMTC period))  CSSFinter
DRX cycle ≤ 320ms | Max(600ms, Ceil(6*M2 Note 3)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
DRX cycle > 320ms | 6  DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: When high speed is not configured, M2 = 1.5; When high speed is configured, M2 = 1.5 if SMTC periodicity > 40 ms;,otherwise M2=1 | 
      Option 2 (CATT, vivo, Xiaomi, MTK, HW, Ericsson, Apple)：
Condition NOTE1,2 | TPSS/SSS_sync_inter
No DRX | Max(600ms, 8  Max(MGRP, SMTC period))  CSSFinter
DRX cycle ≤ 320ms | Max(600ms, Ceil(8*M2)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
DRX cycle > 320ms | 8  DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: When high speed is not configured, M2 = 1.5. When high speed is configured, M2 = 1.5 if SMTC periodicity > 40 ms, otherwise M2=1. | 
      Option 3 (Nokia)：
Condition NOTE1,2 | TPSS/SSS_sync_inter
No DRX | Max(600ms, N Note 4  Max(MGRP, SMTC period))  CSSFinter
DRX cycle ≤ 320ms | Max(600ms, Ceil(N Note 4* M2 Note 3)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
DRX cycle > 320ms | N Note 4  DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: When highSpeedMeasFlag-r16 is not configured, M2 = 1.5; When highSpeedMeasFlag-r16 is configured, M2 = 1.5 if SMTC periodicity > 40 ms;,otherwise M2=1. NOTE 4: When highSpeedMeasFlag-r16 is not configured, N = 8; otherwise N = 5. | 

## Slide 7: Agreement
  Inter-frequency measurement with MG, connected state
    For index detection for inter-frequency measurement with measurement gaps in connected state, M2 is reused:
Condition NOTE1,2 | TSSB_time_index_inter
No DRX | Max(120ms, 3  Max(MGRP, SMTC period))  CSSFinter
DRX cycle ≤ 320ms | Max(120ms, Ceil(3  M2)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
DRX cycle > 320ms | 3  DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: When [high speed] is not configured, M2 = 1.5. When [high speed] is configured, M2 = 1.5 if SMTC periodicity > 40 ms, otherwise M2=1. | 

## Slide 8: Agreement
  Inter-frequency measurement with MG, connected state
    Measurement delay requirement for inter-frequency measurement with MG in HST in connected state for HST
      Option 1 (QC):
      Option 2 (HW, OPPO):
        -7 samples for 160ms < DRX cycle≤ 320ms
        -6 samples for DRX cycle>320ms and SMTC <= 40ms
      Option 3 (CATT):
Condition NOTE1,2 | T SSB_measurement_period_inter
No DRX | Max(200ms, 6  Max(MGRP, SMTC period))  CSSFinter
DRX cycle≤ 160ms | max(200ms, ceil(6 x M2 Note 3) x max(SMTC period,DRX cycle)) x CSSFintra
160ms < DRX cycle≤ 320ms | ceil(5 x M2 Note 3 x Kp) x max(SMTC period,DRX cycle)
DRX cycle>320ms | ceil( Y Note 4 x Kp ) x DRX cycle x CSSFintra
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: M2 = 1.5 if SMTC periodicity > 40 ms, otherwise M2=1 NOTE 4: Y=3 when SMTC <= 40ms, Y=5 when SMTC > 40ms | 
Condition NOTE1,2 | T SSB_measurement_period_inter
No DRX | Max(200ms, 8  Max(MGRP, SMTC period))  CSSFinter
DRX cycle ≤ 160ms | Max(200ms, Ceil(8  M2)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
160ms < DRX cycle≤ 320ms | Max(200ms, Ceil(7  M2)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
DRX cycle > 320ms | 8  DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: When high speed is not configured, M2 = 1.5. When high speed is configured, M2 = 1.5 if SMTC periodicity > 40 ms, otherwise M2=1. | 

## Slide 9: Agreement
  Cont. from last slide:
      Option 4 (CMCC):
      Option 5 (vivo, Xiaomi, OPPO): For inter-frequency measurement with MG, the enhanced requirements specified for LTE-NR inter-RAT measurements in R16 HST could be used as baseline
      Option 6 (Apple, Ericsson):
Condition NOTE1,2 | T SSB_measurement_period_inter
No DRX | Max(200ms, 8  Max(MGRP, SMTC period))  CSSFinter
DRX cycle≤ 160ms | Max(200ms, Ceil(8  M2 Note 3)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
160ms <DRX cycle ≤ 320ms | Max(200ms, Ceil([4]  M2 Note 3)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
DRX cycle > 320ms | Y Note 4  DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: M2 = 1.5 if SMTC periodicity > 40 ms, otherwise M2=1 NOTE 4: Y1= [3] when SMTC <= 40ms, Y1= [8] when SMTC > 40ms | 
Condition NOTE1,2 | T SSB_measurement_period_inter
No DRX | Max(200ms, [6]  Max(MGRP, SMTC period))  CSSFinter
DRX cycle ≤ 320ms | Max(200ms, Ceil([6]  M2NOTE 3)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
DRX cycle > 320ms | [6]  DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: When [highSpeedMeasFlag-r17] is not configured, M2 = 1.5; When [highSpeedMeasFlag-r17] is configured, M2 = 1.5 if SMTC periodicity > 40 ms;,otherwise M2=1. | 

## Slide 10: Agreement
  Cont. from last slide:
      Option 7 (MTK, Ericsson, Xiaomi):
      Option 8 (Nokia):
Condition NOTE1,2 | T SSB_measurement_period_inter
No DRX | Max(200ms, 8  Max(MGRP, SMTC period))  CSSFinter
DRX cycle ≤ 320ms | Max(200ms, Ceil(8  M2 Note 3)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
DRX cycle > 320ms | 4  M2 Note 3 DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: When RRM enhancement for high speed is not configured, M2 = 1.5; When RRM enhancement for high speed is configured, M2 = 1.5 if SMTC periodicity > 40 ms;,otherwise M2=1. | 
Condition NOTE1,2 | T SSB_measurement_period_inter
No DRX | Max(200ms, 5  Max(MGRP, SMTC period))  CSSFinter
DRX cycle≤ 160ms | Max(200ms, Ceil(5  M2 Note 3)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter
160 ms ≤DRX cycle ≤ 320ms | 4  M2 Note 3 DRX cycle  CSSFinter
DRX cycle > 320ms | Y Note 4  DRX cycle  CSSFinter
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: M2 = 1.5 if SMTC periodicity > 40 ms; otherwise M2=1 NOTE 4: Y=3 when SMTC <= 40ms, Y=5 when SMTC > 40ms | 

## Slide 11: Agreement
  Inter-frequency measurement in idle state
    Whether define the enhancement for inter-frequency measurement in idle mode for HST
      Option 1 (HW, OPPO, QC, Ericsson, Xiaomi, CATT, CMCC, vivo): Yes
      Option 2 (MTK, Nokia): No
      Option 3 (Apple): introduce a dedicated UE capability indicating the support of inter-frequency measurement in idle mode for HST

## Slide 12: Agreement
  Inter-frequency measurement in idle state
    if it is agreed to enhance the inter-frequency measurement requirements in idle mode, how to perform the enhancement
      Option 1 (HW, QC, CATT, CMCC, Ericsson): using the same requirement as for intra-frequency measurement for HST
DRX cycle length [s] | Tdetect,NR_Inter [s] (number of DRX cycles) | Tmeasure,NR_Inter [s] (number of DRX cycles) | Tevaluate,NR_Inter [s] (number of DRX cycles)
0.32 | 2.56 x M2 (8 x M2) | 0.32 x M3 (1 x M3) | 0.96 x M4 (3 x M4)
0.64 | 5.12 (8) | 0.64 (1) | 1.92 (3)
1.28 | 8.96 (7) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)
Note 1: when SMTC < = 40 ms, M2 = M3 = M4 = 1; and when SMTC > 40 ms, M2 = 1.5, M3 = M4 = 2 |  |  | 
      Option 2 (OPPO, Xiaomi, MTK, vivo): The R16 enhanced EUTRA-NR inter-RAT measurement requirements in idle mode could be reused for NR inter-frequency measurements
DRX cycle length [s] | Tdetect,NR_Inter [s] (number of DRX cycles) | Tmeasure,NR_Inter [s] (number of DRX cycles) | Tevaluate,NR_Inter [s] (number of DRX cycles)
0.32 | 4.16 x M2 (13 x M2)Note 1 | 0.64 x M3 (2 x M3)Note 1 | 0.96 x M4 (3 x M4) Note 1
0.64 | 7.68 (12)) | 1.28 (2) | 1.92 (3)
1.28 | 12.8(10) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)
Note 1: M2=1.5, M3=2 and M4=2 if SMTC periodicity of measured intra-frequency cell > 40 ms; otherwise M2=M2=M3=1. |  |  | 

## Slide 13: Agreement
  Principle on the requirements if there are HST inter-frequency layers and non-HST inter-frequency layers to be measured
    Option 1 (HW, QC, Ericsson, Apple, CATT, vivo): If RAN4 decided to specify inter-frequency measurement enhancement in FR1 HST, the requirements shall follow the principle:
    NHST_inter-f carrier * THST_interf + NnonHST_inter-f carrier * TnonHST_interf
    Option 2 (OPPO, MTK, Nokia): FFS

## Slide 14: Agreement
  NSCC_SSB for CSSFoutside_gap,i
    Option 1(Nokia, Xiaomi, CMCC, vivo, QC, Ericsson, Apple): NSCC_SSB clarification/correction should cover non-HST as well as HST, i.e. unified NSCC_SSB design for both HST and non-HST
    Option 2 (CMCC, MTK): for high speed train scenario, it is proposed to clarify that only SCell(s) measured without MG are counted in NSCC_SSB for the calculation of CSSFoutside_gap,i
    Option 3 (HW): keep NSCC_SSB as it is in the spec
  Kp for the requirements on deactivated SCell
    FFS whether Rel-16 Kp requirements modifications (if any) shall also apply for R17 HST

## Slide 15: Agreement
  L1-SINR
    FFS whether L1-SINR measurement is applicable to HST
    If L1-SINR measurement is applicable to HST, whether it is necessary to specify upper bound of side condition for L1-SINR measurement
      Option 1 (CMCC, vivo): legacy L1-SINR accuracy requirements can be reused for high speed train scenario, no restriction is needed
      Option 2 (MTK, Ericsson): If RAN4 confirm the L1-SINR measurement will be applied for HST, then the upper bound of the side condition SSB Ês/Iot ≤5 dB should be introduced, for CMR only case at least
      Option 3 (Nokia): L1-SINR for CMR only does not seem to face the same side condition problem as SS-SINR

## Slide 16: Agreement
  Scell link recovery
    Option 1 (CATT, CMCC, vivo, Nokia): For SCell link recovery, it depends on network. There is no need to have the limitation on the number of band(s)in the spec
    Option 2 (MTK): For SCell link recovery, RAN4 needs to study how many band(s) is supported in R17 HST in FR1
    Option 3 (OPPO, HW, Nokia, vivo): The same limitation on the number of band(s) on which UE is performing beam failure detection for SCell in R16 can be reused in R17 HST

## Slide 17: Agreement
  CSSF
    Option 1(HW, OPPO, QC, CATT, CMCC, Ericsson, Nokia, vivo): For CSSF, it depends on network. There is no need to have the limitation on the number of Scell (s) in the spec
    Option 2 (MTK): For CSSF, RAN4 needs to study how many SCell(s) is supported in R17 HST in FR1

## Slide 18: Agreement
  Signaling
    FFS whether highSpeedMeasFlag-r16 can be reused for the indication of application of enhanced RRM requirements for HST CA
      Option 1 (CMCC, HW, OPPO, MTK, Nokia, Ericsson, CATT, vivo): Yes, the highSpeedMeasFlag-r16 can be reused for the indication of application of enhanced RRM requirements for HST CA
      Other option is not precluded
    FFS whether NW shall indicate which inter-frequency layers need to be measured more often, for which enhanced inter-frequency measurement requirements shall apply
      Option 1 (Apple, vivo): NW shall indicate which inter-frequency layers need to be measured more often, for which enhanced inter-frequency measurement requirements shall apply
      Other option is not precluded

## Slide 19: Agreement
  Release independent
    Option 1 (CATT, CMCC, Ericsson): Rel-17 NR HST RRM enhancement can be release independent from Rel-15
    Option 2 (vivo, OPPO, Ericsson, vivo): The release independent issue is not discussed until the features discussed in R17 FR1 HST becomes stable