## Slide 1: WF on FR2 HST RRM requirements
3GPP TSG-RAN WG4 Meeting #99-e
Electronic Meeting, 19 – 27 May 2021
Agenda: 9.8.4
R4-2108342
Document for: Approval
Nokia, Nokia Shanghai Bell

## Slide 2: Background
The Rel-17 NR HST FR2 Enhancements WI is presented in WID RP-202118.
The Work plan of the WI, including RRM core and perfromance part can be found in R4-2016920.
R4-2105794 WF on FR2 HST RRM requirements has been approved at the previous meeting RAN4#98-bis-e.
Corresponding Email summaries in RAN4#99-e:
  R4-2108147 Email discussion summary for [99-e][223]NR_HST_FR2_RRM, first round.
  R4-2108395 Email discussion summary for [99-e][223]NR_HST_FR2_RRM, second round.

## Slide 3: Maximum supported speed
Use 350kmph as a reference maximum train speed and define RRM requirements to guarantee that.

## Slide 4: HST FR2 network deployment flag
Add a flag to enable the UE to identify different/enhanced RRM requirements in HST FR2 deployment.
Add HST FR2 network deployment flag to the combined LS to RAN2 on all HST FR2 signalling flags.

## Slide 5: NW signalling and CPE capabilities for HST FR2 deployments
Continue the discussion after the deployment options and presence of non-CPE UEs is clarified:
  UE identification of support for HST FR2 deployment:
    Option 1: Flag is not needed.
    Option 1a: Only roof-mounted CPE is considered that should always have a capability to work in HST FR2 scenario in this WI.
    Option 2: UE capability is needed
  NW signalling of Uni- and/or Bi-directional deployment:
    Option 1: Network can indicate which high-speed scenario it is.
    Option 2: Such a flag is not needed.
  CPE indication of support of uni-/bi-directional operation
    Option 1: CPE indication of support of different deployment types is not needed.
    Option 2: Different capabilities are needed if different requirements are agreed.

## Slide 6: Decreasing RX beam number
FFS the feasible number of RX beams from RRM perspective
  deployment scenario study is used as reference

## Slide 7: Network assistance for reducing RX beam number
FFS: to be discussed depending on the outcomes of the deployment scenarios

## Slide 8: Beam search scaling factor N
FFS: to be discussed depending on the outcomes of the deployment scenarios and when the number of RX beams is determined

## Slide 9: Non-overlapping SSB locations in time domain among adjacent RRHs
FFS: how non-overlapping SSB locations in time domain among adjacent RRHs, one belongs to serving and one belongs to the neighboring cell in FR2 HST will impact core requirement and test cases.
  Option 1: The FR2 HST neighboring cell search/measurement requirement is applicable when SSB locations in time domain among adjacent RRHs, one belongs to serving and one belongs to the neighboring cell, are not overlapping.
  Other options are not precuded

## Slide 10: Requirements for long DRX configurations in CONNECTED state
Option 1: Apply existing R16 requirements
Option 2: Apply requirements for short DRX configurations
Option 3:
  FFS the upper bound of DRX cycle which is determined based on the maximum target CPE speed.
  Enhancements are defined for small DRX cycle ≤ the upper bound; for DRX cycle > the upper bound, existing Rel-16 FR2 requirements are reused

## Slide 11: Connected state mobility requirements
Connection Mobility Control
  RRC Release with Redirection
    Not applicable to FR2 HST
  RRC re-establishment
    FFS: Definition of criteria of known cell for FR2
    FFS: Enhancement of requirements on Connection Mobility Control - RRC re-establishment.
Handover
  FFS: A need for enhancements based on the agreements about RX beam sweep number reduction.

## Slide 12: Timing requirements
Autonomous timing adjust step Tq for FR2 in high-speed scenario is [4.5]Ts
FFS possible solutions and RRM impacts of large propagation delay difference:
  Solution 1: One-time large TA adjustment
  Solution 2: NW-based pre-compensation of different propagation delays
  Solution 3(a): Only use bi-directional with Scheme-1, i.e., don’t use uni-directional; and don’t use bi-directional with Scheme-2/3.
  Solution 3(b): Bi-directional deployment with interruption allowed by following Scheme-2 but no dedicated beam for coverage hole from neighboring RRH.
  Solution 4: Uni-directional deployment with interruption allowed.
  Other solutions are not precluded
  FFS: Impact on SSB-based measurement accuracy (e.g., SS-RSRP)

## Slide 13: Signalling requirements
RLM/BFD:
  FFS: including RLM evaluation period for Qout and Qin especially regarding the scaling factor N=8 and the factor P for HST in FR2
Link recovery:
  FFS: analyse and evaluate beam failure and candidate beam detection evaluation period for Qout especially regarding the scaling factor N=8 and the factor P for FR2 HST scenario

## Slide 14: TCI state switching delay
Revise TCI known conditions for HST scenario
FFS the TCI state switching delay requirements considering the following aspects :
  delay requirement for unknown TCI state condition
  the impact of one additional L1-RSRP measurement period due to unknown TCI state condition
  the problem of large difference in propagation delays
  re-using of existing TCI switching delay in known case

## Slide 15: TCI state switching enhancement
FFS whether the following enhancement for TCI state switching are needed
  Option 1: UE can initiate TCI state switch if it selects a candidate DL RS from the candidate set associated with the current TCI state
  Other options are not precluded

## Slide 16: Cell identification requirements
PSS/SSS detection
  FFS whether reusing the Rel-16 FR1 HST scaling factor M2 for FR2 HST is acceptable.
  FFS reduction of Mpss/sss_sync_w/o_gaps, which is proportional to the number of samples (S) and of receiver sweeping beams (N)
Intra-frequency measurements
  FFS whether reusing the Rel-16 FR1 HST scaling factor M2 for FR2 HST is acceptable.
  FFS reduction of Mmeas_period_w/o_gaps, which is proportional to the number of samples (S) and of receiver sweeping beams (N)

## Slide 17: Restriction on SMTC periodicity in measurement requirements
FFS: the upper bound of SMTC periodicity, with [40] ms as a basis
FFS: impact on the specification if upper bound of SMTC periodicity is agreed.

## Slide 18: L1-RSRP measurement enhancements
FFS the values of K and N

## Slide 19: Cell reselection enhancements in IDLE/INACTIVE mode
Cell reselection requirements in IDLE/INACTIVE mode are enhanced
FFS enhancement details
  upper bound of DRX cycle
  scaling factor N1
  others are not precluded

## Slide 20: Criterion for the RRM requirements definition
RAN4 to study whether to define metric of applicability of the RRM requirements in FR2 HST. This metric can be defined as:
  Option 1: Maximum performance degradation allowed (Max serving DL SNR degradation below threshold) Can be used at least for L1 measurements, intra-frequency cell identification, handover.
  Other options are not precluded

## Slide 21: Summary of Applicability of Rel-15/16 Requirements to Rel-17 HST FR2
RRM Req. Category | Sub-Category | Whether or not applicable to FR2 HST
Idle/inactive state mobility | Cell selection/re-selection, measurement | FFS, Enhance
Connected state mobility | Handover | FFS
 | Connection Mobility Control - RRC re-establishment | FFS
 | Connection Mobility Control - Random Access | No impact identified
 | Connection Mobility Control - RRC Release with Redirection | Not applicable to FR2 HST
Timing | Autonomous timing adjustment | Enhance
 | TX timing, timer, TA, Cell Phase Sync accuracy, deriveSSB-IndexFromCell tolerance | FFS
 | MRTD/MTTD | No impact identified
Signalling | RLM | FFS
 | Interruption | No impact identified
 | SCell Activation and Deactivation Delay | Not applicable to FR2 HST
 | UE UL carrier RRC reconfiguration delay | Not applicable to FR2 HST
 | Link Recovery | FFS
 | Active BWP switch delay | No impact identified
 | Active TCI state switching delay | FFS
 | PSCell Change | Not applicable to FR2 HST
 | Uplink spatial relation switch delay | FFS
 | UE-specific CBW change | No impact identified
 | Pathloss reference signal switching delay | No impact identified
Measurement Procedure | General measurement requirement | No impact identified
 | NR intra-frequency measurements | FFS, Enhance
 | NR inter-frequency measurements | Not applicable to FR2 HST
 | Inter-RAT measurement | Not applicable to FR2 HST
 | L1-RSRP/L1-SINR Measurement | FFS
 | CSI-RS based L3 measurements | Deprioritize
 | NR measurements with autonomous gaps | Not applicable to FR2 HST
Requirements’ classification categories:
  Not applicable to FR2 HST: the requirement is not applicable to Rel-17 FR2 HST UE
  No impact identified: no change on Rel-15/16 requirement is needed, and the same requirement applies to Rel-17 FR2 HST UE.
  FFS: need to discuss whether or not the requirement is applicable to Rel-17 FR2 HST UE and/or whether or not Rel-15/16 requirement needs to be changed/enhanced
  Deprioritize: can be discussed and studied further but with low priority.
  Enhance: it was agreed to enhance the requirements
FFS how to capture “Not applicable to FR2 HST” in the specification

## Slide 22: Contributions list in RAN4#99-e
T-doc No. | Title | Company
R4-2109064 | General discussion on RRM for NR FR2 HST | CATT
R4-2109065 | Discussion on number of RX beams for NR FR2 HST | CATT
R4-2109066 | Discussion on RRM requirements impacts for NR FR2 HST | CATT
R4-2109365 | Discussion on FR2 HST RRM requirement - geneal | Apple
R4-2109366 | Discussion on number of Rx beam for FR2 HST | Apple
R4-2109367 | Discussion on RRM requirement for FR2 HST | Apple
R4-2109509 | Discussion on RRM requirements for FR2 HST | CMCC
R4-2109572 | On NR FR2 HST RRM Requirements | Qualcomm, Inc.
R4-2110221 | General RRM requirements for HST FR2 | Ericsson
R4-2110222 | RX beam number for HST FR2 | Ericsson
R4-2110223 | RRM requirements impacted for HST FR2 | Ericsson
R4-2110238 | Further discussion on RRM requirements for FR2 HST | Samsung
R4-2110378 | General aspects of RRM requirements for HST in FR2 | Huawei, HiSilicon
R4-2110379 | Discussion on RRM requirements for high speed train scenario in FR2 | Huawei, HiSilicon
R4-2110954 | Discussion on the number of RX beams for FR2 HST | Intel Corporation
R4-2110955 | Discussion on the RRM requirements impact of FR2 HST | Intel Corporation
R4-2111168 | Further simulation analysis for HST in FR2 | Nokia, Nokia Shanghai Bell
R4-2111171 | Discussion on RRM requirements for FR2 HST | Nokia, Nokia Shanghai Bell