## Slide 1: WF on R17 NR MG enhancements - Multiple concurrent and independent MG patterns
Mediatek Inc.
3GPP TSG-RAN WG4 #99-e Meeting
Electronic Meeting, May 19-27, 2021
R4-2108346

## Slide 2: Definition
No consensus on keeping ‘common period of time’ in the definition of concurrent gap in this meeting.
Refinement of concurrent gap definition
  Concurrent gaps are multiple measurement gaps configured by RRC message(s)
    Either by same or separate RRC messages
    Whether and how to introduce new IE(s) or duplicate the existing IE is left to RAN2.
    Note: if existing IE is to be used, the configuration mechanism shall allow NW to use the same IE to either configure additional concurrent MGP or update the configured MGP.

## Slide 3: Applicability and configurations
Introduce the association between measurement gap and dedicated use case(s).
  FFS how to handle the case when the association is not provided.
Inform RAN2 that the measurement gap can be associated to one or multiple use cases in the following, while the detail on how to implement the association is left to RAN2
  One or more MO(s) for same or different RATs
  SSB and/or CSI-RS in each associated NR MO
  PRS
FFS whether to allow concurrent gap for the case with only non-NR RAT measurement objectives

## Slide 4: UE capability related issues
Max number of supported concurrent gap:
  When UE doesn’t support per-FR gap,
    Assume max 2 MGs as a starting point, when defining the requirements (e,g., overlapping, overhead cap, interruption, …)
    Larger number can be considered if RAN4 has extra time in Rel-17.
    UE capability can be discussed later and independently.
  When UE supports per-FR gap,
    Agreement:
      Allow network to fall back to use per-UE gap
    FFS whether to allow simultaneous configuring per-UE gap and per-FR gap
    Assume max 2 MGs in an FR as a starting point, when defining the requirements (e,g., overlapping, overhead cap, interruption, …)
    FFS the max number of supported concurrent gaps across all FRs, e.g.,
      Only per-FR gaps are configured
      per-UE gap and per-FR gap are configured simultaneous, if agreed

## Slide 5: UE capability related issues
Agreement:
  No separate UE capability is needed for the gap patterns supported for concurrent gap
    Revisit it in the future based on the conclusion in overhead cap discussion, if needed

## Slide 6: Overlapping issues
FFS whether to define requirements for Fully-overlapped (FO)
  Option 1: Yes, with gap sharing rules
  Option 1a : Yes, with priority rule
  Option 2: No
  Option 3: No in 1st phase
FFS whether to define requirements for Fully-partial overlapped (FPO)
  Option 1: Yes, with gap sharing rules
  Option 1a : Yes, with priority rule
  Option 2: No
  Option 3: No in 1st phase

## Slide 7: Overlapping issues
FFS whether to define requirements for Partially-fully overlapped (PFO)
  Option 1: Yes, with priority or sharing rule
  Option 2: No
  Option 3: No in 1st phase
FFS whether to define requirements for Partially-partial overlapped (PPO):
  Option 1: Yes, with priority or sharing rule
  Option 2: No
  Option 3: No in 1st phase
FFS whether to define gap cancel rules for fully non-overlapped (FNO) considering the following scenarios
  URLLC scenario
  HARQ feedback (k1, k2)
  FFS other option (e.g. min distance)

## Slide 8: Overlapping issues
If at least one of the FO, FPO, PFO and PPO cases is agreed further discuss based on the general assumption:
  UE is required to measure only in one MG in occasions where the two MG s are overlapped
    For per-FR gap case, different FR will be considered separately.
  FFS the rule for colliding gap occasions
    Option 1: Gap sharing
      A factor for gap sharing percentage, e.g., given 50% gap sharing, the measurement w.r.t. one gap will share roughly 50% of the time, while the other gap share the remaining
    Option 2: Priority
      UE will only do the measurement w.r.t. the gap with higher priority all the time
    Option 3: other option is not precluded
  FFS the data will be scheduled on the dropped gap occasions.

## Slide 9: Overhead issues
Whether to define an overhead cap for concurrent gap
  Option 1: Yes
    FFS the detail rule
  Option 2: No

## Slide 10: Measurement gap related requirements
The legacy requirements that can be re-used for concurrent gaps. including:
  MG patterns (or sequence),
  MG applicability,
  MG reference timing (including MGTA),
  effective MGRP(data scheduling opportunity depends on MG configuration), e.g.,
    A per-FR gap capable UE without FR2 serving cells but configured with FR2 MOs
    A per-FR gap capable UE without FR2 MOs but still configured with FR2 gap(s),
  UE UL behaviour after MG
FFS whether to re-use legacy gap interruption requirement.

## Slide 11: Measurement requirements
FFS whether to apply the following principles in defining measurement requirements
  Principle 2: Each reference signal can only be measured in one MG pattern.
  Principle 3: For a particular gap, only MOs share this gap should be counted in
  Principle 4: Legacy rules for measurement objective and gap (e.g., in Rel-15) should be reused for concurrent gap
  Principle 5: The UE measurement requirements, during the common period of time, are the same whether the measurement gaps are added or removed using concurrent measurement gap feature or pre-configured measurement gap feature.
  Principle 6: Adding a concurrent measurement gap does not affect an ongoing cell detection or measurement negatively
  Principle 7: The measurement delay requirement in case of multiple gaps shall be revisited
  Principle 8: Existing CSSF rules applies also when UE is configured with concurrent MGPs.
  Principle 9: Ensure the positioning-based measurement is fully supported using multiple concurrent measurement gaps.
  Other principles are not precluded.