## Slide 1: WF on NR SL enhancements RRM requirements
LG Electronics
3GPP TSG-RAN WG4 #99e
Electronic Meeting, May. 19-27, 2021
R4-2108352

## Slide 2
Issue 2-1 : Impact due to new operating scenario
2-1-1 : Impact on UE transmit timing requirements due to new operating scenario
  Study the impact on UE transmit timing requirements due to new operating scenario
    For intra-band con-current V2X operating bands in licensed band when NR Cell is configured as synchronization reference source
      whether to reuse NTAoffset = 0 or not
      whether to reuse Tx timing error requirement(Te) or not
2-1-2 : Impact on scheduling availability requirements due to new operating scenario
  After conclusion in RF session on switching period length and switching location for TDM based intra-band con-current sidelink operation, study whether to introduce scheduling availability or not when UE is switching between SL and Uu
2-1-3 : Impact on RRM performance requirements due to new operating scenario
  Treat issue 2-1-3 in RRM performance part after RRM core requirement
2-1-4 : Impact on RRM requirements for FDM based intra-band con-current SL operation
  Further discuss based on the conclusion in RF session

## Slide 3
Issue 2-2 : Impact due to SL-DRX
2-2-1 : Impact on initiation/cease of SLSS transmissions due to SL-DRX
  Study initiation/cease of SLSS transmissions with SL-DRX
    when SyncRef UE is synchronization reference source
    when NR cell is synchronization reference source
    when E-UTRAN cell is synchronization reference source
2-2-2 : Impact on selection/reselection of V2X Synchronization Reference Source due to SL-DRX
  Study the impacts on selection/reselection of V2X sync reference source due to SL-DRX including SyncRef UE identification time and PSBCH-RSRP measurement period
2-2-3 : Impact on interruption due to SL-DRX
  Study whether there is any impact on WAN due to SL-DRX
2-2-4 : Impact on L1 SL-RSRP measurements due to SL-DRX
  No impact
2-2-5 : Impact on Congestion control measurements due to SL-DRX
  No impact

## Slide 4
Issue 2-3 : Impact due to resource allocation enhancement
2-3-1 : Impact on L1 SL-RSRP measurements due to resource allocation related to power consumption reduction
  After RAN1’s conclusion, study the impact
2-3-2 : Impact on L1 SL-RSRP measurements due to resource allocation related to inter-UE coordination
  After RAN1’s conclusion, study the impact
2-3-3 : How to design a test for partial sensing
  Treat issue 2-3-3 in RRM performance part after completion of RRM core requirement
2-3-4 : How to design a test for inter-UE coordination
  Treat issue 2-3-4 in RRM performance part after completion of RRM core requirement

## Slide 5
Issue 2-4 : Impact due to Different Service Types
2-4-1 : Impact on structure of specification
  First identify the requirement that are impacted, and based on that RAN4 can discuss the specification structure
2-4-2 : Baseline of SL RRM requirements
  Consider Rel-16 NR V2X RRM requirements as baseline