## Slide 1: 3GPP TSG-RAN WG4 Meeting #99-e R4-2108633 Electronic Meeting, May. 19 – 27, 2021
CATT…
WF on Link level simulation assumptions

## Slide 2: Summary of link simulation assumptions
Parameter | Value
Carrier frequency | 2 GHz
CBW | 40MHz
SCS | 15kHz
Allocated RBs | Full allocation
Propagation | TDL-A 10ns delay spread, Maximum Doppler frequency: 5Hz (used as Baseline) TDL-D 10ns delay spread, Maximum Doppler frequency: 5Hz
MCS | 256QAM: MCS 24 in TS 38.214 Table 5.1.3.1-2: MCS index table 2 for PDSCH, and other MCSs are not precluded 1024QAM: MCS 24 in the following Table according to the agreement in RAN1 #104, and other MCSs are not precluded
Precoding | Precoding configuration defined in 38.101-4 Section 7.2 for fading channels; follow PMI
Symbol type | CP-OFDM

## Slide 3: Summary of link simulation assumptions
Parameter | Value
Number of HARQ transmission | 8 HARQ processes, maximum 4 transmissions
RV sequence | {0,2,3,1}
RANK | One and Two
BS antenna configuration | Take 1 and 2 Tx antenna as baseline. Companies also welcome to bring 8TX results if they demonstrate differing trends
UE antenna configuration | 4
Antenna correlation (Tx and Rx) | Low correlation
Channel estimation | Practical
Receiver type | MMSE-IRC
PDSCH configuration | Type A mapping, Start symbol 1, Duration 13 (for D slots)
DMRS configuration | DMRS type : Type 1, Single symbol, additional DM-RS (dmrsAdditionalPosition): pos1
txEVM | 0.5%, 1%, 1.5%, 2%, 3%.
rxEVM | 

## Slide 4: Related contributions
R4-2108692, Email discussion summary for [99-e][311] NR_DL1024QAM_BSRF, Moderator (Ericsson)
R4-2109111, Link level simulation results for 1024QAM for NR FR1, CATT, RAN4#99-e
R4-2110141, 1024QAM simulation assumptions and preliminary results, Nokia, Nokia Shanghai Bell, RAN4#99-e
R4-2110606, Initial simulation results for NR 1024QAM, ZTE Corporation, RAN4#99-e
R4-2110663, Link simulation for support of 1024QAM, Huawei, HiSilicon, RAN4#99-e
R4-2110482, Link Simulation Results for BS EVM, Ericsson, RAN4#99-e