## Slide 1
3GPP TSG-RAN WG4 Meeting #99-e R4-2108635
Electronic Meeting, May. 19-27, 2020
Agenda Item: 9.7.3
WF on UE demodulation for FR1 HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-2103876 WF on UE demodulation for FR1 HST, RAN4#98-e
  R4-2106098 WF on UE demodulation for FR1 HST, RAN4#98-bis-e

## Slide 3: PDSCH requirements for CA scenarios
  SCS configuration and applicability rules for SCS configuration
 | Number of CA Duplex modes | Number of required tests if UE supports all duplex modes
Option 1 | 3 (FDD 15+FDD15, FDD 15+TDD 30, TDD 30+TDD 30) | 2 (FDD 15 + TDD 30; TDD 30 + TDD 30)
Option 3 | 3 (FDD 15+FDD15, FDD 15+TDD 30, TDD 30+TDD 30) | 3 (FDD 15 + FDD 15; FDD 15 + TDD 30; TDD 30 + TDD 30)
Option 4 | 5 (FDD 15 + FDD 15; FDD 15 + TDD 15; FDD 15 + TDD 30; TDD 30 + TDD 30, TDD 15+TDD 15) | 2 (FDD 15 + TDD 30; TDD 30 + TDD 30) TDD 15 is tested if FDD 15+TDD 30 is not supported

## Slide 4: PDSCH requirements for CA scenarios
  Applicability rule for HST-SFN joint transmission scheme and DPS transmission scheme
    Option 1: If UE supports demodulationEnhancement-r16, only HST-SFN JT requirements shall apply, otherwise HST-DPS requirements shall apply for CA.
    Option 2: Define applicability rule that UE has passed DPS CA requirements can skip SFN CA requirements
    Option 3: Define two UE capabilities for HST-DPS CA and HST-SFN CA, UE perform the test only when UE supports it. if UE supports both, test one scheme:
      If UE has passed HST-DPS CA tests, HST-SFN CA tests can be skipped
      If UE has passed HST-SFN CA tests, HST-DPS CA tests can be skipped

## Slide 5: PDSCH requirements for CA scenarios
  HST-DPS channel model
    Extend the visibility for SSB and CSI-RS for HST-DPS to -Ds to Ds.
    Update the Doppler shift equation and Doppler shift trajectory to include 2nd nearest RRH for HST-DPS channel model (ref. to R4-2108557).

## Slide 6: PDSCH requirements for CA scenarios
  FFS applicability rule between single carrier and CA
  FFS whether HST PDSCH CA requirements can be release independent from Rel-15

## Slide 7: PDSCH requirements for CA scenarios
  Simulation
    Since huge performance gap for HST-SFN is observed, companies are suggested to check the summary on simulation results and come back in the next meeting if necessary

## Slide 8: Enhanced transmission schemes
  Do not define requirements for multi-DCI based transmission scheme in HST-SFN scenario