## Slide 1: Way Forward on general and PDSCH demodulation requirements for inter-cell interference MMSE-IRC
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #99-e
E-meeting, 19 – 27 May 2021
Agenda Item: 9.11.2.1
R4-2108664

## Slide 2: Common test parameters
Background: RAN4 meeting #98-bis-e agreements
  Physical cell ID of 0 for the serving cell, and cell ID i for interferer i (where i ≥ 1, maximum number of i is FFS)
  SCS: FDD 15kHz, TDD 30kHz (Same SCS is used for the target and the interference cells)
  TDD DL/UL configuration for 30kHz SCS: 7D1S2U(S=6D+4G+4U)
  Number of carriers: In Rel-17, MMSE-IRC receiver performance requirements with interference cell condition is defined only for single carrier scenario
  PDCCH and PDSCH allocation in time domain
    Use symbols #0 and #1 of each slot for PDCCH
    PDSCH mapping type A, Start symbol 2, Duration 12
  PDSCH allocation in frequency domain: Full PRB
  DMRS configuration
    For both serving and interfering cells, DMRS Type 1 with single symbol front loaded and 1 additional DMRS, with FDM applied between DMRS and data (number of CDM groups without data is equal to 1), i.e., overlapped DMRS between target and interferer
  Antenna configuration
    2 Tx as baseline for serving cell and interfering cells
    UE with 2 and 4 RX
    ULA low correlation as baseline

## Slide 3: Common test parameters
Network type
  Synchronized for FDD and TDD
  FFS asynchronized for FDD
Channel bandwidth
  Use 10MHz for FDD 15kHz and 40MHz for TDD 30kHz for initial simulation purpose
  FFS whether to consider 40 MHz for FDD 15kHz and 100 MHz for TDD 30kHz for requirements definition
  SSB configuration
  Option 1: All SSBs (serving cell and interference cell(s)) are in the same time/frequency resources
  Option 2: Serving cell SSB and interference cell(s) SSB(s) are in the different time/frequency resources
  TRS/CSI-RS configuration
  TRS/CSI-RS colliding with TRS/CSI-RS interference
  Propagation condition
  Consider TDLA30-10 and TDLC300-100 channel models for evaluation purpose and select only one for requirements definition

## Slide 4: Target PDSCH parameters for scenario 1
Background: RAN4 meeting #98-bis-e agreements
  Transmission rank: Use rank 1 as baseline
  PRB bundle size: Set PRB bundle size as 2 for target PDSCH
  HARQ process number: 4 for FDD 15kHz SCS and 8 for TDD 30kHz SCS as baseline
  RAN4 meeting #99-e agreements
  MCS
    Use MCS 4 (QPSK, CR=0.3) and MCS 13 (16QAM, CR=0.5) for initial simulation purpose
    Further discuss MCS for requirements definition
    Consider MCS corresponding to QPSK and 16QAM modulation formats
  Precoding model
    Random precoder with Type I SP codebook
  Performance measurement point
    Option 1: SINR at 70% TP
    Option 2: SNR at 70% TP

## Slide 5: Interference model for scenario 1
Background: RAN4 meeting #98-bis-e agreements
  Transmission rank of interfering PDSCH
    Use the following assumptions initial simulation purpose: random rank with 70% and 30% probability for rank 1 and rank 2 transmission in the interfering cell(s)
  Precoding of interfering PDSCH
    Random precoding with single panel type I codebook per slot and per PRB bundling granularity, with PRB bundling size of 2.
  Modulation order of interfering PDSCH
    Use 16QAM randomly modulated symbols for initial simulation assumption and other options not precluded.

## Slide 6: Interference model for scenario 1
Deployment for initial simulations
  Consider Homogeneous deployment assumptions
  FFS whether for consider HetNet deployment assumptions
DIP values for Homogeneous deployment assumptions for initial simulations
  Consider DIP1/2 = -1.73/-8.66 dB (INR1/2 = 5.43/-1.50 dB in case of 2 interference cells and INR 3.1 dB in case of 1 interference cell) as baseline for initial link level analysis for Synchronous network
  Results for other interference profiles are welcome
  Other options are not precluded for requirements definition
  FFS assumptions for asynchronous network
  INR values for HetNet deployment assumptions for initial simulations (in case HetNet is agreed)
  Option 1: INRs 11.39 and 5.45 dB (DIPs -1.23 and -7.16 dB)
  Other options are not precluded

## Slide 7: Interference model for scenario 1
  Number of explicitly modeled interference cells
  Companies are encouraged to check performance with 1 and 2 interference cells for initial simulations
  Further discuss the assumptions for requirements definition
Analysis of NR interference profile
  System level analysis from interested companies is not precluded
Methodology for interference profile configuration
  Option 1: Use the DIP methodology
  Option 2: Use the INR methodology

## Slide 8: Release independence
RAN4 discuss whether the UE demodulation with inter-cell interference is released independent from Rel-15 or not, after RAN4 agree with the detailed simulation assumption