## Slide 1: Impact on TS 38.101 due to the introduction of BCS2 for DC_(n)71AA T-Mobile USA, Skyworks
3GPP TSG-RAN WG4 #99-e
Online, , 19th May 2021 - 27th May 2021
R4-2111487

## Slide 2: Background
E-UTRA – NR configuration / Bandwidth combination set |  |  |  |  |  | 
Downlink EN-DC configuration | Uplink EN-DC configurations | Component carriers in order of increasing carrier frequency |  |  | Maximum aggregated bandwidth (MHz) | Bandwidth combination set
 |  | Channel bandwidths for E-UTRA carrier (MHz) | Channel bandwidths for NR carrier (MHz) | Channel bandwidths for E-UTRA carrier (MHz) |  | 
DC_(n)71AA | DC_(n)71AA3 | 15 | 5 |  | 20 | 0
 |  | 10 | 5, 10 |  |  | 
 |  | 5 | 5, 10, 15 |  |  | 
 |  |  | 5 | 15 |  | 
 |  |  | 5, 10 | 10 |  | 
 |  |  | 5, 10, 15 | 5 |  | 
 |  | 5 | 5,10,15,20 |  | 253 | 1
 |  | 10 | 5,10,15 |  |  | 
 |  | 15 | 5,10 |  |  | 
 |  |  | 5,10,15,20 | 5 |  | 
 |  |  | 5,10,15 | 10 |  | 
 |  |  | 5,10 | 15 |  | 
 |  | 5 | 5,10,15,20 |  | 35 | 2
 |  | 10 | 10,15,20 |  |  | 
 |  | 15 | 15,20 |  |  | 
 |  |  | 5,10,15,20 | 5 |  | 
 |  |  | 10,15,20 | 10 |  | 
 |  |  | 15,20 | 15 |  | 
DC_(n)71AA is a peculiar REL-15 combination for which:
  Dual UL transmissions are mandatory for DPS capable UEs,
  Single switched Uplink is allowed for non DPS capable UEs
  For BCS 0 and BCS 1:
    n71 UL CBW is restricted to 15MHz
    the maximum UL aggregated CBW is restricted to 20MHz
At RAN4 #98, a text proposal has been agreed to introduced a new BCS to support a maximum UL aggregated BW of 30MHz for DC_71A_n71A
RAN4 has also agreed to introduce asymmetric UL 20MHz / DL 35MHz for standalone n71 REFSENS.
A request to study the introduction of BCS 2 (in blue) is presented where:
  The uplink n71 is extended to 20MHz,
  LTE UL CBW  NR UL CBW,
  The maximum DL aggregated BW is 35MHz,
  The intention is to use n71 UL 20MHz only in DC with an LTE band other than B71, ie DC_2A-(n)71AA. No intention to use dual UL in DC_(n)71AA.
This draft document summarizes a proposed option to handle this request while minimizing its impact on the technical specifications

## Slide 3
E-UTRA – NR configuration / Bandwidth combination set |  |  |  |  |  | 
Downlink EN-DC configuration | Uplink EN-DC configurations | Component carriers in order of increasing carrier frequency |  |  | Maximum aggregated bandwidth (MHz) | Bandwidth combination set
 |  | Channel bandwidths for E-UTRA carrier (MHz) | Channel bandwidths for NR carrier (MHz) | Channel bandwidths for E-UTRA carrier (MHz) |  | 
DC_(n)71AA | DC_(n)71AA3,6 | 15 | 5 |  | 20 | 0
 |  | 10 | 5, 10 |  |  | 
 |  | 5 | 5, 10, 15 |  |  | 
 |  |  | 5 | 15 |  | 
 |  |  | 5, 10 | 10 |  | 
 |  |  | 5, 10, 15 | 5 |  | 
 |  | 5 | 5,10,15,20 |  | 253 | 1
 |  | 10 | 5,10,15 |  |  | 
 |  | 15 | 5,10 |  |  | 
 |  |  | 5,10,15,20 | 5 |  | 
 |  |  | 5,10,15 | 10 |  | 
 |  |  | 5,10 | 15 |  | 
 | - | 5 | 5,10,15,20 |  | 356 | 2
 |  | 10 | 10,15,20 |  |  | 
 |  | 15 | 15,20 |  |  | 
 |  |  | 5,10,15,20 | 5 |  | 
 |  |  | 10,15,20 | 10 |  | 
 |  |  | 15,20 | 15 |  | 
NOTE 1: Void NOTE 2: Void NOTE 3: For maximum DL aggregated bandwidth of 25 and MHz, the asymmetric UL and DL channel bandwidth combination of Table 5.3.6-1 in TS 38.101-1 [2] is used with a maximum UL contiguous aggregated bandwidth of 20 MHz. Furthermore, a restriction is imposed on bandwidth combinations so that only a subset of BCS1 is allowed to be used on the uplink, and this subset is equivalent to BCS0. NOTE4: Only single switched UL is supported. NOTE5: The minimum requirements only apply for non-simultaneous Tx/Rx between all carriers. NOTE6: Bandwidth Combination Set 2 only applies to intra-band EN-DC paired with another E-UTRA band without both bands of the intra-band combination in the uplink. |  |  |  |  |  | 
Impact on: “Table 5.3B.1.2-1: EN-DC configurations and bandwidth combination sets defined for intra-band contiguous EN-DC”
NOTE 3: Optional editorial corrections
New NOTE 6: reflects the new downlink only intra-band EN-DC wording in 38.306.

## Slide 4
Impact on: “Table 5.5B.2-1: Intra-band contiguous EN-DC configurations”
DC_(n)71AA2 | DC_(n)71AA | No4
NOTE 1: Uplink EN-DC configurations are the configurations supported by the present release of specifications. NOTE 2: Requirements in this specification apply for NR SCS of 15 kHz only. NOTE 3: Single UL allowed due to potential emission issues, not self-interference. NOTE 4: For UE(s) supporting dynamic power sharing it is mandatory to do dual simultaneous UL. For UE(s) not supporting dynamic power sharing single UL is allowed. Uplink DC_(n)71AA not applicable to BCS2. NOTE 5: The minimum requirements only apply for non-simultaneous Tx/Rx between all carriers. NOTE 6: Only single switched UL is supported |  | 
Note 4: Clarify that Single Uplink Allowed attributes are not applicable to BCS2.

## Slide 5
Impact on: Table 7.3B.2.1-1: Reference sensitivity (MSD) for intra-band contiguous EN-DC
No need to specify dual UL MSD test points since only n71 UL is specified
Only single UL MSD test points need to be studied,
For the special case of UL n71 =20MHz: this is not supported by BCS2, only supported in higher order combinations, example DC_2A-(n)71AA where:
  UL configuration = DC_2A_n71A, max 40MHz agg. BW
    E-UTRA B2 = 20MHz max
    NR n71 = 20 MHz max
  DL configuration = CA_2A-71A_n71A, max 55MHz agg. BW
    E-UTRA B2 = 20MHz max
    E-UTRA B71 = 15 MHz max
    NR n71 = 20MHz max
Single Uplink MSD use-cases / Aggressor - Victim |  |  |  |  |  | 
Downlink EN-DC configuration | Uplink EN-DC configurations | Component carriers in order of increasing carrier frequency |  |  |  | 
 |  | Aggressor | Victim |  | Maximum UL aggregated bandwidth (MHz) | Maximum DL aggregated bandwidth (MHz)
DC_(n)71AA | DC_(n)71AAX | NR 20 | LTE 5,10,15 | NR 20 | 20X | 35
 | DC_(n)71AAXX | NR 15 | LTE 5,10,15 | NR 15 | 15 | 20,25,30
 |  | NR 10 | LTE 5,10,15 | NR 10 | 10 | 15,20,25
 |  | NR 5 | LTE 5,10,15 | NR 5 | 5 | 10,15,20
 |  | LTE 15 | NR 5,10,15,20 | LTE 15 | 15 | 20,25,30,35
 |  | LTE 10 | NR 5,10,15,20 | LTE 10 | 10 | 15,20,25,30
 |  | LTE 5 | NR 5,10,15,20 | LTE 5 | 5 | 10,15,20,25
NOTE X: Only applicable to BCS2. NOTE XX: Applicable to BCS0, BCS1, BCS2. |  |  |  |  |  | 
It is proposed to capture the single UL REFSENS test points for BCS0,1 and BCS2 in Table 7.3B.2.1-1 with
  A footnote “x” to specify the test points that are only applicable to BCS2
  A separate footnote to specify the test points that are applicable to BCS 0,1 if such points are needed.

## Slide 6: Impact Summary
Option |  | Impact to 38.101-3 and 38.101-1 TS |  |  |  | 
 |  | 38.101-3 Table 5.3B.1.2-1 "BCS" table | 38.101-3 Table 5.5B.2-1 "SUO" table | 38.101-3 Table 7.3B.2.1-1: "MSD" table | 38.101-1 Table 5.3.6-1 "Asymmetric UL/DL" table | 38.101-1 DC_(n)71AA A-MPR specifications
1 | BCS2 only used with LTE Pcell in another | New Footnote 6 adds text aligned with the new downlink only intra-band EN-DC wording in 38.306. | Note 4 states that SUO attributes are not applicable to BCS2 | Single UL REFSENS test points needed1 | No Impact | No impact
NOTE 1: Impact of UL n71 20MHz on LTE B71 MSD can be captured in the DC_(n)71AA single UL MSD table with footnote “X”. |  |  |  |  |  | 
Pro & cons of the approach
No impact on legacy UEs – no change to legacy specifications
Aligned with the intended deployment configuration and removes ambiguity about n71 20MHz UL usage,

## Slide 7: Proposal
Proposal 1: Adopt the specification changes described above for DC_(n)71AA BCS2