## Slide 1: Tentative A-MPR tables for band 26
R4-B26ah-0049
Nokia Corporation
19.1.2012

## Slide 2: Way forward on co-existence with Narrow Band Systems in the 806-824 MHz range
-42 dBm/6.25 kHz for 806–813.5 MHz protection with 0.75 MHz offset for 1.4, 3 and 5 MHz channel BW
-42 dBm/6.25 kHz for 806–816 MHz protection with 3 MHz offset for 3 and 5 MHz channel BW
-42 dBm/6.25 kHz for 806–816 MHz protection with 8 MHz offset for 5, 10 and 15 MHz channel BW
Channel Bandwidth | Foffset ≥ 0.75 MHz for -42 dBm/6.25 kHz emission requirement |  | 
1.4 | RB_start (RBs) | 0 | 1
 | L_CRB (RBs) | >0 | 4-5
 | A-MPR | ≤6 | ≤3
3 | RB_start (RBs) | 0-3 | 4
 | L_CRB (RBs) | >0 | 10
 | A-MPR | ≤4 | ≤3
5 | RB_start (RBs) | 0-6 | 7-9
 | L_CRB (RBs) | >0 | >12
 | A-MPR | ≤4 | ≤2
Channel Bandwidth | Foffset ≥ 3 MHz for -42 dBm/6.25 kHz emission requirement | 
5 | RB_start (RBs) | 0-2
 | L_CRB (RBs) | 1-4 and >20
 | A-MPR | ≤3
Channel Bandwidth | Foffset ≥ 8 MHz for -42 dBm/6.25 kHz emission requirement | 
10 | RB_start (RBs) | 0
 | L_CRB (RBs) | 1-4
 | A-MPR | ≤3
15 | RB_start (RBs) | TBD
 | L_CRB (RBs) | TBD
 | A-MPR | TBD

## Slide 3: Way forward on co-existence with 850 MHz Lower Band (LTE_e850_LB)
[-30 dBm/MHz] emission limit; no objection except NII: Accept provided that it is also accepted for LTE_e850_LB UE emission limit to APAC700
[851]-859 MHz protection range (859-894 MHz is Band 26 DL -> -50 dBm/MHz emission limit applies); no objection
[2] MHz offset; no objection; Ericsson: the lower limit of LTE_e850_LB is pending decision on BS-BS coexistence issue between Band 5/26 BS and LTE_e850_LB BS
For 1.4, 3, 5, 10, [15] MHz channel BW for Band 26; no objection; Qualcomm and Motorola Solutions have concern on the feasibility to deploy 15 MHz channel BW with 2 MHz offset
Channel Bandwidth | Foffset ≥ 2 MHz for -30 dBm/1 MHz emission requirement |  |  | 
3 | RB_start (RBs) | 0-10 | 11-13 | 14
 | RB_start1 + L_CRB2 [RBs] | n.a. | 15 | n.a.
 | L_CRB (RBs) | >6 | n.a. | >0
 | A-MPR | ≤5 | ≤3 | ≤4
5 | RB_start (RBs) | 0-12 | 13-20 | 21-24
 | RB_start1 + L_CRB2 [RBs] | n.a. | 22 | n.a.
 | L_CRB (RBs) | >10 | n.a. | >0
 | A-MPR | ≤6 | ≤3 | ≤4
10 | RB_start (RBs) | 0-22 | 23-37 | 38-49
 | RB_start1 + L_CRB2 [RBs] | n.a. | 39 | n.a.
 | L_CRB (RBs) | >20 | n.a. | >0
 | A-MPR | ≤5 | ≤5 | ≤5
15 | RB_start (RBs) | 0-40 | 41-54 | 55-74
 | RB_start1 + L_CRB2 [RBs] | n.a. | 56 | 56
 | L_CRB (RBs) | >20 | n.a. | n.a.
 | A-MPR | ≤5 | ≤5 | ≤4

## Slide 4: Way forward on co-existence with narrow band systems in the 851-859 MHz range (2 MHz offset)
Channel Bandwidth | Foffset ≥ 2 MHz for -57 dBm/6.25 kHz emission requirement |  |  | 
1.4 | RB_start (RBs) | 0-2 |  | 
 | L_CRB (RBs) | >3 |  | 
 | A-MPR | ≤4 |  | 
3 | RB_start (RBs) | 0 | 1-7 | 8-12
 | RB_start1 + L_CRB2 [RBs] | n.a. | n.a. | ≥14
 | L_CRB (RBs) | 1-2and >6 | >6 | n.a.
 | A-MPR | ≤9 | ≤8 | ≤6
5 | RB_start (RBs) | 0-3 | 4-14 | 15-19
 | RB_start1 + L_CRB2 [RBs] | n.a. | n.a. | ≥21
 | L_CRB (RBs) | 1-3 and >10 | >6 | n.a.
 | A-MPR | ≤10 | ≤10 | ≤6
10 | RB_start (RBs) | 0-11 | 12-28 | 29-36
 | RB_start1 + L_CRB2 [RBs] | n.a. | n.a. | ≥38
 | L_CRB (RBs) | 1-3 and >18 | >10 | n.a.
 | A-MPR | ≤10 | ≤10 | ≤10
15 | RB_start (RBs) | 0-19 | 20-39 | 40-53
 | RB_start1 + L_CRB2 [RBs] | n.a. | n.a. | ≥55
 | L_CRB (RBs) | 1-3 and >24 | >15 | n.a.
 | A-MPR | ≤10 | ≤10 | ≤10
Channel Bandwidth | Foffset ≥ 2 MHz for -53 dBm/6.25 kHz emission requirement |  |  |  | 
1.4 | RB_start (RBs) | 0-1 |  |  | 
 | L_CRB (RBs) | >4 |  |  | 
 | A-MPR | ≤3 |  |  | 
3 | RB_start (RBs) | 0-3 | 4-7 | 8-13 | 14
 | RB_start1 + L_CRB2 [RBs] | n.a. | n.a. | ≥15 | n.a.
 | L_CRB (RBs) | >8 | >6 | n.a. | >0
 | A-MPR | ≤7 | ≤5 | ≤5 | ≤6
5 | RB_start (RBs) | 0-3 | 4-13 | 14-19 | 20-24
 | RB_start1 + L_CRB2 [RBs] | n.a. | n.a. | ≥21 | n.a.
 | L_CRB (RBs) | 1 and >10 | >8 | n.a. | >0
 | A-MPR | ≤9 | ≤8 | ≤5 | ≤6
10 | RB_start (RBs) | 0-11 | 12-27 | 28-37 | 38-49
 | RB_start1 + L_CRB2 [RBs] | n.a. | n.a. | ≥39 | n.a.
 | L_CRB (RBs) | 1 and >18 | >12 | n.a. | >0
 | A-MPR | ≤9 | ≤9 | ≤8 | ≤6
15 | RB_start (RBs) | 0-19 | 20-39 | 40-54 | 55 -74
 | RB_start1 + L_CRB2 [RBs] | n.a. | n.a. | ≥56 | n.a.
 | L_CRB (RBs) | 1 and >27 | >18 | n.a. | >0
 | A-MPR | ≤9 | ≤9 | ≤9 | ≤8

## Slide 5: Way forward on co-existence with narrow band systems in the 851-859 MHz range (6 MHz offset)
Channel Bandwidth | Foffset ≥ 6 MHz for -57 dBm/6.25 kHz emission requirement |  |  | 
5 | RB_start (RBs) | 0-5 |  | 
 | L_CRB (RBs) | >18 |  | 
 | A-MPR | ≤3 |  | 
10 | RB_start (RBs) | 0-4 | 5-28 | 29-44
 | RB_start1 + L_CRB2 [RBs] | n.a. | n.a. | ≥46
 | L_CRB (RBs) | 1-3 and >27 | >20 | n.a.
 | A-MPR | ≤9 | ≤6 | ≤5
15 | RB_start (RBs) | 0-12 | 12-46 | 46-61
 | RB_start1 + L_CRB2 [RBs] | n.a. | n.a. | ≥63
 | L_CRB (RBs) | 1-3 and >32 | >20 | n.a.
 | A-MPR | ≤10 | ≤10 | ≤10
Channel Bandwidth | Foffset ≥ 6 MHz for -53 dBm/6.25 kHz emission requirement |  |  |  | 
5 | RB_start (RBs) | 0-5 |  |  | 
 | L_CRB (RBs) | >18 |  |  | 
 | A-MPR | ≤2 |  |  | 
10 | RB_start (RBs) | 0-3 | 12-35 | 36-44 | 45-49
 | RB_start1 + L_CRB2 [RBs] | n.a. | n.a. | ≥46 | n.a.
 | L_CRB (RBs) | 1 and >30 | >20 | n.a. | >0
 | A-MPR | ≤5 | ≤5 | ≤4 | ≤6
15 | RB_start (RBs) | TBD |  |  | 
 | RB_start1 + L_CRB2 [RBs] | TBD |  |  | 
 | L_CRB (RBs) | TBD |  |  | 
 | A-MPR | TBD |  |  |