## Slide 1: OTA sensitivity and reference sensitivity
R4-75-BS-AAS-AH-0076
Agenda item: 3.3.4
Source: Huawei

## Slide 2: Huawei proposals presented
A cap on the value that may be declared as OTA sensitivity.
The cap value for isotropic antenna is referred to as ”basic sensitivity” in [1] and [2].
The cap value is scaled with the estimated directivity

## Slide 3: Basic sensitivity
Calculated from simulations described in TR25.942.([3])

## Slide 4: Directivity variation in RoAoA
Peak directivity does not apply over the entire RoAoA but OTA sensitivity does.
The most basic AAS is reference model. Eventual adaptive behaviour does not affect the model.
RoAoA delimiter

## Slide 5: EIS requirement cap
Directivity variation margin is added to make the OTA sensitivity feasible inside the entire RoAoA for all AAS BS.
The directivity variation margin also include directivity estimate errors and antenna implementation margin.

## Slide 6: Estimated directivity [4]

## Slide 7: Directivity estimation models
36000+ model:
D = 10*log10(36000/( θBW*φBW)+0.3)
Directivity calculation from total radiation pattern can be optionally used if preferred by vendor.

## Slide 8: References
[1] R4-150949
[2] R4-150950
[3] TR25.942
[4] R4-147671