## Slide 1: WF on measurement gap issues for eMTC
Nokia Networks, [Ericsson], [Huawei], [Qualcomm], …
R4-77AH-IoT-0122
3GPP TSG-RAN WG4 Meeting NB-IoT
Budapest, Hungary, 20-22 January, 2016
Agenda Item: 3.6

## Slide 2: Background
An MTC UE can only work on a sub-band of 6-PRB.
The MTC UE has to re-tune to the central 6-PRB to perform intra-frequency cell detection and/or measurement.
Re-tuning is achieved using measurement gap.
Discussions related to gap sharing between intra- and inter-frequency RRM, as well as the impact of gap usage to the delay requirement of cell detection and/or measurement is ongoing.

## Slide 3: Background
Focus is on intra-frequency RRM for Rel-13 eMTC and there are several options regarding gap sharing when defining the performance requirements:
  Option 1: Assume all gaps can be used for intra-frequency RRM
  Option 2: Pre-define gap sharing between intra- and inter-frequency RRM
  Option 3: Share the gap equally among all intra- and inter-frequency carriers

## Slide 4: Agreements
From RAN4 perspective the legacy gap pattern is re-used by Rel-13 MTC UEs for re-tuning to central PRBs dedicated for intra-frequency.Currently defined gap patterns are used for MTC UE to perform intra-frequency cell detection and/or measurement.
Gap pattern 0 and gap pattern 1 are both valid gap patterns.

## Slide 5: Way Forward
Measurement gap usage/distribution is left to UE implementation as long as the requirements are fulfilled.
Rel-13 solution should not prevent introduction of inter-frequency measurement support in a later phase.
The Rel-13 eMTC intra-frequency minimum requirements are derived using either of following:
  Legacy Inter-frequency messurements requirements
  Small Cell Enhancement requirements
Interested comanies are encouraged to bring detailed views.

## Slide 6
Option 4: techniques for sharing of gaps among all intra-f and configured inter-f carriers are FFS.