## Slide 1: Way forward on how to apply ACLR and ACS on coexistence study for standalone case
Intel, Ericsson, Huawei, Nokia, Qualcomm, ZTE
3GPP TSG-RAN WG4 Meeting #77 NB-IOT AH R4-77AH-IoT-0153 Budapest, Hungary, 20 – 22 Jan, 2016

## Slide 2: Background
The difference of NB-IoT BW and LTE BW is large
Different companies used different methods to apply the ACLR and ACS in the interference calculations

## Slide 3: Way forward on how to apply ACLR and ACS on coexistence study for standalone case
Definition and assumption
  LTE ACLR and ACS are defined for its own bandwidth size
  NB-IoT ACLR and ACS are defined for its own bandwidth size
  Attenuations are flat in the adjacent 10 MHz
  ACLR and ACS are the inputs to the simulations
  ACLR_e is the effective ACLR in the interference calculation
  ACS_e is the effective ACS in the interference calculation
Interference from LTE to NB-IoT
  ACLR_e = ACLR – 10*log10((180kHz/(# of IoT users))/9MHz)
  ACS_e = ACS [pessimistic assumption]
Interference from NB-IoT to LTE
  ACLR_e = ACLR – 10*log10((9MHz/(# of LTE users))/180kHz) [pessimistic assumption]
  ACS_e = ACS
The effective ACLR (ACLR_e) and effective ACS (ACS_e) shall be applied in the coexistence simulation for the calculation of victim system interference

## Slide 4: Illustration of flat assumption of ACLR and ACS
 |  |  |  |  |  |  | 10MHz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 10MHz |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | LTE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | NB-IoT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | NB-IoT ACS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | LTE ACLR |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | LTE interfering NB-IoT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | 10MHz |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 10MHz |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | LTE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | NB-IoT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | NB-IoT ACLR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | LTE ACS |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | NB-IoT interfering LTE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |