## Slide 1: Way forward on power leakage modeling for in-band and guard-band
Intel, Ericsson, Huawei, Nokia, Qualcomm, ZTE
3GPP TSG-RAN WG4 Meeting #77 NB-IOT AH R4-77AH-IoT-0154 Budapest, Hungary, 20 – 22 Jan, 2016

## Slide 2: Background
Different companies used different granularity on power leakage modeling

## Slide 3: Way forward on power leakage modeling for in-band and guard-band (3.75kHz sub-carrier spacing)
This is for UL with 3.75kHz sub-carrier spacing of NB-IoT
Companies are encouraged to provide both power leakage modeling as below, but it is fine if only one is provided
  ============================================================================
Power leakage from each NB-IoT tone to each LTE PRB:
  48 (tones) to 49 (PRB) --- In-band
  48 (tones) to 50 (PRB) --- Guard-band
Power leakage from each LTE PRB to each NB-IoT tone:
  49 (PRB) to 48 (tones) --- In-band
  50 (PRB) to 48 (tones) --- Guard-band
  ============================================================================
Power leakage from NB-IoT (all tones together) to each LTE PRB:
  Whole NB-IoT BW to 49 (PRB) --- In-band
  Whole NB-IoT BW to 50 (PRB) --- Guard-band
Power leakage from LTE (all PRB together) to each NB-IoT tone:
  Whole LTE BW to 48 (tones) --- In-band
  Whole LTE BW to to 48 (tones) --- Guard-band

## Slide 4: Way forward on power leakage modeling for in-band and guard-band (15kHz sub-carrier spacing)
This is for UL with 15kHz sub-carrier spacing of NB-IoT
Companies are encouraged to provide power leakage modeling to the next meeting
  ============================================================================
Power leakage from NB-IoT (all tones together) to each LTE PRB:
  Whole NB-IoT BW to 49 (PRB) --- In-band
  Whole NB-IoT BW to 50 (PRB) --- Guard-band
Power leakage from LTE (all PRB together) to each NB-IoT tone:
  Whole LTE BW to each tone --- In-band
  Whole LTE BW to each tone --- Guard-band