## Slide 1: Way forward on Intra-frequency Cell Identification Requirements without Gap
Intel
3GPP TSG-RAN WG4 Meeting AH-1801 San Diego, US, 22-26 January 2018
R4-1800153

## Slide 2: Background
In TS 38.133 there are 2 sets of requirements for cell identification for intra-frequency measurements without gap
  The UE shall be able to identify a new detectable intra frequency cell within Tidentify_intra_without_index if the UE has already identified an SS block with different time index and the same physical cell ID, or the UE has been indicated that the neighbour cell is synchronous with the serving cell. Otherwise UE shall be able to identify a new detectable intra frequency cell within Tidentify_intra_with_index
  Tidentify_intra_without_index = TPSS/SSS_sync + T SSB_measurement_period ms
  Tidentify_intra_with_index = TPSS/SSS_sync + T SSB_measurement_period + TSSB_time_index
  TPSS/SSS_sync is the PSS/SSS detection delay
  T SSB_measurement_period is the measurement period of SSB based measurement
  TSSB_time_index is the SSB Index acquisition delay
These requirements in Sections 9.2.5.1 and 9.2.5.2 in TS 38.133 are TBD

## Slide 3: Way Forward
The time period for PSS/SSS detection in FR1 is
  TPSS/SSS_sync = max(600ms,6* SMTC_period)
The time period for PSS/SSS detection in FR2 is
  TPSS/SSS_sync = max(600ms,3*N* SMTC_period), where N=8
The time period for Time Index detection in FR1 is
  TSSB_time_index = 2*SMTC_period
The time period for Time Index detection in FR2 is
  TSSB_time_index = 4*N*SMTC_period, where N=8
The measurement period for intra-frequency measurements without gaps in FR1 is
  TSSB_measurement_period = max(200, 5*SMTC_period) ms
The measurement period for intra-frequency measurements without gaps in FR2 is
  TSSB_measurement_period = max(200, 3*N*SMTC_period) ms , where N=8