## Slide 1
3GPP TSG-RAN WG4 Meeting AH-1801 R4-1800216 San Diego, US, 22 - 26 Jan, 2018
Agenda item: 4.3.2.4.2
Document for: Approval
Proposals on UE dynamic EN-DC power sharing
KDDI Corporation

## Slide 2: Background
In RAN#78, following proposals were endorsed in RP-172833.
  Proposal 1
  Agree to introduce Rel-15 capability signaling to indicate whether the UE supports dynamic EN-DC power sharing. Dynamic power sharing means that the UE can operate with P_LTE + P_NR > P_powerclass configuration
  Agree that the intent is to make dynamic EN-DC power sharing mandatory at a future time
  Check any possible updates on status above in March
  Proposal 2
  For UEs without dynamic LTE-NR power sharing capability, the support of single UL operation (Operation A with Case 1 in Slide 5) is mandatory with capability signalling
  Single UL operation is optional for dynamic power sharing capable UEs
This contribution proposes how to achieve contents of proposal 1 above, namely how to mandate dynamic EN-DC power sharing in the future.

## Slide 3: KDDI’s Proposals
Proposal#1: It would be appropriate to re-use concept of “NS versioning bits” in order to mandate dynamic EN-DC power sharing in the future.
Proposal#2: Send LS to RAN2 to inform of RAN4 decision after approval of proposal#1 above. Draft LS is available in R4-1800217 as well.
RAN4 may have to decide name of versioning bit and its bit length before sending LS to RAN2.

## Slide 4: What is “NS versioning bits”?
In Annex H of TS36.101, one can find NS versioning bits which are named as “modifiedMPRbehavior”.
When certain UE receives NS_xx, UE shall behave as specified in 6.2.4 of TS36.101.
These bits are used when this UE behavior can be different between Rel. X and Rel. Y. For easy understanding, example is shown in the next slide.

## Slide 5: Example: NS_05 versioning
A-MPR requirements for NS_05 are shown below;
CBW [MHz] | Parameters |  |  |  |  |  |  | 
15 | Fc [MHz] | 1932.5 |  |  |  |  |  | 
 | RBstart | 0-7 | 8 – 66 |  |  |  | 67-74 | 
 | LCRB [RBs] | ≥1 | ≤30 | 31 – 54 |  | >54 | ≤6 | >6
 | A-MPR [dB] | ≤11 | 0 | ≤3 |  | ≤5 | ≤5 | ≤1
20 | Fc [MHz] | 1930 |  |  |  |  |  | 
 | RBstart | 0-23 | 24-75 |  |  |  | 76-99 | 
 | LCRB [RBs] | ≥1 | ≤24 | 25 – 40 | 41 – 50 | > 50 | ≤6 | >6
 | A-MPR [dB] | ≤11 | 0 | ≤3 | ≤5 | ≤10 | ≤5 | ≤1
Table 6.2.4-18: A-MPR for "NS_05"
CBW [MHz] | Parameters |  |  | 
15 | Fc [MHz] | 1932.5 |  | 
 | RBstart | 0-7 | 8 – 66 | 67-74
 | LCRB [RBs] | N/A | ≤ MIN(30, 67-RBstart) | N/A
20 | Fc [MHz] | 1930 |  | 
 | RBstart | 0-23 | 24-75 | 76-99
 | LCRB [RBs] | N/A | ≤ MIN(24, 76-RBstart) | N/A
Table 6.6.3.3.1-2: RB restrictions for additional requirement (PHS)
Below requirement is mandatory for ver.12.9.0 and backward (including all of Rel. 9, 10 or 11).
Below is mandatory for Rel. 13 and onward. On the other hand, support of this requirement is optional for Rel. 12 and backward.
UE behavior can be different between different releases when NS_05 is received.

## Slide 6: How to specify optional or mandatory
Notes
- This bit shall be set to 1 by a UE supporting intra-band contiguous CA bandwidth class C
- This bit shall be set to 1 by a UE supporting A-MPR associated to NS_05 for Band 1.
Table H.1-1: Definitions of the bits in the field modifiedMPRbehavior
Index of field (bit number) | Definition (description of the supported functionality if indicator set to one) | Notes
0 (leftmost bit) | - The MPR for intra-band contiguous carrier aggregation bandwidth class C with non-contiguous resource allocation specified in Clause 6.2.3A in version 12.5.0 of this specification | - This bit shall be set to 1 by a UE supporting intra-band contiguous CA bandwidth class C
1 | - The A-MPR associated with NS_05 for Band 1 in Clause 6.2.4 in version 12.10.0 of this specification. | - This bit can be set to 1 by a UE supporting A-MPR associated to NS_05 for Band 1.
Note for ver 12.9.0 and below. This means optional.
Note for ver 12.10.0 and above. This means mandatory.
modifiedMPRbehavior is null..
modifiedMPRbehavior is “null” or “0” or “1” because modified NS behavior is optional..
modifiedMPRbehavior shall be “1” because modified NS behavior is mandatory
Legacy UE
Rel. 12 UE
Rel. 13 (and onward) UE
<Brief overview>

## Slide 7: Conclusion
Proposal#1: We propose to re-use concept of “NS versioning bits” to mandate dynamic EN-DC power sharing in the future.
Proposal#2: Send LS to RAN2 to inform of RAN4 decision after approval of proposal#1 above. Draft LS is available in R4-1800217 as well.
RAN4 may have to decide name of versioning bit and its bit length before sending LS to RAN2.

## Slide 8: Example of versioning bit (1/2)
For RAN2 spec [TS38.331];
Name of versioning bit: [modifiedFeaturesupport]
Field descriptions in RAN2 spec: [Field encoded as a bit map, where at least one bit N is set to "1" if UE supports modified feature support N, see TS 38.101. All remaining bits of the field are set to “0”. The leading / leftmost bit (bit 0) corresponds to modified feature support 0, the next bit corresponds to modified feature support 1 and so on. Absence of this field means that UE does not support any modified feature support. ]
Bit length: [32]

## Slide 9: Example of versioning bit (2/2)
For RAN4 spec,
In TS38.101-3, Annex X;
  Annex X.1 Indication of modified MPR behavior
  This annex contains the definitions of the bits in the field modifiedfeaturesupport indicated in [RAN2 spec] by a UE supporting an modified feature support in a later release of this specification.
Index of field (bit number) | Definition (description of the supported functionality if indicator set to one) | Notes
0 (leftmost bit) | - Support of dynamic EN-DC power sharing | - This bit can be set to 1 by a UE supporting dynamic EN-DC power sharing.
1 | - Reserved for another feature. | - Reserved for another feature.
Notes
- This bit shall be set to 1 by a UE supporting dynamic EN-DC power sharing.
- Reserved for another feature.
For Rel. 15. This description means dynamic EN-DC power sharing support is optional.
For Rel. 16 (or Rel. 17?). This description means dynamic EN-DC power sharing support is mandatory.
Table X.1-1: Definitions of the bits in the field modifiedfeaturesupport