## Slide 1: WF on NR BS RF FRCs - update
Ericsson, Huawei, ZTE, CATT, Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 RAN4#85
San Diego, CA, USA, January 22nd -26th, 2018
R4-1800334
Document for: Approval

## Slide 2: Background
Based on the agreed simulations assumptions ( R4-1711926 and emails exchanged), contributions listed in References slide were submitted in RAN4#85 providing simulations results.
Following two slides capture companies’ results.
This updated version captures further emails agreements made till Dec. 15th

## Slide 3: Background Simulation results for REFSENS and ICS SNR

## Slide 4: Background: Simulation results for Dynamic Range SNR

## Slide 5: Observations
Some assumptions are not common, they were missing from the previous agreements and might explain some difference in results.

## Slide 6: Agreements
Following slides capture agreed simulation assumptions and TBS

## Slide 7: Simulation assumptions - DMRS
DMRS pattern type 1:
  1 symbol front loaded + 1 additional
  No FDM, no data in DMRS symbol
              OR

## Slide 8: Simulation assumptions
Receiver type: MMSE

## Slide 9: Simulation assumptions - PTRS
No PTRS for FR1
For FR2, following PTRS parameters:
  KPTRS : 2 (PTRS every 2 RBs)
  LPTRS : 1 (all symbols with PTRS)
  No phase noise simulation, PTRS REs are not used for data

## Slide 10: REFSENS and ICS assumptions
Parameter | Value
Propagation | AWGN
Modulation | QPSK
Coding rate | 1/3
Symbol type | CP-OFDM
HARQ | None
#antenna | 1
Channel estimation | practical
Criteria | SNR at 95% throughput

## Slide 11: Dynamic Range assumptions
Parameter | Value
Propagation | AWGN
Modulation | 16QAM
Coding rate | 2/3
Symbol type | CP-OFDM
HARQ | None
#antenna | 1
Channel estimation | practical
Criteria | SNR at 95% throughput

## Slide 12: TBS for FRC
TBS and CB CRCs shall be calculated as follow:
  BG:
    For code rate ≤ 1/4, BG2 is selected；
    For 1/4 ＜code rate≤ 2/3, BG2 is selected if TBS≤3824（without CRC）
    For TBS ≤ 292, BG2 is selected
    Otherwise, BG1 is selected
  TB CRC:
    24bits if TB size>3824, 16bits if TB size ≤3824；
  CB CRC:
    24bits;
TBS size shall be given without CRC (payload only).

## Slide 13: Agreements
Finalize TBS size (without CRC) and DMRS pattern selection:
  Deadline/email approval: Dec. 15th
SNR values (practical channel estimation) shall be provided for next January Ad-hoc.
No margin should be included.
Rx requirements based on FRCs will remain TBD in TS 38.104.

## Slide 14: REFSENS and ICS FRCs TBS

## Slide 15: Dynamic Range FRCs TBS

## Slide 16: References
[1] R4-1714138, Discussion on FRC and simulation results for BS REFSENS and ICS SNR , Huawei
[2] R4-1714139, Discussion on FRC and simulation results for BS Dynamic Range SNR, Huawei
[3] R4-1714143, Simulation results for receiver sensitivity SNR, CATT
[4] R4-1714147, Simulation results for dynamic range SNR, CATT
[5] R4-1713129, on ICS requirement for FR1 NR BS, ZTE
[6] R4-1713132, Simulation results for FR1 REFSENS requirement, ZTE
[7] R4-1713134, Simulation results for FR2 OTA Sensitivity requirement, ZTE
[8] R4-17131087, Simulation results for FR1 dynamic range requirement, ZTE
[9] R4-1712688, Simulation results for FR1 dynamic range requirement, Nokia
[10] R4-1712690, Simulation Results for FRC for BS receiver dynamic range requirements, Nokia
[11] R4-1712694, Simulation Results for FRC for BS receiver in-channel selectivity requirements, Nokia
[12] R4-1712631, Simulation results - FRC FR1 for REFSENS and ICS, Ericsson
[13] R4-1712632, Simulation results for FR1 REFSENS requirement, Ericsson
[14] R4-1712633, Simulation results - FRC FR1 for Dynamic Range, Ericsson