## Slide 1: Way forward on measurement reporting time requirements
Ericsson
3GPP TSG-RAN WG4 Meeting AH-1801
San Diego, CA, USA, 22 – 26 January 2018
R4-1800344

## Slide 2: SSB time acquisition time for FR1
RAN4 will specify the SSB time index acquisition requirements, TSSB_time_index, as follows, depending on the DRX cycle, SS block based RRM measurement timing configuration (SMTC), and Measurement gap repetition period (MGRP):
Nattempts = [1], which is the number of attempts to acquire the configured SSB time index (corresponding to PBCH-DMRS sequence acquisition) with 99% success rate at SINR=-6dB.
The same Tssb_time_index requirement (delay) applies for both SSB based and CSI-RS based measurements.
 | Without measurement gap | With measurement gap
Non-DRX or DRX cycle < SMTC periodicity | Nattempts × (SMTC period) | Nattempts × max(SMTC period, MGRP)
DRX cycle >= SMTC periodicity | Nattempts × (DRX cycle) | Nattempts × max(DRX cycle, MGRP)
Table 1 Time period for time index detection

## Slide 3: SSB time acquisition time for FR2
RAN4 will specify the SSB time index acquisition requirements, TSSB_time_index, with functions of Nattempts, DRX cycle, SMTC period, MGRP, depending on the configuration
  The formula is same as Table 1 in the previous slide
  Nattempts is the number of attempts to acquire the configured SSB time index (corresponding to PBCH decoding) with 99% success rate at SINR=-6dB
Nattempts = [2] for SCS=120kHz and Nattempts = [3] for SCS=240kHz
The same Tssb_time_index requirement (delay) applies for both SSB based and CSI-RS based measurements

## Slide 4: CSI-RS based measurement reporting time
RAN4 will specify two CSI-RS based measurement reporting time requirements depending on the network configuration:
  Case 1: Network does not provide the associated SSB information or Network provides the associated SSB information but the SSB index is known to UE
    Tidentify_without_ssb = TPSS/SSS_sync + TCSI-RS_measurement_period
  Case 2: Network provides the associated SSB information
    Tidentify_with_ssb = TPSS/SSS_sync + TCSI-RS_measurement_period + TSSB_time_index
  where
    TPSS/SSS_sync: time period used in PSS/SSS detection for the configured physical cell Id for CSI-RS (same definition as the SSB based measurements)
    TCSI-RS_measurement_period: the measurement period of CSI-RS based measurements
    TSSB_time_index: the time period used to acquire the index of the SSB being measured (same definition as the SSB based measurements)