## Slide 1: Compromised peak EIRP requirement for mmW
Qualcomm, Motorola Mobility, TMO, Sony, [ ]
R4-1800405
3GPP TSG-RAN WG4 AH meeting
San Diego, USA, 22 - 26 Jan 2018
Agenda item: 4.3.2.1.3

## Slide 2: Background for peak EIRP
Going in to 3GPP WG4#85 Reno
  Intel/Apple proposal was 20.2 dBm QPSK
  Qualcomm proposal was 28.2 dBm pi/2 BPSK
  Other companies proposals were in between these numbers
Coming out of the meeting compromises were\
  Intel/Apple 21.2 dBm QPSK
  Qualcomm 25.2 dBm QPSK

## Slide 3: Way Forward on peak EIRP
Current 3GPP requirement (R4-1714445) TS 38.101-2 v15.0.0
  The handheld UE peak EIRP range is in TS 38.101-2
    For 28 GHz: [21.2-25.2] dBm
    For 39 GHz: [19.4-23.7] dBm
To recognize the challenges with the formfactor integration compromised numbers for peak EIRP requirement are as follows
  23.2 dBm @ 28 GHz
  21.5 dBm @ 39 GHz
These requirements apply for single band UEs