## Slide 1
3GPP TSG-RAN WG4 Meeting AH-1801 R4-1800443
San Diego , US, 22 - 26 Jan, 2018
Agenda Item: 4.6.1
WF on RRM requirements for SA operation
CMCC

## Slide 2: Overall RRM requirements (1)
Types | Functionality | Requirements is needed or not for SA | Whether NSA requirements can be reused for SA operation
RRC_IDLE state mobility | cell selection | Not needed | N/A
 | Measurement capability | needed | Reuse NSA agreements Note: The number of frequency layers could reuse the agreements of NSA operation, but the requirements architecture need to be updated
 | Cell reselection, including intra-frequency, inter-frequency and inter-RAT | needed | Define new requirement
RRC_INACTIVE state mobility | Measurement capability | needed | Reuse NSA agreements Note: The number of frequency layers could reuse the agreements of NSA operation, but the requirements architecture need to be updated
 | Cell reselection, including intra-frequency, inter-frequency and inter-RAT | needed | Define new requirement

## Slide 3: Overall RRM requirements (2)
Types | Functionality | Requirements is needed or not for SA | Whether NSA requirements can be reused for SA operation
RRC_CONNECTED state mobility | Handover | needed | Define new requirement
 | RRC re-establishment | needed | Define new requirement
 | RRC connection release with redirection | needed | Define new requirement
 | Random access | needed | Reuse NSA agreements Note: the current progress need to be updated for SA operation
Timing | UE transmit timing | needed | Reuse NSA agreements
 | timer accuracy | needed | Reuse NSA agreements
 | timing advance | needed | Reuse NSA agreements
 | cell phase synchronization accuracy | needed | Reuse NSA agreements
 | NR-NR DC MRTD | needed | Define new requirement
 | NR-NR DC MTTD | needed | Define new requirement

## Slide 4: Overall RRM requirements (3)
Types | Functionality | Requirements is needed or not for SA | Whether NSA requirements can be reused for SA operation
signalling | Radio link monitoring | needed | Reuse NSA agreements
 | NR PSCell addition/release delay | needed | Reuse NSA agreements
 | NR SCell Activation and Deactivation Delay | needed | Reuse NSA agreements
 | Interruption | needed | Define new requirement
 | SUL carrier RRC reconfiguration delay | needed | Reuse NSA agreements
Measurement procedure | Measurement capability | needed | Reuse NSA agreements Note: the number of frequency layers could reuse the agreements of NSA operation, but the requirements architecture need to be updated
 | Intra/inter measurement, including cell detection | needed | Reuse NSA agreements
 | Inter-RAT measurement, including cell detection | needed | Define new requirement
 | Measurement gap | needed | Define new requirement
 | Event triggering and reporting criteria | needed | Define new requirement
Measurement performance requirement | Measurement accuracy | needed | Define new requirement