## Slide 1: WF on general MSD principles for EN-DC band combinations
LG Electronics
R4-1800544
3GPP TSG-RAN WG4 Meeting #AH-1801
San Diego, California, U.S.A., 22-26 Jan., 2018

## Slide 2: Background
How to define MSD requirements for EN-DC UE due to intermodulation exists
  1) In LTE, only the worst case MSD is defined for each band[1][3]
    This means that even if there are multiple IMD’s only the one resulting highest MSD is specified
  2) In xDL/2UL LTE CA (x=3,4,5), only defined MSD requirements for 3rd own Rx band [5][6][7][8]
    Approved TP(R4-1713226) at last RAN4 meeting for EN-DC band combination showed the same principle can be applied to analysis MSD levels in LTE(xDL/1UL) + NR(2DL+1UL) DC band combinations.
One MSD related WF[2] was agreed in EN-DC UE when 1 Tx or 2Tx switch.
  IMD impact to LTE secondary component carriers will not be considered.
  This agreement is only for considered for switching of 1Tx or 2Tx

## Slide 3: Way forward
Proposal1: Basic principle for EN-DC UE should be follow the agreed WF [1] as a baseline in LTE 2UL CA. It means only the highest MSD is specified automatically in TS38.101-3.
  Some exceptions should be accepted based on request of the proponent of the EN-DC band combination.
  Multiple IMDs for each CA band combos will be studied and analyzed in technical report.
Proposal2: In LTE(xDL/1UL, x=1,2,3,4) + NR(yDL+1UL, y=1,2) DC band combinations, same principle can applied to define MSD requirements based on coexistence analysis results.
Proposal3: MSD level at LTE secondary cells by IMD problems should be specified in TS38.101-3.

## Slide 4: Reference
[1] R4-144031, “WF on 2UL inter-band CA MSD test configurations”, Mediatek, RAN4#71
[2] R4-1714356, “Way forward on single UL transmission”, Apple, Nokia, Vodafone, OPPO, Xiaomi, RAN4 #85
[3] R4-1702446, “WF on the MSD test principles for xDL/2UL CA”, LG Electronics
[4] R4-1713226, “TP on self-interference studies for LTE (xDL/1UL) and NR (2DL/1UL) DC band combinations”, LG Electronics
[5] TR36.715-00-02
[6] TR36.714-00-02
[7] TR36.860-13
[8] TR36.860-12