## Slide 1: Way forward on the requirement for SS/PBCH index acquisition time
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #85 San Diego, USA, 22nd – 26th January 2018
Agenda Item: 4.6.5.1
R4-1800609

## Slide 2: Observation
UE wouldn’t be aware of the DMRS error before PBCH CRC which means that UE has no idea whether the error in SS/PBCH detection is due to DMRS error or PBCH error or both.
Combining of the consecutive SS/PBCH block with same index could be of better performance only under the condition that DMRS is correctly acquired.
DMRS | PBCH | SSB index | Combine with the next shot
× | × | × | ×
√ | × | × | √
√ | √ | √ | N/A

## Slide 3: Way forward
Cascade detection of PB-DMRS and PBCH should be considered for the delay requirements for NR FR2 SS/PBCH index acquisition.
For FR1, cascade detection of PB-DMRS and PBCH also need to be considered for SS/PBCH index acquisition delay requirement.
Receiver beamforming should be considered for FR2 when considering SS/PBCH index acquisition requirements.
How to decide the FR2 SS/PBCH index acquisition time requirement should be discussed in the AH1801 meeting.