## Slide 1: WF on NR MU and test tolerance
CATR, Anritsu, Intel
3GPP TSG-RAN WG4 AH-1801 R4-1800745
San Diego, USA, 22 – 26 Jan 2018
Agenda item: 4.7.2
Document for: Approval

## Slide 2: Progress
A LS is sent to RAN5 to shift the MU work.
The baseline MU for EIS has been approved into TR38.810 and the RAN4 part of the MU work will be finalized in the next meeting.
The applicability of the baseline setup is approved.
The work plan for alternate methods is approved.

## Slide 3: MU value for quality of quiet zone
Agreements:
  At calibration stage, the offset of reference AUT from the center of QZ should be excluded.
  How to exclude the MU value of “offset of reference AUT phase center ” is FFS
Open Issue:
  How to estimate the effect of the ripple on calibration stage– Quality of the QZ for Calibration part

## Slide 4: Reference AUT vs Calibration AUT
Do we need to add requirements for calibration AUT?
  No requirements are needed for calibration AUT

## Slide 5: TRP Measurement Grids
The group agrees to consider the following options:
  Option 1:
    Determine the UE directivity and HPBW using measurements.
    Work out a procedure to determine the minimum number of measurement points as a function of UE directivity and HPBW.
  Option 2:
    Define measurement grids according to UE type.
    The impact of this option on MU needs to be assessed.
  Option 3:
    Manufacturer declaration of desired measurement grid.
    The impact of this option on test setup and MU applicability needs to be defined.
  Option 4:
    Define a MU threshold limit for the measurement grid size.
  Other options are not precluded:

## Slide 6: Directivity and HPBW masks for reference AUT
How to qualify the reference antenna:
  Meet the reference AUT masks based on vendor’s datasheet.

## Slide 7: Equivalence framework for alternate test methodologies
Update the equivalence framework based on technical justification and MU assessment.
Measurements are not required.

## Slide 8: MU scope
For alternative methods, the MU elements discussion and MU assessment for MOP and REFSENSE is required in RAN4.

## Slide 9: Phase impacts on baseline setup
The phase characterization procedure in the QZ needs to be finalized based on the [R4-1801263].
The impacts of the offset of antenna array from the center of the QZ needs to be re-evaluated for different antenna and steering assumptions. [R4-1800971].

## Slide 10: Other actions
Conference call prior to RAN4#86 to progress on open items